COPYRIGHT STATEMENT

        CM IS NOT FREE SOFTWARE. IT IS COPYRIGHTED PROPERTY OF
        SERGE S. PACHKOVSKY (OWNER). YOUR CAN USE AND DISTRIBUTE IT,
        PROVIDED THAT YOU OBEY THE FOLLOWING CONDITIONS:
          1. NO PART OF CM DISTRIBUTION IS REMOVED OR CHANGED BY ANY WAY
          2. YOU DO NOT CHARGE ANYONE FOR CM
          3. ANY PROFIT MAKING USE OF CM REQUIRES PRIOR WRITTEN
             PERMISSION FROM OWNER.


    If you have suggestion on the following development of CM, or
had detected a bug in it, or wish to tell me how one or another protected
program is to be dealt with (so it can be included into later versions of
CM), you can mail to:

        FIDO:           2:5000/19

        E-Mail:         ps@dialnet.msk.su

    If you can't reach nether one of them, post letters to my home address:

USSR, 630015, Novosibirsk-15, Dzerdginsky av., 1a flat 89, Serge S. Pachkovsky
(630015, £. �®¢®á¨¡¨àáª-15, ¯à. „§¥à¦¨­áª®£® ¤.1  ª¢. 89, � çª®¢áª¨© ‘.‘.)

    If you find CM of value and continue to use it, pray send me letter 
to one of the addresses above, stating your name, area of interests and 
means of reaching you by email. Enjoy!


                AT Copymaster
                -------------

    CM is a bit-copying utility specifically designed to utilize most
abilities of AT floppy disk controller (FDC). CM can work with 360K, 1.2M,
720K or 1.44M floppy drives using any recording density. With 300 RPM 5«-inch
drive and most FDCs, it can copy FM (single density) floppies. It can even
copy disks, which have different recording density on the SAME track -
feature which no one software or hardware bit-copier have.
    CM works with FDC in polling mode, which requires CPU services each 16
mks for high density drive. Therefore, CM requires relatively fast CPU - 6
MHz / 0 WS 80286 is an absolute minimum. Because CM operations are tightly
related with computer hardware, it will not work on computers even with minor
incompatibilities. IBM's own PS/2 model 50 (and probably some other MCA
machines) is an example.
    Before CM can copy any disk, it should first learn a little about your
FDC, CPU and floppy drives. This is done by '/I' (Install) command switch,
e.g., 'CM B: /I'. If you have more then one floppy drive, you should install
CM for each one you will be using. You will see something like the following:


[A]     AT CopyMaster v0.44a (C) 1990,1991 Serge S. Pachkovsky
               Compiled Apr 30 1991 at 13:42:09
[B]     ROM changed - need reinstallation
[C]     CPU speed changed - need reinstallation
[D]     Drive B is 3« inch 1.4 Mb high density
[E]     Insert BLANK diskette in drive B: Push any key when ready ...

[F]     Testing for hardware forbidden data rates ...
            Clock 0 (expecting 500 KBS,MFM) format failed
            Clock 1 (expecting 300 KBS,MFM) found 299.87 KBS
            Clock 2 (expecting 250 KBS,MFM) found 249.76 KBS
            Clock 3 (expecting 125 KBS, FM) found 124.86 KBS
[G]     Testing revolution time. This takes about 15"
        Disk B revolution time is 199.74 ms
[H]     Sizing controller write buffer. This takes up to 3 minutes
            At 300 KBs buffer seems to be at least 27 bit(s)
            At 250 KBs buffer seems to be at least 28 bit(s)
            At 125 KBs buffer seems to be at least 31 bit(s)


    [A] shows version of CM and compilation date/time. First public release
        is version 0.44a, compiled 30 April 1991.

    [B] CM tries to keep track of moving to another computer by checksumming
        motherboard ROM, in order to use always correct FDC timing.

    [C] CM measures CPU speed by counting time required to access FDC control
        registers, so this message can be caused by change in CPU operation
        mode (real/protected) or by replacement of FDC itself. Anyhow,
        internal timing parameters show be recalculated in both cases.

        If you move CM to other computer, but never [B] nor [C] does not
        appear, you should reinstall CM by hand, because timing parameters of
        floppy drive on new computer could still differ.

    [D] If CM prints here drive type different from you are using, it shows
        that something is wrong with your computer's CMOS.

    [E] Floppy will be erased by CM installation procedure, so it should be
        something you don't care of.

    [F] AT FDC have four software-selectable clocks (or data transfer rates).
        Original AT FDC does not checks for the validity of clock for
        particular drive, so any can be selected for any drive. However,
        never FDCs forbade certain transfer rates for some drive/media types.
        (Example above was for 720K floppy in 1.44 3¬-inch drive).
        AT FDC uses 500, 300, 250 and 125 KBS (thousands of bits per second)
        clocks. If actual transfer rate will differ significantly (by more
        then 5%), CM will not be able to use it. (This is most often
        happens for clock 3, 125 KBS, which was not used by IBM software
        at all and was therefore overlooked by some "compatibles").

    [G] Revolution time is an important characteristic of each drive.
        Generally speaking, all drives except 1.2M 5«-inch should revolve by
        200ñ4 ms, while 1.2M - by 167ñ3.5 ms. Nevertheless, CM should be able
        to deal correctly with any reasonable revolution time outside these
        margins.

    [H] CM needs to know interval which passes between feeding data value to
        FDC and it's appearance on drive data lines. This delays, converted
        to number of data bits for current transfer rate, are printed. Lesser
        difference between values should indicate faster CPU/FDC subsystem.

    CM saves all measured values into it's own body, so it should NOT be
compressed. (In fact, CM will refuse to work at all if it's disk file image
was modified).

    After CM was installed, you can copy floppy to disk image, specifying
command: 'CM A: MYFILE.CM' or disk image back to floppy by command:
'CM MYFILE.CM A:'. (Of course, you can create image on one computer and then
restore it on another, provided that both have floppy drives of the same
type).
    Command line switches can influence significantly on CM operations. Thus,
analysis of high density disk can take from about 5 minutes to 2 hours,
while standard switch values will take about 50 minutes.

    CM accepts the following command line switches:

/S:ratelist - Selects data transfer rates, which CM will for during floppy
    analysis. This can be H (500 KBs), M (300 KBs), L (250 KBs) or F (125
    KBs). Values should be separated by colon, e.g. '/S:H:M'. CM will try
    clocks in the order specified, so if you know that most of your disk use
    500 KBs rate, while 300 KBs rate occurs on a single track, CM will work
    much faster with '/S:H:M' when with '/S:M:H'. (Although results will be
    the same).
        By default CM uses the following transfer rates:
        /S:H:M      for 1.2M 5«,        /S:H:L      for 1.44M 3¬,
        /S:L        for 360K 5« and 720K 3¬
/D:{Y|N}    - Turns double-stepping mode on and off. 1.2M drive emulates 360K
    one by skipping each second track. If you are sure that nothing of
    interest can be found on odd tracks, you can instruct CM not to look on
    them, thus halving operation time. Default is '/D:N'
/T:XX:YY    - Instructs CM to copy tracks XX to YY (inclusive). Most 360 5«
    drives have 43 tracks ('/T:0:42') while 1.2, 720 and 1.44 drives have 84
    tracks ('/T:0:83'). Nevertheless, CM will check by default only 42 tracks
    for 360K drive and 83 tracks on others.
        Then '/D:Y' switch is used, XX and YY are doubled by CM.
/H:{0:1}    - Select head to copy. Default is both.
/G:{Y|N}    - GAP analysis level. With '/G:Y' CM will examine GAP (empty
    space which follows each data sector) for possible protection data,
    slowing down operations. If you are sure that nothing can be found here
    (or CM knows this particular protection scheme, see /P switch), you can
    select '/G:N'. Default is '/G:Y'.
/Q:{Y|N}    - Verbosity level. Setting '/Q:N' will cause a lot of curious
    information about disk to be printed. For example, I'd got the following
    messages in response to 'CM B: NUL /T:1:1 /H:0 /S:L /Q:N':

        Reading track 01 head 0  9 sectors found    (249.8 KbPS)
            Sector 01/00/01/02 Off  11485
            Sector 01/00/02/02 Off  61737
            Sector 01/00/03/02 Off 111997
            Sector 01/00/04/02 Off 162289
            Sector 01/00/05/02 Off 212559
            Sector 01/00/06/02 Off 262813
            Sector 01/00/07/02 Off 313115
            Sector 01/00/08/02 Off 363457
            Sector 01/00/09/02 Off 413721

    For each sector on track CM printed it's ID (Cylinder/Head/Record/leNgth)
    as written in corresponding field on data track (all values are in hex),
    along with sector offset ('Off') from the beginning of track (i.e., from
    index hole). Sector position is measured in system clock units and should
    be multiplied by 0.41905 to convert to mks. You can got slightly
    different sector offsets in subsequent runs of CM.
        Other message deserving attention, is '(249.8 KbPS)', which is actual
    data transfer rate. FDC can synchronize with wide range of data rates for
    a given clock number (this is especially true for clock 3, MFM), so
    measured transfer rate significantly different from nominal one can give
    hint on floppy disk origin. CM can't reproduce data transfer rate, so it
    attempts to inform you about possible protection mark here.
        Selecting '/Q:Y' will suppress almost all CM messages, if they are
    not caused by possibly incorrect operation, when you should be alerted.
    By default CM selects level of verbosity intermediate between '/Q:Y' and
    '/Q:N'.
/M:{Y|N}    - Search for multiply data transfer rates enable/disable. Setting
    '/M:Y' will permit CM to search tracks with multiply transfer rates,
    slowing down operations. Because such tracks are rare to occur, default
    is '/M:N'.
/W:{Y|N}    - This switch instructs CM how to interpret data that reads
    differently in subsequent operations. '/W:Y' tells CM that it is an
    intended protection mark, which should be reproduced, '/W:N' instructs CM
    to attempt to recover accidentally damaged data.
        Default is '/W:Y'.
/P:{Y|N} or
/P:Number   - Instructs CM to look for familiar protection schemes ('/P:Y')
    or to copy disk by default ('/P:N'). '/P:Number' tells to use scheme
    Number. Currently, you can use the following values:
        1 - Alex Simkin's scheme (PC Shield). CM should detect this by
            default
        2 - Maximize data fields instead of perfect timing. CM will never
            select this by itself.
    Default is '/P:Y'.
/A          - Append to the existing disk image. (You can use copy/b
    to merge files instead).

    Only /T /H and /Q are applicable for image-to-floppy operation.