ALS100Plus+ Integrated Audio Controller

with 3D Sound

User’s Guide

Ver. 1.10

April 15, 1997

Introduction

Chapter 1

Introduction

The ALS100Plus Integrated Audio Subsystem is a single chip designed for plug and play specification which minimizes support and installation issues. This highly-integrated plug and play audio subsystem for IDE CD-ROM interface incorporates the following functions:

• 	Subsystem control logic

•	Built-in 3D Sound Effect Processor

• 	Digital to analog and analog to digital conversions

• 	Mixer functions

• 	Digital to analog conversion for the synthesizer

• 	Enhanced Game/MIDI port support

• 	 IDE CD-ROM controller

• 	The ALS100Plus fully supports the ISA Plug and Play standard. For non-ISA Plug and Play compatible systems, a software utility ISA Configuration Utility”, (ICU) is available that sets the IRQ and DMA addresses. Sound card implementations designed around the ALS100Plus are completely jumper and switch free.

Important Notice

This User’s Guide is intended to assist OEM customers in evaluating Avance Logic graphics products; it is not intended to be the User’s Guide for the end-user. Avance Logic encourages the development of documentation based on the information contained herein. For your convenience, copies of this manual are available on diskette in Microsoft Word 7.0. Ask your local Avance Logic sales representative for a copy. This manual is also available on the Avance Logic Bulletin Board System (BBS) at 886-2- 2982050.

Specifications

Chapter 2

Hardware Features

• 	Single, mixed-signal, high performance VLSI sound ASIC

• 	Three software selectable DMA lines (0, 1, 3)

• 	Software selectable interrupt lines (5, 7, 9, 10, 11)

• 	8-bit ISA Plug and Play bus interface

• 	8-bit or 16-bit CD-ROM interface

• 	DMA interface with FIFO

• 	Enhanced Game port support

• 	MIDI port with input and output FIFO

• 	8-bit or 16-bit monaural/stereo digital audio from 4 kHz to 48 kHz

• 	Full duplex

Built-in Functional Blocks

• 	ISA Plug and Play support logic and resource ROM

• 	High speed 16-bit digital to analog and analog to digital converters with filters

• 	3D Sound Effect Processor

• 	Digital to analog converter to support FM/wavetable synthesis

• 	Thirty-two level stereo audio mixer with six input sources (DAC, synthesizer, PC speaker, microphone, line in, and CD audio)

• 	Built-in amplifier for the microphone input

• 	ADPCM decompression engine

• 	High speed DMA interface with FIFO

• 	MPU-401 MIDI controller with FIFO

• 	IDE CD-ROM controller

Control logic is built into the ALS100Plus+ to support the following functions:

• 	Audio Input

· 	CD-ROM Audio

· 	Line In

· 	Wavetable

· 	Microphone

· 	PC Speaker In

• 	Audio Output

· 	Stereo Line-Out

· 	Power stereo output

• 	Game/MIDI Port

· 	External MIDI input and output

· 	Joystick input and MIDI connector

• 	Wavetable connector

· 	Optional Yamaha OPL3 FM Synthesizer

· 	Optional Yamaha OPL4 Wavetable Synthesizer

• 	CD-ROM Controller

· 	ATAPI IDE

Software Support

• 	Windows 3.1

• 	Windows 95

• 	Windows NT 3.51 and 4.0

• 	Windows Sound System

• 	OS/2 Warp

• 	All DOS-based games

Compatibility

• 	Adlib

• 	All Sound Blaster Pro applications

• 	All Sound Blaster 16 applications

• 	Yamaha OPL3 FM Synthesizer

• 	Yamaha OPL4 Wavetable Synthesizer

• 	MPU-401 UART MIDI

Applications

• 	16-bit stereo sound cards

• 	PC motherboard based sound systems

• 	MIDI controller

• 	Enhanced Game port support

• 	IDE CD-ROM controller

• 	Wavetable card support

Emulation

• 	Sound Blaster Pro

• 	Sound Blaster 16

• 	Sound Blaster ADPCM

• 	MPU-401 UART MIDI interface

Hardware

Installation

Chapter 3

Evaluation Sound Card

AS9650 Sound Card Description

• 	16-bit ISA Plug and Play design

• 	ATAPI IDE CD-ROM interface

• 	Game/MIDI port

• 	Audio inputs from:

· 	External Wavetable card

· 	ATAPI IDE CD-ROM audio

· 	Microphone

· 	Line In

• 	Audio Outputs to:

· 	Line Out

· 	Main/Speaker Out

• 	FM/Wavetable support

Input/Output Connections

Phonejacks, connectors, and headers are used to connect other devices to the sound cards. A phonejack is a single hole receptacle for a phoneplug and headers and connectors are multi-hole receptacles for multi-pin plugs. The Mainpeaker Out, Line Out, Line In, and Microphone In connections are phonejacks, the Game/MIDI Port is a D-shell 15-pin connector, and the Wavetable, CD-ROM audio, CD-ROM data/external controller connections are headers of various sizes.

Speaker Out-  The Speaker Out phonejack provides the built-in power amplifier outputs for the left and right stereo channels.  The power amplifier has a miximum output power of two watts per channel with four ohm speakers.

Line Out - The Line Out phonejack provides the non-amplified outputs for the left and right stereo channels. This output is for attaching powered speakers or an external audio amplifier.

Line In - The Line In phonejack is used to attach monaural or stereo devices such as a cassette, Digital Audio Tape, or Minidisc players for playback, mixing, or recording.

Mic In - The Microphone In phonejack is used to attach a monaural microphone for live audio input for playback, mixing, or recording.

Game/MIDI Port - The Game/MIDI Port connector is used to attach a joystick for game interaction or to attach an external MIDI device for playback, mixing, or recording.

Wavetable - The Wavetable connector is used to attach a Wavetable card for playback, mixing, or recording.

ATAPI IDE/Sony CD-ROM Audio - The ATAPI IDE/Sony CD-ROM Audio connector is used to connect the audio cable from either an ATAPI IDE or Sony CD-ROM drive for playback, mixing, and recording.

Mitsumi CD-ROM Audio - The Mitsumi CD-ROM Audio connector is used to connect the audio cable from a Mitsumi CD-ROM drive for playback, mixing, or recording.  Only  one of the two CD-ROM audio connectors may be used at a time.

ATAPI IDE CD-ROM Data - The ATAPI IDE CD-ROM Data connector is used to connect the data cable from an ATAPI IDE CD-ROM device.

Sound Card Installation

1.	Power off the system and all peripheral devices. Unplug all power cords from the power utility outlets.

2.	Momentarily touch the chassis of the system unit with your bare hand to discharge any static electricity.

3.	Remove the cover from the system unit.

4.	Locate a free 16-bit ISA expansion slot and remove its cover plate. Retain the screw.

5.	Carefully remove the sound card from the anti-static envelope and install it into the expansion slot.

6.	Secure the sound card with the screw removed earlier.

7.	Attach any CD-ROM Audio, CD-ROM Data, and Wavetable card cables to the sound card.

Note: Only on11.	 Remoskette from the

Windows NT

EnsureALS100 is instroperly and powerInsert‘ALS100 Windows NT Drive’ diskette into : ).  Go to [Control Pan] and cho fo‘Avance Logic, I’.

While ins“Driver ” warning message will appear an‘midima’ or [re-install].  Please select [re-instal

Configure ’s and’sif neceasth app on s.

Re-bsystand remove driverdriverta into .

OS/2  4

Before inALS100 Device Driver, make sur	OS/	Warp 4.0 Revision 9.023 or later.  Fo/R from	OS/2 command prompt.  If OS/2 has already	II; if not, please proceed to Part I.  Pa	availableALS100 setup pALSND.

Part I.  OS/2 Warp		A.  Diskette Installation of OS/2 Warp 4.0

Instaoceed tofoALS100 Device Driver Installation.

CD-ROM Installation  of OS/2 Warp 4.0 with Multimedia Support

IALS100 Device Driver Installation.

C.    CD-ROM Installation  of OS/2 Warp 4.0 without Multimedia Support

From WarpCenter, click on [System Setup] object.

Click on [Install/Remove] menu item.

Choose [Selective Install] item and click it.

As System Configuration SettiALS100 Device Driver Installation.

Part II. ALS100 has been properly installed.  Power on your computALS100 Device Driver diskette into your floppy disk drive.

From OS/2 WarpCenter, click on [System Setup] object.  Click on menu item [Install/RemovALS100 Device Driver diALS100 Adaptor” for installation and proceed until installation isALSND Setup Program

The following gives an exampALSNDB

Device=C:\MMOS2\ALSNDB.SYS 1 D1 I5 A220 M4 /N:ALS01

D ALS100, 8 bit DMA channels are available for 0,1 & 3.

I5		:  The ‘	 5, 7, 9, 10 & 11.

A220	:  ‘A’ indicates the base I/O address of DSP, and the available

ports are 220, 240, 26 Physical Devic

Setup Utility Program

A3CONFIG.EXE

This utility is used to set up the ALS100Plus+ sound card. It is automatically started when the Avance Logic software drivers are first installed in a DOS or Windows 3.1 application. It should be re-run anytime the system hardware configuration is changed or a change to the ALS100Plus+ sound card configuration is desired. The a3config.exe utility resides in the directory into which the Avance Logic software drivers were stored.

To run the a3config.exe utility, perform the following:

1.	If Windows 3.1 is running, exit the application and at the C:\> prompt, set the current directory to the directory containing the a3config.exe utility (A3SOUND was the default directory at installation time), type a3config.exe, and then press the Enter key to execute the utility.

2.	The ALS100Plus+ Sound Chip Configuration Program screen will be displayed. Use the Tab, Space, Enter, Down Arrow, and ESC keys and/or the mouse to select and set options in menus, to move between menus, and to make and set changes to values.

3.	In the Sound Chip Configuration Program menu, the SB16 configuration screen showing the I/O port, DMA, and IRQ settings will be displayed, and the d9.In the Sound Chip Configuration Program menu, 8-Bit Sound/16-Bit Sound/FM Music box will be displayed. Select each box and verify the correct operation of the ALS100

10.	When satisfied with the operation of the ALS100

Trouble Shooting

The ALS100Plus+ sound card is designed to run trouble free once it is installed and set up. Most problems will be encountered during installation and setup or will be encountered later when something is changed in the system. The following are descriptions of and solutions for the more common problems that you may encounter. Please review these problems before requesting technical assistance.

Problems in DOS

1.	Problem:	Cannot load the CD-ROM software driver

Cause:	The CD-ROM port may not be enabled. Check the config.sys file for the line device=c:\a3sound\cdsetup.sys”. If it is not present, perform the steps outlined in the Solution. If it is present, call for technical assistance.

Solution:	Run the a3config.exe utility. In the Device menu, select “CD-ROM” and press [OK] to configure the CD-ROM. Verify that the line “device=c:\a3sound\cdsetup.sys” is now in the config.sys fil

FCC Notice

This equipment has been tested and found to comply with the limits for a Class B digital device, pursuant to Part 15 of the FCC Rules. These limits are designed to provide reasonable protection against harmful interference in a residential installation. This equipment generates, uses, and can radiate radio frequency energy and, if not installed and used in accordance with the instructions, may cause harmful interference to radio communications. However, there is no guarantee that interference will not occur in a particular installation. If this equipment does cause harmful interference to radio or television reception, which can be determined by turning the equipment off and on, the user is encouraged to try to correct the interference by one or more of the following measures:

1.	Re-orient or relocate the receiving antenna.

2.	Increase the separation between the equipment and the receiver.

3.	Connect the equipment into an outlet on a circuit different from that to which the receiver is connected.

4.	Consult the dealer or an experienced radio/TV technician for help.

Shielded interconnect cables must be employed with this equipment to insure compliance with