About FCON.EXE
==============

FCON.EXE is a utility that allows the user to easily enable feature connector 
operation. This utility is required only for 2 or 4 MByte configurations of 
Trio64 as the BIOS automatically enables feature connector operation for 
1-MByte configurations. For Trio32, the feature connector is always enabled.

Usage:

FCON [e|d] [p|v]
        where e = enable        d = disable
              p = pass-through feature connector
              v = VAFC (VESA Advanced Feature Connector)


Some ReelMagic Video cards with VGA have only one output, so if these cards 
hook up to Trio64 with 2 or 4 MBytes, you must add FCON to the AUTOEXEC.BAT 
in order to enable the feature connector. The screen will not be activated 
until the FCON.EXE in the AUTOEXEC.BAT has been executed.