E2000plus-series Ethernet Adapters
Installation file for
\PCTCP directory
============================================================================


*****************************************
* Packet Driver Installation for PC/TCP *
*****************************************

The packet driver for PC/TCP is located in the \PCTCP directory of the
E2000plus driver diskette.

1. Run the E2000.COM program by entering the following
   at the DOS command line --

       A:>\PCTCP\E2000  <Packet_INT#> [IRQ#] [IO_Addr#]

       (NOTE: This assumes the driver diskette is in drive A.)

       where --
       <Packet_INT#>:   interrupt vector number, which can be
                        decimal, hexadecimal or octal format.
                        if:
                        decimal format -- from 96 to 128
                        hexadecimal ----- from 0x60 to 0x80
                        octal format ---- from 0140 to 0200

       [IRQ#]:          interrupt setting.
                        The following settings can be selected 3, 4, 5, 9,
                        10, 11, 12, 15.

       [IO_ADDR#]:      I/O Base Address setting.
                        The following settings can be selected:
                        0x300 0x320 0x340 0x360 0x380 0x3A0 0x3C0 0x3E0
                        0x200 0x220 0x240 0x260 0x280 0x2A0 0x2C0 0x2E0


      EXAMPLE:    E2000  0x60 3 0x300
                  (manual selection)
                  --> Packet_INT# = 0x60, IRQ# = 3, IO_Addr# = 0x300

                  E2000  0x60
                  (automatic selection)
                  --> Packet_INT# = 0x60, IRQ# & IO_Addr# = automatic selection

2. Execute the ETHDRV.EXE device program, which is included with the
   FTP PC/TCP software package.

   The Ethernet adapter should now work with FTP PC/TCP.