E2000plus-series Ethernet Adapters
Installation file for
\WFW311 directory
============================================================================


************************************************************
* NDIS Driver Installation for Windows for Workgroups 3.11 *
************************************************************

1. To install NDIS drivers in Windows for Workgroups, user
   should be in the Windows environment first and choose the Network
   Setup icon.

2. Click on "Drivers" in the Network Setup window.

3. Choose the "Add Adapter" item in network driver.

4. When the new menu is displayed, choose the "Unlisted or Updated
   Network Adapter" item for the new driver.

5. There is a box for entering the device and directory. Key in
   "A:\WFW311" <enter>.

6. Input the correct values for IRQ channel and I/O address. These
   two values must agree with adapter's actual parameters. Use the 
   View Configuration function in the SETUP.EXE program to see them.
   For the Others as Required input, nothing needs to be entered.

7. Click the Driver Setup icon in the Network Driver window. Set the driver
   type to be "real mode", "real and enhanced mode", or "enhanced
   mode" NDIS driver, leave Windows for Workgroups, and reboot.