MOUSE.DOC - Programming Interface

The following provides information to programmers who want to
include the AT&T MOUSE 6300 in their application programs. This
document includes descriptions of the graphics and text cursors,
and descriptions of the mouse functions and extended mouse
functions.

This protocol is compatible with the protocol of Microsoft Corp.
as it is documented in the installation and operation manual
published by Microsoft Corp. entitled Microsoft Mouse for the
IBM Personal Computer.

These notes apply to the Mouse Driver (mouse.com) release 1.0,
2/28/85.

The programming interface uses the 8086 software interrupt 51.
Parameter values are passed and returned via 8086 registers.
This interface can be used from assembly language programs or
from high level language programs such as C, Modula-2, or
Pascal.

Programming Interface from the GWBASIC Interpreter

It is possible to make a mouse system call from a BASIC program
running under the GWBASIC interpreter.  The following shows how
to make these calls.

Insert an initialization sequence such as:

                 10  DEF SEG=0
                 20  MSEG=256*PEEK(51*4+3)+PEEK(51*4+2)
                 30  MOUSE=256*PEEK(51*4+1)+PEEK(51*4)+2
                 40  DEF SEG=MSEG

Be sure that the statements appear before any calls to mouse
functions.  Then use the CALL statement to make the call.

                 CALL MOUSE(M1%,M2%,M3%,M4%)

where MOUSE is the variable containing the entry offset of the
mouse software, and M1%, M2%, M3%, and M4% are the names of the
integer variables you have chosen for parameters in this call. 
They correspond to the values for AX, BX, CX, and DX which are
described in this document.  As an example:





                 100  'Set minimum and maximum horizontal
                 position to
                      '(320,100)
                 200  M1%=7 'function number is 7
                 300  M3%=0 'minimum coordinate
                 400  M4%=639 'maximum coordinate
                 500  CALL MOUSE(M1%,M2%,M3%,M4%) 
                 
                 
**Cursor Descriptions - Text and Graphics Cursors**

The characteristics of the cursor are determined by Functions 9
and 10. MOUSE 6300 has both text and graphics cursors available.
The graphics cursor is a shape that moves over the images on the
screen. The shape can include an arrow, a sight mark, or others.
The software text cursor is a character attribute that moves
from character to character on the screen. The hardware text
cursor is a moving, sometimes flashing block which also moves
from character to character on the screen. The three cursors are
exclusive - only one can be on the screen at one time. You have
the option of choosing which cursor will appear on the screen
and of switching from one cursor to the other.

Note that when a mouse function refers to the graphics cursor
location it is referring to the point on the screen that lies
directly under the cursor's target area. The target area is the
point in the cursor block that the mouse software uses to
determine the cursor coordinates. The upper left corner of the
cursor block is used to determine the coordinates.

**Notice to System Programmers**

System programmers who intercept the keyboard hardware interrupt
(int 9) or the video i/o software interrupt (int 10h) should
exercise utmost care, and note the following:

The mouse driver itself intercepts these two interrupts.

The mouse driver expects to receive all the codes which are
relevant for the mouse from the keyboard.  If a program which
intercepts the keyboard interrupt is loaded after the driver the
following codes from the keyboard should fall through and be
left available for the mouse driver:


                               -2-
LOGITECH - mouse.doc for AT&T                      v.1.0  2/85



                 77h, 78h, 79h, F7h, F8h, F9h
                 7Ah, 7Bh, 7Ch, 7Dh, FAh, FBh, FCh, FDh,
                 FEh and the next 2 codes which follow an
                 occurrence of FEh (FEh is the prefix character
                 for mouse movement reports).

Codes 74h, 75h, 76h, F4h, F5h, F6h are reserved for future use
by mouse software.

All other codes are left by the mouse driver to the next
interrupt handler on the chain (presumably the ROM resident
keyboard interrupt handler).

With regard to video (int 10h) the program should guarantee that
video mode changes (function 0) are intercepted by the mouse
driver. The mouse driver guarantees consistency of the screen
contents to programs that write on the screen via int 10h (or
via DOS).  

Some programs write directly on the video memory.  In this case
the application program should use function 2 (hide cursor) or
16 (conditional hide cursor) before writing, then function 1
(show cursor) after writing.  GWBasic is an example of such a
program.

To check for the presence in memory of the LOGITECH mouse driver
one should check for a "signature" at the offset 10h from the
entry of software interrupt S1.  The signature is the string
"LOGITECH MOUSE DRIVER".

















                               -3-
LOGITECH - mouse.doc for AT&T                      v.1.0  2/85



List of Mouse Functions

The following functions apply to MOUSE 6300. These functions
will be described in greater detail in subsequent sections. 

Microsoft Compatible Functions

Functions                           Function Number

Mouse Initialization                     0
Show Cursor           1
Hide Cursor           2
Get Mouse Position & Button Status       3
Set Mouse Cursor Position                                4
Get Button Press Information                             5
Get Button Release Information           6
Set Minimum & Maximum X Position         7
Set Minimum & Maximum Y Position         8
Define Graphics Cursor Block                             9
Define Text Cursor                       10
Read Mouse Motion Counters                               11
Define Event Handler                     12
Light Pen Emulation Mode On                              13
Light Pen Emulation Mode Off                             14
Set Mouse Motion/Pixel Ratio                             15
Conditional Hide Cursor                                  16

LOGITECH Specific Functions

Get Acceleration      29
Set Acceleration      30
Set Grid                                 31
Get Mouse Mode        32
Set Mouse Mode        33
Get Keyboard Emulation Configuration     34
Set Keyboard Emulation Configuration     35









                               -4-
LOGITECH - mouse.doc for AT&T                      v.1.0  2/85



**Description of the Mouse Functions**

The following descriptions of the mouse functions specify the
required input and the expected output of each function. The
descriptions also include any special circumstances involved
with each function. The input and output parameters are
specified as values for 8086 registers.


**Mouse Initialization - Function 0**

This function describes whether the mouse hardware and software
are installed. The mouse status is 0 if the mouse hardware and
software are not installed and -1 if the hardware and software
are installed.

                 Input                   Output

                 AX = 0                  AX = mouse status
                                         BX = number of buttons


**Show Cursor - Function 1**

This function increments the internal cursor flag. If the flag
is 0 it displays the cursor on the screen. The cursor tracks the
motion of the mouse, changing position as the mouse changes
position.

                 Input                   Output

                 AX = 1                  ----


**Hide Cursor - Function 2**

This function removes the cursor from the screen and decrements
the internal cursor flag. Although the cursor is hidden it still
tracks the motion of the mouse, changing position as the mouse
changes position.

                 Input                   Output

                 AX = 2                  ----


                               -5-
LOGITECH - mouse.doc for AT&T                      v.1.0  2/85


**Get Mouse Position & Button Status - Function 3**

This function reports the status of the buttons. It also reports
the position of the cursor horizontally and vertically. The
button status is a single integer value with bit 0 representing
the left button and bit 1 the right. When the button is down a
bit is 1 and when the button is up a bit is 0.

                 Input                   Output

                 AX = 3                  BX = button status
                                         CX = horizontal cursor 
                                              position 
                                         DX = vertical cursor
                                              position


**Set Mouse Cursor Position - Function 4**

This function sets the cursor to the specified horizontal and
vertical positions on the screen. The new values must be within
the specified ranges of the virtual screen. If you are not using
a high resolution screen the values are rounded to the nearest
values permitted by the screen for horizontal and vertical
positions.

                 Input                   Output

                 AX = 4                  ----
                 CX = new cursor position
                      (horizontal)
                 DX = new cursor position
                      (vertical)


**Get Button Press Information - Function 5**

This function reports on the current button status.  It gives a
count of button presses since the last call to Function 5, and
it gives the horizontal and vertical position of the cursor the
last time the button was pressed.

The BX parameter indicates which button was pressed. If BX is 0,
the left button is checked.  If BX is 1, the right button is
checked. The button status is a single integer 

                               -6-
LOGITECH - mouse.doc for AT&T                      v.1.0  2/85


value. Bit 0 represents the left button and bit 1 the right. If
the button is down a bit is 1 and if it is up a bit is 0. 
                 Input                   Output

                 AX = 5                  AX = button status
                 BX = button             BX = number of button
presses
                                         CX = cursor at last
press
                                              (horizontal)
                                         DX = cursor at last
press
                                              (vertical)


**Get Button Release Information - Function 6**

This function reports on the current button status. It reports a
count of the button releases since the last call to Function 6,
and it gives the horizontal and vertical position of the cursor
since the last time the button was released.

The BX parameter specifies which button is checked. If BX is 0,
the left button is checked. If BX is 1, the right button is
checked. The button status is a single integer value. Bit 0
represents the left button and bit 1 represents the right
button. If a button is down a bit is 1 and if a bit is 0 a
button is up.


**Set Minimum & Maximum X Position - Function 7**

This function sets the minimum and maximum possible cursor
positions on the screen. All cursor movement is restricted to
this area once the area is set. The virtual screen determines
the maximum and minimum values.

If the cursor is outside the defined area when the call is made,
it moves to just inside the area. If the minimum value is
greater than the maximum the two values are exchanged.

                 Input                   Output

                 AX = 7                  ----
                 CX = minimum position
                 DX = maximum position

                               -7-
LOGITECH - mouse.doc for AT&T                      v.1.0  2/85


**Set Minimum & Maximum Y Position - Function 8**

This function sets the minimum and maximum possible cursor
positions on the screen. All cursor movement is restricted to
this area once the area is set. The virtual screen determines
the maximum and minimum values.

If the cursor is outside the defined area when the call is made,
it moves to just inside the area. If the minimum value is
greater than the maximum the two values are switched.

                 Input                   Output

                 AX = 8                  ----
                 CX = minimum position
                 DX = maximum position


**Define Graphics Cursor Block - Function 9**

This function determines what the shape and color of the cursor
will be when it is in graphics mode, and it identifies the
center of the cursor. The cursor hot spot values must be within
the range of -16 to 16. They define one pixel within the cursor.

                 Input                   Output

                 AX = 9                  ----
                 BX = horizontal cursor hot spot
                 CX = vertical cursor hot spot
                 DX = pointer to screen and cursor masks

**Define Text Cursor - Function 10**

This function selects the software or hardware cursor. When the
hardware cursor is selected this function sets the first and
last scan lines which will be shown on the screen. The value of
the parameter BX selects the cursor type. If the value is 0, the
software text cursor is selected. If the value is 1, the
hardware text cursor is selected. When the software text cursor
is selected, the values of parameters CX and DX specify the
screen and cursor masks. When the hardware cursor is selected,
the parameters of CX and DX must contain the line numbers of the
first and last scan line in the cursor to be shown on the
screen.

                               -8-
LOGITECH - mouse.doc for AT&T                      v.1.0  2/85



                 Input                   Output

                 AX = 10                 ----
                 BX = select cursor
                 CX = screen mask value/scan line start
                 DX = cursor mask value/scan line stop

**Read Mouse Motion Counters - Function 11**

NOTE: In mouse.com there is an accelerator which affects fast
mouse movement. Cursor movement is expanded by the accelerator
if hand movement is over a certain speed threshold. With slow
mouse movement the mouse resolution is 200 Steps per Inch (SPI).
With fast mouse movement it is 400 SPI. Information in the
following sections changes according to whether the accelerator
is in effect or not.

This function returns the horizontal and vertical step count,
which is the distance the mouse has moved in 1/200 inch
increments, since the last call to this function.  With the
Default Accelerator installed the ratio of mouse to cursor
movement is variable between 1/200 and 1/400.  The step count is
always within the range -32768 to 32767. A positive horizontal
count specifies a motion to the right while a positive vertical
count specifies a motion to the bottom of the screen. The step
count is set to 0 after the call is completed.

                 Input                   Output

                 AX = 11                 CX = horizontal count
                                         DX = vertical count

**Define Event Handler - Function 12**

This routine sets the call mask and subroutine address for the
mouse software interrupts. The software interrupts stop
execution of your program and call the specified subroutine
whenever one or more of the conditions defined by the call mask
occur. The call mask is a single integer value which defines the
conditions which will cause an interrupt. Each 
bit in the call mask corresponds to a specific condition:





                               -9-
LOGITECH - mouse.doc for AT&T                      v.1.0  2/85



                 Mask Bit                Condition

                 0                       change cursor position
                 1                       press left button
                 2                       release left button
                 3                       press right button
                 4                       release right button
                 5-15                    not used


                 Input                   Output

                 AX = 12                 ----
                 CX = call mask
                 DX = address offset to subroutine


**Light Pen Emulation Mode On - Function 13**

This function enables light pen emulation by the mouse. When the
mouse emulates the light pen, calls to the pen function will
return the cursor position at the last pen down which is
controlled by the mouse buttons. The pen is down when both
buttons are down. The pen is off the screen when both buttons
are up.

                 Input                   Output

                 AX = 13                 ----

**Light Pen Emulation Mode Off - Function 14**

This function disables the light pen emulation mode. When light
pen simulation is disabled, calls to the pen function return
information about the light pen only.

                 Input                   Output

                 AX = 14                 ----


**Set Mouse Motion/Pixel Ratio - Function 15**

This function sets the mouse motion to screen pixel ratio. 

                               -10-
LOGITECH - mouse.doc for AT&T                      v.1.0  2/85



The horizontal and vertical ratios specify the amount of mouse
motion at 8 pixels with the values falling within the range of 1
to 32767. The default values are 8 steps to 8 pixels
horizontally and 16 steps to 8 pixels vertically. This is
equivalent to 3.2 inches of horizontal mouse movement and 2.0
inches of vertical mouse movement.

                 Input                   Output

                 AX = 15                 ----
                 CX = horizontal step to pixel ratio
                 DX = vertical step to pixel ratio

**Conditional Hide Cursor - Function 16**

This function allows the user to define an area on the screen
within which the mouse will turn off. Performing the Show Cursor
Function - Function 1 - resets the region and turns the mouse
back on. This function is used to guard a portion of the screen
which your program is about to update.

                 Input                   Output

                 AX = 16                 ----
                 CX = left margin
                 DX = top margin
                 SI = right margin
                 DI = bottom margin

**Get Acceleration - Function 29**

This mode returns the acceleration of the mouse in real mouse
mode.

                 Input                   Output

                 AX = 29                 BX = acceleration type
                                         ES:DX = acceleration
vector                                                         
 address

**Set Acceleration - Function 30**

This mode establishes the acceleration of the mouse in real
mouse mode.

                               -11-
LOGITECH - mouse.doc for AT&T                      v.1.0  2/85



                 Input                   Output

                 AX = 30                 ----
                 BX = acceleration type
                 ES:DX = acceleration vector             
                              address

Acceleration type

                 BX = 0   default accelerator

                 BX = 1   use the given accelerator vector

                 BX = 2   no accelerator

Acceleration is an array of 128 bytes. Each element contains the
value to be substituted as relative mouse movements count when
the value used as index for the array is received from the mouse

The Default Acceleration Table is built up in the following
way:  

                 Displacements 0,1,2 and 3 are left unchanged.
                 Displacements 4 through 9 are mapped into 5
                 through 15.
                 Displacements 10 through 14 are mapped into 18
                 through 26.
                 Displacements 15 through 19 are mapped into 29
                 through 37.
                 Displacements 20 through 127 are mapped into 40
                 through 254.

**Set Grid - Function 31**

This function allows the user to set the cursor movements so
that they move on the points of a grid on the screen.

                 Input                   Output

                 AX = 30                                 
                 BX = horizontal grid value
                 CX = vertical grid value



                               -12-
LOGITECH - mouse.doc for AT&T                      v.1.0  2/85



                 Grid Value:             0 = 1 = no grid
                                         distance of points 

Implementation restriction: Only values which are powers of 2
(2,4,8,16...) are allowed as grid values.

The set grid function does not apply in text cursor mode.

**Get Mouse Mode - Function 32**

This function distinguishes between realmouse mode and keyboard
emulation mode. The value returned in BX is 0 when the mode is
mousebase and 1 when it is keybase.

                 Input                   Output

                 AX = 32                 BX = mode

**Set Mouse Mode - Function 33**

This function distinguishes between real mouse mode and keyboard
emulation mode. A bit is 0 when real mouse mode is set and 1
when keyboard emulation mode is set.

                 Input                   Output
                 AX = 33                 ----
                 BX = mode


**Get Keyboard Emulation Configuration - Function 34**

This mode gets the configuration for keyboard emulation mode.

                 Input                   Output

                 AX = 34                 ES:DX = parameter
                 ES:DX = address of      structure loaded with
config-
                 parameter structure     uration values







                               -13-
LOGITECH - mouse.doc for AT&T                      v.1.0  2/85


Parameter Structure

                 WORD    length of left button press string
                 DWORD   pointer to left button press string
                 WORD    length of left button release string
                 DWORD   pointer to left button release string
                 WORD    length of middle button press string
                 DWORD   pointer to middle button press string
                 WORD    length of middle button release string
                 DWORD   pointer to middle button release string
                 WORD    length of right button press string
                 DWORD   pointer to right button press string
                 WORD    length of right button release string
                 DWORD   pointer to right button release string
                 WORD    length of forward movement string
                 DWORD   pointer to forward movement string
                 WORD    length of backward movement string
                 DWORD   pointer to backward movement string
                 WORD    length of left movement string
                 DWORD   pointer to left movement string
                 WORD    length of right movement string
                 DWORD   pointer to right movement string
                 WORD    x scale
                 WORD    y scale

Pointers are offset, segment in the 8086 conventions (offset
lower word, segment upper word).

Lengths are interpreted as buffer length in input.  They will
contain actual string lengths in the output.

Length of the button strings cannot exceed 30.

Length of the movement strings cannot exceed 4.

A length of 0 is legal. In this case the corresponding pointer
will not be used. The value for the corresponding item will not
be returned.

-1 will be returned in length if the buffer is shorter than the
actual string.

**Set Keyboard Emulation Configuration - Function 35**

This mode sets the configuration for keyboard emulation mode.

                               -14-
LOGITECH - mouse.doc for AT&T                      v.1.0  2/85



                 Input 

                 AX = 35
                 BX = configuration type
                 ES:DX = address of parameter structure
containing
                         configuration values

Configuration Type

                 0 = use specified configuration

                 1 = use default configuration; parameter
structure
                     is not used

                 2 = use "reserved" configuration (for LOGITECH
use                        only); parameter structure is not
used.

Parameter Structure
(See chart for Function 34 - Get Keyboard Emulation Config.)
Pointers are offset, segment in the 8086 conventions (offset
lower word, segment upper word).

The length of the button strings cannot exceed 30.

The length of the movement strings cannot exceed 4.

Longer strings will be truncated.

A length of 0 is legal. The corresponding pointer will not be
used and no string will be attached to the specific button or
movement.

Function 35 will not alter the mouse mode. If a new
configuration is issued while the mouse is in keyboard emulation
mode, the new configuration will be in effect immediately. If a
new configuration is issued while the mouse is in real mouse
mode, the new configuration will be in effect at the next
setmouse mode which specifies keyboard emulation mode.

The default configuration in keybase mode is keyboard cursor
keys for mouse movement, <CR> for the left mouse button, <esc>
for the right mouse button, and 5 for both the horizontal and
vertical mouse movement scale.