Triones

Bus Master / PIO Device Drivers

for Intel 82430FX/HX Chipset

Quick Installation Guide

(February 22, 1996)

1. MS-DOS / WINDOWS / WFW

You should install CD-ROM in secondary channel in Windows (WFW).

Change the current directory to a:\ or b:\

Under DOS command line prompt, run the SETUP directly.

After entering the setup utility, just follow the instructions of the setup.

2. WINDOWS NT3.5

From the Program Manager, double click on "Windows NT Setup" in the Main group.

Select "Options/Add/Remove SCSI Adapters..."

Click on Add.

The "Select SCSI Adapter Option" dialog will appear; select "Other (Requires a disk from a hardware manufacturer)" from the "Adapter:" list box.

Next, the "Insert Diskette" dialog box will appear; insert the Triones 82430FX/HX Bus Master EIDE/ATAPI Driver disk into Drive A: and type in "a:\winnt35" and <Return>.

Next, the "Select OEM Option" dialog box will appear; select "82430FX/HX Bus Master EIDE/ATAPI" and click "OK."

Next, the "Select SCSI Adapter Option" dialogbox will appear; click on the "Install" button in the dialog box. If installation is successful, the "SCSI Adapter Setup" dialog box will reappear, and "82430FX/HX Bus Master EIDE/ATAPI" will be listed. That means the driver is installed.

Reboot your system to load the driver.

3. WINDOWS 95

The installation procedures described here are created based on the Windows 95 Final Beta Release version.

Close any running applications.

Remove references to installed real-mode IDE device drivers in the AUTOEXEC.BAT and CONFIG.SYS files, especially any drivers that control ATAPI CD-ROM and special IDE features.

Remove references to the default installed IDE device drivers:

Open the Control Panel folder and invoke the System applet.

Click on the Device Manager option.

Click on the View Devices by Type button. A list of the system devices connected to the system will be displayed.

Click on the Hard disk controllers record and remove all the instances under this record.

Select Yes when prompted to re-start Windows 95.

Windows 95 will re-start.

Install the Bus Master EIDE/ATAPI driver:

After you remove references to the default installed IDE device drivers and re-start the system. Windows 95 will report that a Standard Dual PCI IDE Controller or Standard ESDI/IDE Controller has been detected in the system.

Select Driver from Manufacturer's Disk.

Insert the floppy disk containing the driver file (IDEATAPI.MPD) and installation file (IDEATAPI.INF) into the system.

Choose OK to load the driver from the A:\WIN95.

Windows 95 will display a Select Device window. Choose OK. When Windows 95 reports that a Standard Dual PCI IDE Controller has been detected, the selected device type should be the Intel 82430FX/HX Bus Master IDE Controllers. When Windows 95 reports that a Standard