Microsoft LanManager installation with NE2000 Compatible NDIS driver
     --------------------------------------------------------------------
				     for
                        NIC-2002/UK series LAN Adapter




1. Installation Introduction for LAN Manager V2.0
--------------------------------------------------

 a. Type 'SETUP' in the LanManager Directory.  Press ENTER.

 b. Press ENTER.

 c. Choose "Import Network Drivers..." in "Action".  Press Enter.

 d. Type the specific source drive for the Driver Disk (A: or B:).

 e. Insert the Driver Disk in the specific drive (A: or B:).  Press ENTER.
    "Import Network Drivers" appears.

 f. Press the SPACEBAR to select Network Adapter Card, "NE2000 Compatible
    Ethernet Adapter Card".  Press Enter.

 g. Press NO button.

 h. Press Enter three times.
    Network Driver appears.

 i. Choose "NE2000 Compatible Ethernet Adapter Card" in Network Adapter Cards
    select menu, then press <Add driver> button, and press <Add protocol>,
    press <OK>. Workstation Primary parameters appear, press <OK>.

 k. Press <OK> three times.

 l. Choose "Save" in "Action".

 m. Press F3 to Exit.

*******************************************************************************



2. Installation Introduction for LAN Manager V2.1
--------------------------------------------------

 a. Type 'LMSETUP' in LanManager Directory.  Press ENTER.
    Microsoft LAN Manager Setup appears.

 b. Choose "Network Drivers..." in "Configuration".  Press ENTER.

 c. Choose <Add New Configs>.  Press ENTER.
    Network Adapter Driver appears.

 d. Choose <Other Driver>.  Press ENTER.

 e. Insert the Driver Disk in the specified drive (A: or B:), key in the
    specified drive (A: or B:), then push the <ok> button.

 f. Select an available Network Adapter Driver, NE2000 Compatible
    Ethernet Adapter Card. Push the <OK> button.

 g. Press the SPACEBAR to select the protocol that you want.

 h. Push <OK> button.
    Configuration Complete appears.

 i. Push <Save> button.

 j. Press "F3" to exit.

 k. Press Enter.



Sample configuration files:
---------------------------
3. CONFIG.SYS

   a.<V2.0>
      LASTDRIVE=Z
      BUFFERS = 35
      FILES = 35
      SHELL=C:\DOS50\COMMAND.COM C:\DOS50\e:1000 /p /E:1024
      DEVICE=C:\HIMEM.SYS
      DEVICE=C:\DOS50\SETVER.EXE
      DOS=HIGH,UMB

      DEVICE=C:\LANMAN.DOS\DRIVERS\PROTMAN\PROTMAN.DOS /i:C:\LANMAN.DOS
      DEVICE=C:\LANMAN.DOS\DRIVERS\ETHNE\ACCNE\ETHNE.DOS
      DEVICE=C:\LANMAN.DOS\DRIVERS\PROTOCOL\NETBEUI\NETBEUI.DOS


    b.<V2.1>
      LASTDRIVE=Z
      BUFFERS = 35
      FILES = 35
      SHELL=C:\DOS50\COMMAND.COM C:\DOS50\e:1000 /p /E:1024
      DEVICE=C:\HIMEM.SYS
      DEVICE=C:\LANMAN.DOS\DRIVERS\DOSUTILS\EMM386.EXE NoEMS
      DEVICE=C:\DOS50\SETVER.EXE
      DOS=HIGH,UMB

      DEVICE=C:\LANMAN.DOS\DRIVERS\PROTMAN\PROTMAN.DOS /i:C:\LANMAN.DOS
      DEVICE=C:\LANMAN.DOS\DRIVERS\ETHNE\ACCNE\ETHNE.DOS



4. PROTOCOL.INI file for LAN Manager.

  a. V2.0
       [PROTOCOL MANAGER]
         DRIVERNAME = PROTMAN$

       [NETBEUI_XIF]
         Drivername = netbeui$
         BINDINGS = "ACCNE_NIF"

       [ACCNE_NIF]
       ; PROTOCOL.INI for NE2000 Ethernet Aadapter

           drivername = ETHNE$
       ;   irq = 3
       ;   iobase = 0x300

       ; End of this sample file



   b. V2.1
       [PROTMAN]
         DRIVERNAME = PROTMAN$
         DYNAMIC = YES
         PRIORITY = NETBEUI

       [NETBEUI_XIF]
         Drivername = netbeui$
         SESSIONS = 6
         NCBS = 12
         BINDINGS = "ACCNE_NIF"
         LANABASE = 0

       [ACCNE_NIF]
       ; PROTOCOL.INI for NE2000 Compatible ethernet adapter

           drivername = ETHNE$
       ;   irq = 3
       ;   iobase = 0x300

       ; End of this sample file



5. Autoexec.bat file for LAN Manager.

   a. V2.0

   @echo off
   PROMPT $P$G
   PATH=c:\PE2;C:\DOS50;C:\NC;
   APPEND=C:\PE2;C:\DOS50;
   REM ==== LANMAN 2.0 == DO NOT MODIFY BETWEEN THESE LINES === LANMAN 2.0 ====
   SET PATH=C:\LANMAN.DOS\NETPROG;%PATH%
   C:\LANMAN.DOS\DRIVERS\PROTMAN\NETBIND
   NET START WORKSTATION
   REM ==== LANMAN 2.0 == DO NOT MODIFY BETWEEN THESE LINES === LANMAN 2.0 ====


   b. V2.1
   @echo off
   PROMPT $P$G
   PATH=c:\PE2;C:\DOS50;C:\NC;
   APPEND=C:\PE2;C:\DOS50;

   @REM ==== LANMAN 2.1 == DO NOT MODIFY BETWEEN THESE LINES === LANMAN 2.1 ===
   SET PATH=C:\LANMAN.DOS\NETPROG;%PATH%
   NET START WORKSTATION
   LOAD NETBEUI
   @REM ==== LANMAN 2.1 == DO NOT MODIFY BETWEEN THESE LINES === LANMAN 2.1 ===