Novell Netware installation with NE2000 Compatible driver
          ---------------------------------------------------------
				     for
                        NIC-2002/UK series LAN Adapter


1. Installation for Netware Versions Below 3.11 using IPX
---------------------------------------------------------

   a. Using the correct shell Generation program (shgen, wsgen)
      Select the NE2000 option


2. Installation for All Netware Versions supporting ODI
-------------------------------------------------------

1.   Things You Need
     ---------------
           Before you start the installation  process  make
           sure you have the following:

           a)    Hardware Driver Disk
           b)    Novell DOS ODI WORKSTATION SERVICES diskette.

        The following drivers must be loaded in the exact order

            LSL     - Found on the Novell DOS ODI WORKSTATION SERVICES diskette
            NWMLID  - Found on the NIC-2002 Driver Disk
            IPXODI  - Found on the Novell DOS ODI WORKSTATION SERVICES diskette
            NETX    - Found on the Novell DOS ODI WORKSTATION SERVICES diskette

        If the NIC driver, NWMLID executed successfully, it will inform you of
        the adapter mode and related configurations.  Otherwise you will
        see error messages telling you the reason the driver did not load.

        Note: The ODI driver will always parse your NET.CFG file first.  If the
              related  adapter's configuration  parameters are found, they
              will be defaulted to IRQ 3 BASE 300 even though they
              conflict with parameters stored in the EEPROM of adapter, thus
              it will fail to initialize the adapter.

        Below is a sample NET.CFG file:

                LINK DRIVER NWMLID
                    INT   5
                    PORT  320
                       :
                       :

        You can refer to the Netware Manuals for more information about NET.CFG

        Novell has changed the Ethernet  default frame  type to 802.2
        starting with the release of NetWare v4.0. The move has been made to
        enable it to better support future protocols and networking features.
        Some of these features are:  IPX with checksum, security enhancements,
        and  protocol independence.  Following this change, the default frame
        type of the DOS ODI driver is Ethernet 802.2 when there  is no protocol
        binding in NET.CFG file.  With this situation, if  your server  is not
        NetWare v4.0, please make sure the Ethernet 802.2 frame type has been
        bound before logging in to it.



3. Novell NetWare V4.0x Server Driver Installation
--------------------------------------------------

Things you Need
---------------
Make sure you have the following:

1. Driver Diskette
2. Novell DOS ODI Workstation Services Diskette

Installation Procedure
----------------------
1. Insert the Driver Diskette into drive A: and check the contents of the
   subdirectory \NETWARE\ODI\4.00. It should have the following files:

   ACC40.LAN    ----> your Novell NetWare v4.0 Server Driver
   ACC40.LDI    ----> your Novell NetWare v4.0 Server Driver
                      configuration file

2. At the NetWare prompt (indicated by the Server name), run
   the INSTALL.NLM program by typing:

  server name: LOAD INSTALL     <Enter>

3. Follow the instructions on screen to complete the process.
   Press <Enter> to confirm each choice:

   Maintenance/Selective Install                <Enter>
   LAN Driver Options (Configure/Load/...)      <Enter>

4. Press the <Ins> key to insert other drivers you wish to install.

5. Press <F3> to display the driver loading path as follows:
   A:\NETWARE\ODI\4.00          <Enter>

6. The ACC40.LAN will appear as an item under the
   "Select a LAN Driver" menu.  Select it to load the driver
   and start the binding process.  This will allow you to
   load and bind all 4 frame types supported by NetWare.

7. Next time you reboot your NetWare 4.0x server, do so by
   following steps 2 to 4 above.


Notes about the Novell v4.0x and the v3.1x drivers
--------------------------------------------------

1. The NetWare v4.0x and v3.11 drivers have different
   architectures.  When using NetWare v4.x, you should
   load the MSM.NLM and ETHERTSM.NLM modules
   before loading server driver ACC40.LAN.

2. ACC40.LAN is your server driver for NetWare v4.0.  When
   loading ACC40.LAN, it will check whether or not
   these two modules (MSM.NLM and ETHERTSM.NLM) have been
   loaded.  If not, it will load them automatically.

3. After the ACC40.LAN is loaded, type the "MODULES" command to
   view and confirm that the additional modules, MSM.NLM and
   ETHERTSM.NLM loaded.

4. The default frame type for ACC40.LAN binding in NetWare v4.0x
   is Ethernet_802.2 and not Ethernet_802.3.