Packet Driver installation with NE2000 Compatible NDIS driver
         -------------------------------------------------------------
				     for
                        NIC-2002/UK series LAN Adapter


1. Installation Introductions for the Packet Driver
---------------------------------------------------
   a. Copy NWPD.COM from the \PKTDRV subdir on the driver disk to the
      subdirectory where you want to load the driver.


NWPD syntax:
To load the packet driver use the following syntax:

NWPD [-cTYPE] [-d] [-n] [-w] [-u] [-h] <PD_INT_NO> [IRQ] [IO_BASE]

where:

[-cTYPE]	The Packet Driver will detect card type automatically.
                Options are: NE1000, NE2000, NE2.

[-d]		The "-d" option does not start the LAN card until this driver
		is called by the higher layer programs first.

[-n]		Your  NOVELL server uses NOVELL ISO-like packets.  Your NOVELL
		workstation uses NOVELL 8137 packets.  You can use this option
		to convert NOVELL 8137 packets into  NOVELL ISO-like packets.
		In  your workstation, whatever the packets are, they can com-
		mmunicate with each other.

[-w]            Using this option will allow the packet driver to run under
                Windows.

[-u]		Using this option will unload the Packet Driver.

[-h]		Using this option can display the on-line help.

<PD_INT_NO>	This specifies the software interrupt (IRQ) where  you	will
		load the packet driver.  It must be in the range 0x60 to 0x80.

		The PC/TCP kernel, by default, is loaded at interrupt 0x61 (so
		don't load the packet driver there!)

[IRQ]           This specifies the hardware interrupt (IRQ) of the NIC-2002.

[IO_BASE]       This specifies the Base I/O address of the NIC-2002.



Example:

The following command line loads the NE1000 & NE2000 series Packet Driver
at software interrupt 60h, at I/O address 300, at hardware interrupt 3:

NWPD 0x60 3 0x300

Note:  The default I/O address is 300.
Note:  The default hardware interrupt is 3
Note:  You must place '0x' prior to I/O address and interrupt parameters.

The following command line loads the NE1000 & NE2000 series Packet Driver
at software interrupt 63h, at I/O address 320, at hardware interrupt 5,
running under windows:

NWPD 0x63 5 0x320 -w


After the Packet Driver is loaded, you can run the PC/TCP kernel ETHDRV.EXE.
The PC is then ready for PC/TCP communications.

To run PC/TCP applications, load PC/TCP Kernel
    ("ETHDRV.EXE").

    a) Refer to PC/TCP manual, Command Reference
       section, Chapter 2.3.
    b) The following example will load the Kernel and
       allocate 8 packet buffers.  Increasing the
       # of packet buffers (from the default of 5) prevents
       dropping packets due to a buffer shortage.

	ETHDRV -p 8 <ret>

    c) At this point, you are ready to run PC/TCP applications
       Example: ftp 192.72.24.202
            where '192.72.24.202' is the host address.

       Note: You must know the host address.

      For information regarding the "FTP's PC/TCP Network
      Software for DOS" packages, please contact:

      FTP Software, Inc.
      26 Princess Street
      Wakefield, MA  01880
      (617) 246-0900

How to Communicate with NCSA TelNet.

1. Make sure you have NCSA Telnet V2.3 or later to support the packet
   driver interface.

2. Install the NCSA software onto your system.	Please
   refer to the NCSA documention for detailed instructions.

3. Load Packet Driver (nwpd 0x60):

   a) Refer to "Packet Driver Syntax" section above.
   b) To view the hint screen, type

      nwpd -h <ret>

   c) The following example will load the packet driver
      using interrupt vector 60 (hex).	The iobase
      and irq will be read from the software
      configured adapter:

      nwpd 0x60   <ret>

4. At this point you are ready to run NCSA applications
      Example: ftp 192.72.24.202
            where '192.72.24.202' is host address.

       Note: You must know the host address.

      For information regarding NCSA's products please
      contact:

      National Center for Supercomputing Applications
      264 Computing Applications Building
      605 E. Springfield Ave.
      Champaign, Ill. 61820
      (217) 244-0638
      telbug@ncsa.uiuc.edu