Windows for Workgroups 3.10 installation with NE2000 Compatible NDIS driver
   ---------------------------------------------------------------------------
				     for
                        NIC-2002/UK series LAN Adapter






1. Installation Introduction for Windows for Workgroups
-------------------------------------------------------

a. Select "Control Panel" icon from the Main group in Windows.

b. Select "Network" icon.

c. Select "Adapters" item in "Option" dialog.

d. Press the  Add button.

e. Select "Unlisted or Updated Network Adapter".
   "install driver" appears.

f. Key in the drive and path name for the driver diskette. (A:\ndis or B:\ndis)

g. Insert your Driver Disk in specified drive.  Press ENTER.

h. Press <OK>.

i. Press <close>.

j. Press <OK> twice.

k. Restart computer.


2. Example of CONFIG.SYS file

   FILES=30
   buffers=30
   STACKS=9,256
   DEVICE=c:\windows\HIMEM.sys

   device=C:\WINDOWS\protman.dos /i:C:\WINDOWS
   device=C:\WINDOWS\ethne.dos
   device=C:\WINDOWS\workgrp.sys
   LASTDRIVE=y

3. Example of PROTOCOL.INI file in Windows for Workgroup

   [network.setup]
   version=0x3100
   netcard=uk000xd,1,UK000XD
   transport=ms$netbeui,MS$NETBEUI
   lana0=uk000xd,1,ms$netbeui

   [protman]
   DriverName=PROTMAN$
   PRIORITY=MS$NETBEUI

   [UK000XD]
   DriverName=ETHNE$

   [MS$NETBEUI]
   DriverName=netbeui$
   SESSIONS=10
   NCBS=32
   BINDINGS=UK000XD
   LANABASE=0

4. Example of AUTOEXEC.BAT

   C:\WINDOWS\net start
   C:\WINDOWS\SMARTDRV.EXE
   @ECHO OFF
   PROMPT $p$g
   PATH C:\WINDOWS;
   SET TEMP=C:\WINDOWS\TEMP