******************************************************************************
 *            Advanced NE2000 Compatible Card IBM LAN Server driver           *
 ******************************************************************************


   A. Diskette Introduction :
   ==========================

   This sub-directory contains the following structures:

   LANSRVR
      ³
      ³
      ÃÄÄ DOS         : Contains IBM LAN SERVER driver for DOS.
      ³    ³
      ³    ÃÄÄ 23     : Conatins IBM LAN SERVER V2.x & V3.x driver and
      ³    ³            installation file.
      ³    ÀÄÄ 40     : Contains IBM LAN SERVER V4.0 driver and installation
      ³
      ÀÄÄ OS2         : Contains IBM LAN SERVER driver for OS/2.


   B. Installation Guildline:
   ==========================

      FOR DOS:
      --------

        1.  Insert the Advanced NE2000 Compatible Card driver diskette
            into floppy drive.

        2.  In the directory the IBM LAN Server program located, press
            "INSTALL" to install the driver for Advanced NE2000 Compatible
            Card.

        3.  In the dialog box, select "Network card" and press ENTER
            to continue.

        4.  In the dialog box, select "Change driver for network card."
            and press ENTER to continue.

        5.  In the dialog box, select "Network card not shown in list
            below ..." and press ENTER to continiue.

        6.  To specify the drive and path to Advanced NE2000 Compatible Card
            driver diskette.

            (e.g.,"A:\LANSRVR\DOS\40").

        7.  The "Advanced NE2000 Compatible Card" is shown in the
            listed dialog box.

        8.  If you need to change the configuration, select "Edit settings
            for network card driver." to change configuration such as IOBASE
            or INTERRUPT number.

        9.  After you installed completely, in DOS prompt copy the driver,
            PNPND.DOS, to the hard disk from the directory the driver
            located.


      FOR OS/2:
      ---------

        1.  Insert the Advanced NE2000 Compatible Card driver diskette into
            floppy drive.

        2.  In IBM LAN Server, select or run the MPTS (Multi Protocol
            Transport Service) program. refer to the IBM LAN Adapter and
            Protocol Support Configuration Guide for more information on
            this utility and for more details on how to install additional
            adapters and device drivers.

        3.  From the IBM MPTS dialog box, choose the "INSTALL" button to
            install a Advanced NE2000 Compatible ethernet card for IBM LAN
            Server environment.If the NE2000 Compatible ethernet card has
            already been installed, go to setp 6 below to continue.

        4.  Specify the drive and path (e.g., "LANSRVR") to the Advanced
            NE2000 Compatible Card driver diskette (e.g., "A:\LANSRVR\OS2").

        5.  After installing/copying the appropriate NIF files from Advanced
            NE2000 Compatible Card driver diskette, IBM MPTS dialog box will
            appear again.

        6.  From the IBM MPTS dialog box, select the "Configure".

        7.  In the Configuration dialog box, choose the "Configure LAN
            transports"(default) option and select "Continue".

        8.  When the Configure Workstation dialog box is displayed, remove
            the current configuration from the Current Configuration list
            box.

        9.  Choose the "Advanced NE2000 Compatible Card" from the Network
            Adapters list box, by highlight the entry. Then choose "Add" the
            Advanced NE2000 Compatible Card to the Current Configuration list
            box.

        10. Highlight the appropriate protocols in the Protocols list box.
            Then choose "Add" to add them to Current Configuration list box.

        11. Choose "OK" to finish installation.
 ======================================================================