******************************************************************************
 *              Advanced NE2000 Compatible Card -- SETUP Program              *
 ******************************************************************************


   A. OVERVIEW
   ===========
   The SETUP.EXE Program is used to configure and verify the correct
   configuration and operation of an Advance NE2000 Compatible Card
   before installing the network software.



   B. BEFORE STARTING THE PROGRAM
   ==============================
   1. Be sure you know the configuration of any adapters.

   2. After turning off the PC's power, insert the adapter into the PC.

       ** Ethernet adapters must be on a properly terminated cable
          (use a BNC " T " connector with two 50 Ohm terminators or
           an AUI loopback connector).

   3. Boot the PC to a DOS prompt.

       ** Memory resident (TSR) programs and device drivers should
          not be loaded while the Diagnostic Program is active, so
          you may need to temporarily rename your CONFIG.SYS and
          AUTOEXEC.BAT files.  The Diagnostic Program is always run
          without loading any network software.



   C. STARTING THE PROGRAM
   =======================
     The Advance NE2000 Compatible card support Jumper,Jumperless and
   Plug&Play modes. In Plug&Play mode, the card's configuration is
   determined automatically by the Plug&Play system PC. You can also use
   the SETUP program to change the card's configuration.

   1. Insert the Advanced NE2000 Compatible Card driver diskette and change
      to the SETUP subdirectory. In the DOS prompt, type GE3SETUP to run SETUP
      program, like as below:

      A:>GE3SETUP

   2. Read the opening screen and press Enter.

   3. Adapter configuration:

       View Setup   - The setup program will auto detect and show the card's
                      configurations, such as I/O port, IRQ,... etc.

       Manual Setup - Select Manual Setup to setup hardware configurations
                      that you want, such as I/O, IRQ, card mode, operating
                      mode, Full duplex, BootROM usage.

       Save Configuration - Save the hardware configuration that be changed.


       ***** Warning *******
       After you changed the hardware configuration, you must reset your
       PC. The adapter will load new configurations that you changed from
       EEPROM.

   4. Adapter Diagnostic

      Hardware Configuration - To view the hardware configurations.

      Ethernet Card Test     - To test the adapters' function is correct.

      Transmit/Receive Test  - To verify the adapter transeveiver is ok.

      Cable Test             - To test cable is no fault.


   D. SUPPORT
   ==========
   If you have any additional questions regarding your Diagnostic
   Program, contact your dealer or distributor technical support
   department.

 ======================================================================