Stealth II S220

Product Specification (6. 11. 1997)

State of the art 3D graphics performance for less.

Realistic 3D graphic in real-time for price conscious Windows® user

Best of class 3D performance for your favourite 3D software

Outrageous 2D Windows® acceleration

Advanced Video Playback

Ready for Diamond's DVD and DTV extensions

Hardware

High Performance 3D Graphics Accelerator

Rendition V2100, 64-bit RISC graphics processor

170 MHz RAMDAC

4 MByte SGRAM (100 MHz)

33/66MHz PCI bus

API: Microsoft Direct3D, Rendition Redline™ and Speedy3D™

Horizontal Sync Signals 31,5kHz - 91kHz

Vertical Sync Signals 43,5Hz - 120Hz

VESA Power Management Support

HighColour with 1280x1024 at 85Hz refresh rate

TrueColour with 1024x768 at 85Hz refresh rate

2D Feature Set

BitBlt, Line Draw, Polygon Fill

Hardware cursor

3D Feature Set

Flat and Gouraud Shading

Texture Mapping with

perspective Correction,

Bilinear and Trilinear Filtering

Mip mapping

Transparency (colour key and alpha)

Z-Buffering (16 bpz)

Fogging

Hardware triangle set-up

Alpha Blending

Anti-aliasing

Video

Scaling of digital with X and Y interpolation

Hardware colour space conversion

Video connector (VMI-A) for Diamond’s DVD decoder and digital TV tuner

Software

BIOS

32 KByte EPROM

VESA Bios extension (VBE) v2.0 support

DDC 2B plug & play

Graphics Driver for

Windows® 95 / 98, Turbo Driver

Windows NT™  4.0

Software for Windows® 95

InControl Tools ( 5 Languages)

DirectX 5 incl. Direct3D, DirectDraw and DirectVideo support

Software MPEG-1 decoder

VPE driver for DVD support

Microsoft Internet Explorer

Software for Windows NT( 4.0

DirectX 3

Microsoft Internet Explorer

Driver for DOS

MS-DOS mode centring and refresh tool

MS-DOS diagnostic software

Software Bundles

Game Sampler CD with RRedline™ and Direct3D games

Documentation

HTML manual (5 languages)

InControl Tools on-line help (5 languages)

System Requirements

Pentium™ P5-90 or better or other 100% compatible system

4 MB System RAM

Windows® 95 or Windows NT™ 4.0

One available PCI 2.1 extension slot

No other active VGA or SVGA compatible graphics accelerator in the PC

Compatibility

100% compatible with VGA, SVGA and VESA Standard

Service & Support

5 years warranty

Free Software updates via BBS, CompuServe and Internet:: //http/www.diamondmm.de

Fax-on-Demand Service

Technical support hot-line

Available

October 1997

Display Modes

| Resolution | Colours | 60 Hz | 70 Hz | 72 Hz | 75 Hz | 85 Hz | 120 Hz |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 640x480 | 256 | ( |
| ( | ( | ( | ( |
|  | 64k | ( |
| ( | ( | ( | ( |
|  | 16M | ( |
| ( | ( | ( | ( |
| 800x600 | 256 | ( |
| ( | ( | ( |
| 64k | ( |
| ( | ( | ( |
| 16M | ( |
| ( | ( | ( |
|  | 1024x768 | 256 | ( | ( |
| ( | ( |
| 64k | ( | ( |
| ( | ( |
| 16M | ( | ( |
| ( | ( |
|  | 1152x864 | 256 | ( | ( |
| ( | ( |
| 64k | ( | ( |
| ( | ( |
| 16M | ( | ( |
| 1280x1024 | 256 | ( |
| ( | ( | ( |
| 64k | ( |
| ( | ( | ( |
|  | 1600x1200 | 256 | ( |
| 64k | ( |

Windows®  95 modes; not necessary available for other operating systems.

Germany:

SPEA Software GmbH

a Diamond Multimedia Company

Moosstraße 18 b

82319 Starnberg - GERMANY

Fax: ++49 8151 21258UK:

Diamond Multimedia Systems Ltd.

610 Wharfedale Road

Winnersh Triangle

Wokingham

Berkshire RG41 5TY  UK

Fax: ++44 1189 444401France:

Diamond Multimedia Southern Europe

6, Blvd. Général Leclerc - Bat C - 15iéme Etage

Clichy 92115 - FRANCE

Fax: ++33-1-47561139

Copyright

© 1997 Diamond Multimedia Systems, Inc.  Subject to technical alterations

Trademarks

(() The brands or product names mentioned are/may be trademarks or registered trademarks of their respective holders.