----------------------------------------------------------------------------
----------------------------------------------------------------------------
----                                                                    ----
----     ÛßßßÜ Ûßßßß Ûßßßß Û   Û     Ü     ÛßßßÜ ÜÛßÛÜ Û   Û Ûßßßß      ----
----     ÛÜÜÜß ÛÜÜÜ  ÛÜÜÜ  ÛÜÜß    ÜÜÛÜÜ   ÛÜÜÜß Û   Û ÛÜÜß  ÛÜÜÜ       ----
----     Û     Û     Û     Û  ßÜ     Û     Û     Û   Û Û  ßÜ Û          ----
----     Û     ÛÜÜÜÜ ÛÜÜÜÜ Û   Û           Û     ßÛÜÛß Û   Û ÛÜÜÜÜ      ----
----                                                                    ----
----                   ÜßßßÜ Û   Û ÜßßßÜ ÛßßßÜ ßßßÛßßß                  ----
----                   Û     ÛÜÜÜÛ ÛÜÜÜÛ ÛÜÜÜß    Û                     ----
----                   Û     Û   Û Û   Û Û   Û    Û                     ----
----                   ßÜÜÜß Û   Û Û   Û Û   ÛÝ   Û                     ----
----                                                                    ----
----           ÜÜÜÜÜ  ÜÜÜÜ   ÜÜÜÜÜÜÜ           ÜÜÜÜ    ÜÜÜ              ----
----     FOR     Û    Û   Û  Û  Û  Û           Û   Û  Û   ß             ----
----             Û    ÛßßßÜ  Û     Û   ßßßßß   Ûßßß   Û                 ----
----     THE   ÜÜÛÜÜ  ÛÜÜÜß  Û     Û           Û      ßÜÜÜß             ----
----                                                                    ----
----                                                                    ----
----------------------------------------------------------------------------
----------------------------------------------------------------------------

            This Document has been created for the Universal use
          of all IBM-PC and PC compatible systems, and encourages
          all users to participate in it's spirit by appending this
          document with any additional material that may be useful
          to other users. 

             It is requested that donators submit peeks and pokes
          to be used in IBM BASIC(A) Version 2.00. If the peeks
          and pokes do not function in ALL current versions of DOS,
          please state which versions it DOES work in. It is also
          asked that donors keep the same format as has been initiated
          with the original submissions.

             Donators to Peeks and Pokes assume NO responsibility
          for their submissions....Use on your own judgement.



-------------------------------------------------------------------
KEYBOARD BUFFER                         Jeff Askew  1/16/84
---------------

        DEF SEG=0: POKE 1050 , PEEK(1052): DEF SEG

        This clears the DOS system keyboard buffer.
        Works very well in compiled Basic.

-------------------------------------------------------------------
MONITORS                                Jeff Askew  1/16/84
--------

        ADDRESS = &HB000  '--- &HB800 to test for color monitor
        DEF SEG = ADDRESS: POKE 1,16
        IF PEEK(1) = 16 THEN MONOCHROME = TRUE    '--- or COLOR=TRUE

        This is one simple way to see which monitors are connected.
        If ADDRESS = &HB800 (for color), then substitute COLOR=TRUE
        for MONOCHRONE=TRUE.

-------------------------------------------------------------------
ACTIVE MONITOR                          Jeff Askew  1/16/84
--------------

        DEF SEG=0: IF (PEEK(1040) AND 48) = 48  THEN MONO.ACTIVE = TRUE
           ELSE COLOR.ACTIVE = TRUE

        This determines which monitor is active at the time.

-------------------------------------------------------------------
MONITOR WIDTH                           Jeff Askew  1/16/84
-------------

        SCREEN 0,0,0,0: WIDTH 40: CLS
        OUT 948,2: OUT 949,62

        This changes the screen dimensions to 40 column width,
        but centers the screen in the middle of the monitor.
        ALL of the commands above must be executed before the
        OUT's even if that is the current video mode set, otherwise
        strange things happen.

-------------------------------------------------------------------
MORE COLORS                             Jeff Askew  1/16/84
-----------

        OUT &H3D8,9  '--- in 80x25 color mode
        OUT &H3D8,8  '--- in 40x25 color mode

        This will disable blinking mode, but enable extended
        background colors in text mode. The full 16 colors
        will then be available for the background, not just
        the usual 8.

-------------------------------------------------------------------
MONOTOR PORTS                           Jeff Askew  2/23/84
-------------
                         ----- Monochrome ----

                 OUT 952,1       'Disable Monochrome display
                 OUT 952,15      'Disable Mono Bilnk
                 OUT 952,255     'Normal Mono Pattern

        --- 80 x 25 Color ---                --- 40 x 25 Color ---  
                                  
      OUT 984,1   'Disable Display         OUT 984,0   'Disable Display
      OUT 984,9   'Disable Blink           OUT 984,8   'Disable Blink
      OUT 984,41  'Normal Pattern          OUT 984,40  'Normal Pattern
                                  
         --- 80 x 25 B&W ---                  --- 40 x 25 B&W ---    
                                  
      OUT 984,5   'Disable Display         OUT 984,4   'Disable Display
      OUT 984,13  'Disable Blink           OUT 984,12  'Disable Blink
      OUT 984,45  'Normal Pattern          OUT 984,44  'Normal Pattern
                                  
                                  
        These OUT's are neat little tricks, and can be quite useful.
        For example: Disable the color monitor's display while doing
        the initial drawings for graphics GET statements. This way,
        the shapes will not flash up on the screen. Not earthshaking
        but it adds a touch of class to the program.

-------------------------------------------------------------------
SCREEN DIMENSIONS                       Jeff Askew  1/16/84
-----------------

        POKE 91,xx      '---  Top row
        POKE 92,xx      '---  Bottom row
        POKE 41,xx      '---  Right column

        These locations store the boundries for Basic's scrolling.
        By changing these values from the defaults, you may alter
        the window that the Basic editor scrolls up. This is a
        most interesting set with many potential uses.

-------------------------------------------------------------------
SYSTEM CONFIGURATION                    Jeff Askew  1/16/84
--------------------
        [ DEF SEG=0 ]

        LOCATION 1040:  DDVV RRXI       ( Bit-Mapped. )
                        DD = Number of Disk drives -1.
                        VV = Current video mode:
                             1 - 40x25 with color/graphics card.
                             2 - 80x25 with c/g card.
                             3 - 80x25 with Monochrome card.
                        RR = Ram installed on the motherboard.
                             0/16k, 1/32k, 2/48k, 3/64k
                        X  = Unused.
                        I  = 0 if no disk drives on system,
                             1 if disk drive(s) are present.

        LOCATION 1041:  PPXG CCCX
                        PP  = Number of printer adapters.
                        X   = Unused.
                        G   = Number of game adapters.
                        CCC = Number of RS232-C adapters.

-------------------------------------------------------------------
KEYBOARD STATUS                         Jeff Askew  1/16/84
---------------
        [ DEF SEG=0 ]

        LOCATION 1047:  ICNS AXLR         ( Bit-Mapped. )
                        I = Insert state (1/0).
                        C = Caps-Lock state.
                        N = Num-Lock state.
                        S = Scroll-Lock state.
                        A = Alt-Shift being pressed.
                        X = Ctrl-Shift being pressed.
                        L = Left shift being pressed.
                        R = Right shift being pressed.
                            
        LOCATION 1048:  ICNS XXXX
                        I = Insert being pressed.
                        C = Caps-Lock being pressed.
                        N = Num-Lock being pressed.
                        S = Scroll-Lock being pressed.

        These are very uesful ways to fully control the keyboard
        input. All bits are either on(1) or off(0).

-------------------------------------------------------------------
KEYBOARD                                Jeff Askew  2/23/84
--------

        OUT 97,204      'disables
        OUT 97,76       'enables

        These port patterns can be used to easily disable the
        keyboard interrupts. When the keyboard is disabled or
        'Locked-up', any key struck is totally ignored. It will
        NOT go into the buffer or be processed. Just be sure 
        that your test program enables it again before ending,
        or you will have to do a hard-IPL!!!
-------------------------------------------------------------------
DISK                                    Jeff Askew  2/23/84
----
      [ DEF SEG = 64 ]

        T=PEEK(69)          'Current Track Number
        H=PEEK(70)          'Current Head Number
        S=PEEK(71)          'Current Sector Number
        B=(128*2^PEEK(72))  'Number of Bytes per Sector

        This set of addresses is very useful for determining
        what version DOS is being used and the current location
        of the Read/Write heads.

-------------------------------------------------------------------
PROTECTION                              Jeff Askew  2/23/84
----------
      [ DEF SEG ]

        POKE 1124,255   'Protects program in memory
        POKE 1124,0     'Un-Protects program

        This can enable you to protect or un-protect a BASIC
        program just like saving it with the ',P' argument to
        the SAVE command. An important point to be aware of is
        that when you POKE 1124,255 to protect the program, this
        also blocks out any subsequent POKE statements, and also
        will not allow you to alter the program in any way!!

-------------------------------------------------------------------
MISC                                    Jeff Askew  2/23/84
----       [ DEF SEG ]

          LOCATION (hex)    PURPOSE
           ----------   ----------------
            2E &  2F    Line number of the current line being executed.
           258 & 259    Offset of start of program variables.
            30 &  31    Offset of start of program text.

        The most important of these three is the last one. Using
        this location in DOS 2.00, one may successfully and con-
        sistantly use the SHELL command (what shell command?!?!).
        Use it as such, with the POKE statements IMMEDIATELY
        following the SHELL command:
          
        DEF SEG : A=PEEK(30) : B=PEEK(31)
        SHELL CHKDSK   '-- Invokes any DOS command
        POKE 30,A : POKE 31,B

-------------------------------------------------------------------
COM:                                    Jeff Askew  2/23/84
----

        ADDR = PEEK(com.num*2-2) + 256*(PEEK(com.num*2-1))
        STATUS = PEEK(ADDR+6)

        The byte returned decodes as follows:

                          SRDC LTAB

    S = Received line signal detect     L = Delta receive line signal detect
    R = Ring indicator                  T = Trailing edge ring indicator
    D = Delta set ready                 A = Delta data set ready
    C = Clear to send                   B = Delta clear to send

        This byte allows easy access and control of communications
        activity and is especially useful in custom communications
        software. ( 'com.num' above is the number of the com port:
        i.e. Com1: = 1 , Com2: = 2 , etc...)

-------------------------------------------------------------------
-------------------------------------------------------------------
-------------------------------------------------------------------
--------------------------------------------------------
---------------------------------------