| Table of Contents |
| --- |
| Chapter | 1: Introduction | 1 |
|  | - |  |
| Chapter | 2 |  |
|  | 2.1 Connectors Jumpers ----------------------------------------- | 3 |
|  | 2.2 Install The System CPU Processor------------------------ | 7 |
|  | 2. 3 Set CPU Voltage------------------------------------------------ | 8 |
|  | 2. 4 Install 586 CPU ---------------------------------------------- | 9 |
|  | 2.4-1 Quick to Setting for BUS Clock 100 MHZ frequency CPU------------------------------------------------- | 9 |
|  | 2.4-2 Quick to Setting for INTEL PENTIUM MMX/AMD K6 MMX/CYRIX M2 MMX CLK &Voltage------------------------------------------------------ | 12 |
|  | 2.4-3 Quick to Setting to INTEL PENTIUM &AMD K5 CPU CLK & Voltage----------------------------------- | 18 |
|  | 2.4-4 Quick to Setting for CYRIX 6X86 CPU CLK& Voltage-------------------------------------------------------- | 20 |
|  | 2.5 PCB Layout and Relevant Positions for CLK & Voltage-------------------------------------------------------- | 21 |
|  | 2.6 CPU Multi Ratio & BUS CLK,AGP CLK &PCI CLK------------------------------------------------------------ | 22 |
|  | 2.7 Support 168 pin DIMMX2 &72 pin SIMMX2 FOR SDRAM/FPM/EDO DRAM------------------------- | 23 |
|  | 2.8 Install DRAM AND SDRAM Memory-------------------- | 25 |
| Chapter | 3 |  |
|  | 3.1 Main Menu -------------------------------------------------- | 26 |
|  | 3.2 Standard CMOS Setup ------------------------------------ | 28 |
|  | 3.3 BIOS Features Setup --------------------------------------- | 32 |
|  | 3.4 Supervisor/User Password Setting ------------------------ | 37 |
|  | 3.5 Setup/Integrated Peripherals Features Setup ------------- | 38 |
|  | 3.6 Setup Power Management ---------------------------------- | 43 |
|  | 3.7 Setup PnP/PCI Configuration ------------------------------ | 47 |

Chapter 1                   INTRODUCTION

This main board is a high performance system hardware based on Intel Pentium processor and is equipped with three master PCI slots, four 16-bit ISA slot, two serial ports with 16550 high speed, one parallel with ECP/EPP bi-direction, one PS/2 Mouse port, one infrared port (IR), dual enhanced PCI IDE ports for 4 IDE device mode 5 and DMA mode 2, one FDD port.  The dimension is 22*25 cm.

Features:

(CPU ZIF Socket

- ZIF 321-pin ZIF socket. Socket 7.

- Intel Pentium 90, 100, 120, 133, 150, 166, 180, and 200MHz.

- Intel Pentium-MMX 166/200/233 MHZ

- Switch Voltage Regulator for P55C

- Cyrix M1 P120+/P133+/P150+/P166+/CYRIX M2(MMX)

- AMD K5 /K6 (MMX) CPU

(Chipset

- Main board: ALI ALADDIN M1543/M1542 CHIPSET

- Host bus at 60,66,75,83,100MHZ

(Memory, SIMM 1-2,DIMMx2

( 	The RAM MODULE assortment is flexible.

( 	There are two 168 pin DIMM sockets and two 72 pin SIMM sockets on the motherboard.

( 	You can use 3.3V SDRAM and 5V EDO RAM on the 168 pin DIMM socket

of the motherboard. The total capacity is up to 256MB.

(	Otherwise, you can use 5V EDO RAM and FPM RAM on the 72 pin SIMM socket of the motherboard. The total capacity is up to 128MB.

- SIMM RAM MODULE and DIMM RAM MODULE, The total capacity is      up to 384MB.

(Pipe Line Cache

- 64 bit Cache.

- Implements level two (L2), external cache write through or write-back design, featuring two pipe line sram on board.

- External cache size is on board 512K Cache RAM.

(Expansion Slots, ISA1-ISA3,PCI1-PCI3, AGP1

- Builds three 16-bit ISA slots and three 32-bit PCI slots (PCI 1 to PCI 3)

- Support one AGP (Accelerated Graphics Port) slot, 66MHZ protocol.

(Enhanced PCI IDE & ISA I/O

- Built in enhanced PCI Local Bus IDE controller.

- Ultra DMA/33 Support BUS master IDE

- Supports 4 PCI IDE devices.  PIO Mode 5 and DMA Mode 2 and CDROM driver.  BIOS auto detects HDD.

- Two serial ports with 16550, Infrared port (IR), one Parallel port with ECP/EPP pocket device, bi-dirction, one PS/2 mouse port, two FDD.  Through ECP/EPP, the board increases the performance of printer or connect SCSI or IDE devices.

- Controlled by BIOS.  Disable I/O function by BIOS in order to Install an I/O card.  Set COM 1 and COM 2 as COM 3 and COM 4 by BIOS.

(System Green BIOS

- Flash BIOS option on board, AWARD deep green BIOS, PLUG & PLAY, PnP function.

- Auto configuration for PCI add-on cards.

(  I/O Device‘s power saving, APM & SMI.

- Implements the EPA Energy Star PC specification with Deep Green system design.

# Full-on	: System runs in full speed CPU clock.

# Doze	: System scales-down CPU clock.

# Standby	: System scales-down the CPU clock, and turns off video display, and spin-off hard disk driver.

# Suspend	: With SMM CPU, stop CPU clock in suspend mode.

(ACPI (ATX Power Supply Mode)

- power management.  Soft-off Control

- Support Modem Ring-in

- RTC Alarm wake up

( Power Connect

- AT/ATX option

  - Connectors & Jumpers

FRONT1:Power LED, Speaker, SLEEP LED, ATX POWER SWITCH, Reset, Hard disk LED, Turbo LED, Turbo Switch.

Speaker            Sleep      Power

LED       LED

|  |  | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 |  |  |  |  |  |  |  |  |

Tubro    Tubro    HDD   ATX

RESET   Switch     LED    LED  POWER

SWITCH

FRONT1(1-3): Power LED

| PINOUT | ASSIGNMENTS |
| --- | --- |
| 1 2 3 | LED OUTPUT NC GND |

FRONT1(4-5): SLEEP LED

| PINOUT | ASSIGNMENTS |
| --- | --- |
| 1 2 | LED OUTPUT HIGH |

FRONT1(6): NOT CONNECT

FRONT1(7-10): Speaker Connect

| PINOUT | ASSIGNMENTS |
| --- | --- |
| 1 2 3 4 | speaker output GND GND VCC |

FRONT1(11-12): ATX POWER Switch Connect

FRONT1(13-14): Hard Disk LED connect

| PINOUT | ASSIGNMENTS |
| --- | --- |
| 1 2 | VCC LED1 Signal |

FRONT1(15-16): Turbo LED connect

| PINOUT | ASSIGNMENTS |
| --- | --- |
| 1 2 | VCC LED1 Signal |

FRONT1(17-18): Turbo switch connect (Default close)

FRONT1(19-20): RESET switch connect

JP1: CPU CLK SELECT.     Please refer section 2-4 relating

JP2: IR connect.

| PINOUT | ASSIGNMENTS |
| --- | --- |
| 1 2 3 4 5 | VCC FIRRX Signal IRRX2 Signal GND IRTX2 Signal |

JP3: COMS CLEAR SETTING

| JP3 | Function |
| --- | --- |
| 1-2 | NORMAL |
| 2-3 | CMOS CLEAR |

JP5: FOR 168 PIN SDRAM (Synchronous DRAM)

OR FPM/EDO DRAM Voltage SELECT

| JP5 | Function |
| --- | --- |
| 1-2,1-2 | +5V EDO/FPM |
| 2-3,2-3 | +3.3V SDRAM |

JP6: FAN +12 POWER

| +12V | GND |
| --- | --- |

JP7: CPU Voltage Jumper setting. Please refer section 2-3 relating.

JP8: Flash ROM VCC Select

| JP8 | Function | REMARK |
| --- | --- | --- |
| 1-2 1-2 | +12V VPP | Reserved |
| 2-3 2-3 | +5V VPP | Factory Default |

MOUSE1: PS/2 MOUSE CONNECT

| PINOUT | ASSIGNMENTS |
| --- | --- |
| 1 2 3 4 5 | MDATA N.C GND VCC MSCLK |

KBCONN1: AT KEYBOARD CONNECT

J1: ATX POWER SUPPLY CONNECT

CN1: AT POWER SUPPLY CONNECT

CN4: Primary IDE CONNECT

CN5: Secondary IDE CONNECT

CN3: Floppy CONNECT

CN2: PRINT CONNECT

COM1: COM1 CONNECT

COM2: COM2 CONNECT

USB-1: USB-1 CONNECT

| PINOUT | ASSIGNMENTS |
| --- | --- |
| 1 3 5 7 9 | VCC USBP0- USBP0+ GND_A GND_B |

USB-2: USB-2 CONNECT

| PINOUT | ASSIGNMENTS |
| --- | --- |
| 2 4 6 8 10 | VCC USBP1- USBP1+ GND_A GND_B |

SIMM 1-2: 72 pin DRAM Module Socket

DIMM 1-2: 168 pin SDRAM Module Socket

U11: LM 75 FOR CPU Temperature detect

U10: CPU ZIF SOCKET 7

2.2 Install The System CPU Processor
Install 586 CPU on the ZIF Socket 7

- Locate the 321-pin ZIF Socket.

- Raise the ZIF Socket retaining arm to the open position.  Pin Coordinates  A-1 will be the arm corner.

- Position the notched corner of microprocessor over the notched corner of the ZIF Socket and align the pins of CPU over the Socket.

- Carefully insert the aligned CPU into the ZIF Socket and press Firmly.  After CPU inserted, press ZIF retaining arm downwards.

- Examine the installed CPU to ensure it is install in the correct direction and pin aligned properly.

JP7:   SET CPU VOLTAGE

| CPU POWER MODE | JP7 | EXAMPLE | CPU POWER MODE | JP7 | EXAMPLE |
| --- | --- | --- | --- | --- | --- |
| ONLY 3.52V |  | AMD-K5 CYRIX M1 | DUAL 2.7V & 3.3V |  | FOR FUTURE CPU |
| ONLY 3.4V |  | FOR FUTURE CPU | DUAL 2.6V & 3.3V |  | FOR FUTURE CPU |
| ONLY 3.3V |  | INTEL PENTIUM | DUAL 2.5V & 3.3V |  | FOR FUTURE CPU |
| DUAL 3.2V & 3.3V |  | AMD K6 PR-233 MHZ | DUAL 2.4V&3.3V |  | AMD K6-3 400/500 |
| DUAL 3.1V & 3.3V |  | FOR FUTURE CPU | DUAL 2.3V & 3.3V |  | FOR FUTURE CPU |
| DUAL 3.0V & 3.3V |  | FOR FUTURE CPU | DUAL 2.2V&3.3V DUAL 2.2V&3.45V |  | AMD-K6 266 /300MHZ |
| DUAL 2.9V & 3.3V |  | IBM 6X86MX AMD -K6 CYRIX M2 | DUAL 2.1V & 3.3V |  | FOR FUTURE CPU |
| DUAL 2.8V & 3.3V |  | IBM 6X86L INTEL PENTIUM MMX | DUAL 2.0V & 3.3V |  | FOR FUTURE CPU |

INSTALL 586 CPU

2.4-1 QUICK TO SETTING FOR BUS CLOCK 100HZ FREQUENCY CPU

A:  AMD-K6-2

(1) CPU CLK

(2) SET CPU Voltage

In case the marking voltage on CPU is not meet up with our manual,

Please setup according to CPU marking, You can reference our manual section 2-3: the jumper setting of CPU Voltage.

For better reliability,we suggest Using PC-100 SDRAM for 100MHZ CPU.

AMD K6-III

- CPU CLK

| PRODUCT NAME | CPU SPEED MHZ | BUS MHZ | JP1 | MULTIPLIER |
| --- | --- | --- | --- | --- |
| AMDK6-III 400 | 400 | 100 |  | 4X |
| AMDK6-III 450 | 450 | 100 |  | 4.5X |
| AMDK6-III 475 | 475 | 95 |  | 5X |
| AMDK6-III 500 | 500 | 100 |  | 5X |

(2)SET CPU VOLTAGE

| CPU POWER TYPE / JUMPER | JP7 |
| --- | --- |
| DUAL 2.4V&3.3V |  |

B: CYRIX-M2

CPU CLK

- SET CPU VOLTAGE

In case the marking voltage on CPU is not meet up with our manual,

Please setup according to CPU marking,

You can reference our manual section 2-3: the jumper setting of CPU Voltage.

For better reliability,we suggest Using PC-100 SDRAM for 100MHZ CPU.

2.4-2 QUICK TO SETTING FOR INTEL PENTIUM MMX /AMD K6 MMX /CYRIX M2 MMX CLK & VOLTAGE

A/ INTEL PENTIUM MMX

- CPU CLK

AMD K6 MMX

(1) CPU CLK

SET CPU VOLTAGE

In case the marking voltage on CPU is not meet up with our manual,

Please setup according to CPU marking,

You can reference our manual section 2-3: the jumper setting of CPU Voltage.

Only use ICS9148B-36 freqency Generator can be support bus CLK 95

MHZ.

For better reliability,we suggest Using PC-100 SDRAM for 100MHZ CPU.

### CYRIX M2 MMX

(1) CPU CLK

- SET CPU VOLTAGE

In case the marking voltage on CPU is not meet up with our manual,

Please setup according to CPU marking,

You can reference our manual section 2-3: the jumper setting of CPU Voltage.

2-4-3 QUICK TO SETTING FOR INTEL PENTIUM & AMD K5 CPU

CLK & VOLTAGE

2.4-4 QUICK TO SETTING FOR CYRIX 6X86 CPU CLK & VOLTAGE

SET CPU VOLTAGE

CYRIX M2 MMX

CPU CLK

Product Name     CPU Speed     BUS CLK      JP1           Multiplier

2.8 Install DRAM AND SDRM Memory

The Board supports different types 72-pin SIMM and DIMM whatever single side or double side. There is no jumper nor connector needed for memory configuration. The RAM MODULE assortments is flexible. There are two 168 pin DIMM sockets and two 72 pin SIMM sockets on the motherboard.

You can use 3.3V SDRAM and 5V EDO RAM on the 168 pin DIMM socket of the motherboard. The total capacity is up to 256MB. Otherwise, you can use 5V EDO RAM and FPM RAM on the 72 pin SIMM socket of the motherboard. The total capacity is up to 128MB. SIMM RAM MODULE and DIMM RAM MODULE, The total capacity is up to 384MB.

It also supports both fast page DRAM or EDO DRAM SIMM, but can’t use them at same bank, i.e. one SIMM is fast page DRAM and the other is EDO SIMM.

SIMM can be use parity (x36) or none parity (x32). The 70ns fast page SIMM or 60ns EDO DRAM needed, at least.

Example:

| BANK 0&1, DIMM | BANK 2&3, DIMM2 | BANK 4&5, SIMM1,2 | TOTAL |
| --- | --- | --- | --- |
| 8MB | NONE | NONE | 8MB |
| NONE | 8MB | NONE | 8MB |
| NONE | NONE | 8MB | 8MB |
| 8MB | 8MB | NONE | 16MB |
| NONE | 8MB | 8MB | 16MB |
| 8MB | NONE | 8MB | 16MB |
| 8MB | 8MB | 8MB | 24MB |
| 16MB | 16MB | NONE | 32MB |
| 32MB | NONE | 32MB | 64MB |
| 32MB | 32MB | NONE | 64MB |
| 64MB | 64MB | NONE | 128MB |
| 128MB | 128MB | NONE | 256MB |
| 128MB | 128MB | 128MB | 384MB |

Chapter 3                             BIOS SETUP

3.1 Main Menu

Once you enter the Award BIOS CMOS Setup Utility, the Main Menu will appear on the screen.  The Main Menu allows you to select from several setup functions and two exit choices.  Use the arrow keys to select among the items and press <Enter> to accept and enter the sub-menu.

ROM PCI/ISA BIOS (2A5KFF9A)

CMOS SETUP UTILITY

AWARD SOFTWARE, INC.

| STANDARD CMOS SETUP BIOS FEATURES SETUP CHIPSET FEATURES SETUP POWER MANAGEMENT SETUP PNP/PCI CONFIGURATION SETUP LOAD BIOS DEFAULTS LOAD SETUP DEFAULTS | INTEGRATED PERIPHERALS SUPERVISOR PASSWORD USER PASSWORD IDE HDD AUTO DETECTION HDD LOW LEVEL FORMAT SAVE & EXIT SETUP EXIT WITHOUT SAVING |
| --- | --- |
| Esc : Quit F10 : Save & Exit Setup | (((( : Select Item (Shift) F2 : Color |
| Time, Date, Hard Disk Type… |

Note that a brief description of each highlighted selection appears at the bottom of the screen.

Setup Items

The main menu includes the following main setup categories.  Recall that some systems may not include all entries.

Standard CMOS Setup

This setup page includes all the items in a standard, AT-compatible BIOS.

BIOS Features

This setup page includes all the items of Award special enhanced features.

Super/User Password Setting

Change, set, or disable password.  It allows you to limit access to the system

and Setup, or just to Setup.

Chipset Features Setup

This setup page includes all the items of chipset special features.

Power Management Setup

This entry only appears if your system supports Power Management, “Green

PC”, standards.

PNP/PCI Configuration Setup

This entry appears if your system supports PNP/PCI.

Load BIOS Defaults

The BIOS defaults have been set by the manufacturer and represent settings which provide the minimum requirements for your system to operate.

Load Setup Defaults

The chipset defaults are settings which provide for maximum system

performance. While Award has designed the custom BIOS to maximize performance, the manufacturer has the right to change these defaults to meet

their needs.

Integrated Peripherals

This section page includes all the items of IDE hard drive and Programmed Input/ Output features.

IDE HDD Auto Detection

Automatically detect and configure hard disk parameters.  The Award BIOS includes this ability in the event you are uncertain of your hard disk’s parameters.

HDD Low Level Format

If supported by your system, this provides a hard disk low level format utility.

Save & Exit Setup

Save CMOS value changes to CMOS and exit setup.

Exit Without Save

Abandon all CMOS value changes and exit setup.

- Standard CMOS Setup

The items in Standard CMOS Setup Menu are divided into 10 categories. Each category includes no, one or more than one setup items. Use the arrow keys to highlight the item and then use the <PgUp> or <PgDn> keys to select the value you want in each item.

ROM PCI/ISA BIOS (2A5KKF9A)

STANDARD CMOS SETUP

AWARD SOFTWARE. INC.

| Date (mm:dd:yy) : Fri, Dec 6 1996 Time (hh:mm:ss) : 15 : 40 : 00 HARD DISKS TYPE SIZE CYLS HEAD PRECOMP LANDE SECTOR MODE |
| --- |
| Primary Master Primary Slave Secondary Master Secondary Slave | : Auto : Auto : Auto : Auto | 0 0 0 0 | 0 0 0 0 | 0 0 0 0 | 0 0 0 0 | 0 0 0 0 | 0 0 0 0 | AUTO AUTO AUTO AUTO |
| Drive A : 1.44M, 3.5in Drive B : None |
| Video Halt On | : EGA/VGA : All ,But Keyboard | Base Memory : 640K Extended Memory : 15360 K Other Memory : 384K Total Memory : 16384K |
| ESC : Quit F1 : Help | (((( : Select Item (Shift) F2 : Change Color | PU/PD/+/- : Modify |

Date

The date format is <day>, <date> <month> <year>.  Press<F3> to show the calendar.

| day | The day, from Sun to Sat, determined by the BIOS and is display-only |
| --- | --- |
| date | The date, from 1 to 31 (or the maximum allowed in the month) |
| month | The month, Jan through Dec. |
| year | The year, from 1900 through 2099 |

Time

The time format is <hour><minute><second>. The time is calculated based on the 24-hour military-time clock.  For example, 1 p.m. is 13:00:00

Daylight saving

The category adds one hour to the clock when daylight-saving time begins.  It also subtracts one hour when standard time returns.

| Enabled | Enabled daylight-saving |
| --- | --- |
| Disabled | Disabled daylight-saving |

Primary Master/ Primary Slave/Secondary Master/

Secondary Slave

The categories identify the types of 2 channels that have been installed in the

computer. There are 45 predefined types and 4 user definable types are for

Enhanced IDE BIOS. Type 1 to Type 45 are predefined. Type user is user-

definable.

Press PgUp or PgDn to select a numbered hard disk type or type the number

and press <Enter>. Note that the specifications of your drive must match with

the drive table. The hard disk will not work properly if you enter improper

information for this category. If your hard disk drive type is not matched or

listed, you can use Type “User” to define your own drive type manually.

If you select Type “User’, you will need to know the information listed

below. Enter the information directly from the keyboard and press <Enter>.

This information should be included in the documentation from your hard

disk vendor or the system manufacturer.

If the controller of HDD interface is ESDI, the selection shall be “Type 1”.

If the controller of HDD interface is SCSI, the selection shall be “None”.

If you select Type “Auto”, BIOS will Auto-Detect the HDD & CD-ROM

Drive at the POST stage and showing the IDE for HDD & CD-ROM Drive.

| TYPE | drive type |
| --- | --- |
| CYLS. | number of cylinders |
| HEADS | number of heads |
| PRECOMP | write precom |
| LANDZONE | landing zone |
| SECTORS | number of sectors |
| MODE | mode type |

If a hard disk has not been installed select NONE and press <Enter>.

Drive A Type/ Drive B Type

The category identifies the types of floppy disk drive A or drive B that have

been installed in the computer.

| None | No floppy drive installed |
| --- | --- |
| 360K, 5.25 in | 5-1/4 inch PC-type standard drive; 360 kilobyte capacity |
| 1.2M, 5.25 in | 5-1/4 inch AT-type high-density drive; 1.2 megabyte capacity |
| 720M, 3.5 in | 3-1/2 inch double-sided drive; 720 kilobyte capacity |
| 1.44M, 3.5 in | 3-1/2 inch double-sided drive; 1.44 megabyte capacity |
| 2.88M, 3.5 in | 3-1/2 inch double-sided drive; 2.88 megabyte capacity |

Video

The category selects the type of video adapter used for the primary system

monitor. Although secondary monitors are supported, you do not have to

select the type in Setup.

| EGA/VGA | Enhanced Graphics Adapter/Video Graphics Array, For EGA, VGA, SEGA, SVGA, or PGA monitor adapters. |
| --- | --- |
| CGA 40 | Color Graphics Adapter, power up in 40 column mode |
| CGA 80 | Color Graphics Adapter, power up in 80 column mode |
| MONO | Monochrome adapter, includes high resolution monochrome adapters |

Error Halt

The category determines whether the computer will stop if an error is

detected during power up.

| No errors | Whenever the BIOS detects a non-fatal error the system will be stopped and you will be prompted. |
| --- | --- |
| All errors | The system boot will not be stopped for any error that may be detected. |
| All, But Keyboard | The system boot will not stop for a keyboard error, it will stop for all other errors. |
| All, But Diskette | The system boot will not stop for a disk error; it will stop for all other errors. |
| All, But Disk/Key | The system boot will not stop for a keyboard or disk error; it will stop for all other errors. |

Memory

The category is display-only which is determined by POST (Power on Self Test)

of the BIOS.

Base Memory

The POST will determine the amount of base (or conventional) memory

installed in the system. The value of the base memory is typically 512K for

systems with 512K memory installed on the motherboard, or 640K for

system with 640K or more memory installed on the motherboard.

Extended Memory

The BIOS determines how much extended memory is present during the

POST. This is the amount of memory located above IMB in the CPU’S

memory address map.

Other Memory

This refers to the memory located in the 640K to 1024K address space. This

is memory that can be used for different applications. DOS uses this area to

load device drivers in an effort to keep as much base memory free for application programs. The BIOS is the most frequent user of this RAM area since this is where it shadows RAM.

3.3 BIOS Features Setup

This section allows you to configure your system for basic operation.  You have the opportunity to select the system‘s default speed, boot-up sequence, keyboard operation, shadowing and security.

ROM PCI/ISA BIOS (2A5KKF9A)

BIOS FEATURES SETUP

AWARD SOFTWARE. INC.

| Virus Warning CPU Internal Cache External Cache Quick Power On Self Test Boot Sequence Swap Floppy Drive Boot Up Floppy Seek Boot Up Numlock Status Boot Up System Speed Gate A20 Option Typematic Rate Setting Typematic Rate (Chars/Sec) Typematic Delay (Msec) | : Disabled : Enabled : Enabled : Enabled : C, A, SCSI : Disabled : Enabled : On : High : Fast : Disabled : 6 : 250 | Video BIOS Shadow C8000-CBFFF Shadow CC000-CFFFF Shadow D0000-D3FFF Shadow D4000-D7FFF Shadow D8000-DBFFF Shadow DC000-DFFFF Shadow | : Enabled : Disabled : Disabled : Disabled : Disabled : Disabled : Disabled |
| --- | --- | --- | --- |
| Security Option PCI/VGA Palett Snoop Assign IRQ For VGA OS Select For DRAM >64MB Report No FDD For WIN 95 | : Setup : Disabled : Enabled : Non-OS2 : No | ESC : Quit F1 : Help F5 : Old Values F6 : Load BIOS Defaults F7 : Load Setup Defaults | (((( : Select Item PU/PD/+/- : Modify (Shift) F2 : Color |

Virus Warning

When this item is enabled, the Award BIOS will monitor the boot sector and partition table of the hard disk drive for any attempt at modification.  If an attempt is made, the BIOS will halt the system and the following error message will appear.  Afterwards, if necessary, you will be able to run an antivirus program to locate and remove the problem before any damage is done.

!WARNING!

Disk boot sector is to be modified

Type “Y” to accept write or “N” to abort write

Award Software, Inc.

| Enabled | Activates automatically when the system boots up causing a warning message to appear when anything attempts to access the boot sector or hard disk partition table. |
| --- | --- |
| Disabled | No warning message will appear when anything attempts to access the boot sector or hard disk partition table. |

NOTE:

Many disk diagnostic programs which attempt to access the boot sector table can cause the above warning message. If you will be running such a program, we recommend that you first disable Virus Protection before band.

CPU Internal Cache/External Cache

These two categories speed up memory access. However, it depends on CPU/chipset design. The default value is enable.

| Enabled | Enabled cache |
| --- | --- |
| Disabled | Disable cache |

Quick Power On Self Test

This category speeds up Power On Self Test (POST) after you power up the

computer. If it is set to Enable, BIOS will shorten or skip some check items

during POST.

| Enabled | Enable quick POST |
| --- | --- |
| Disabled | Normal POST |

Boot Sequence

The category determines which drive to search first for the disk operating system (i.e., DOS). Default value is A, C.

| C,A | System will first search for hard disk drive then floppy disk drive. |
| --- | --- |
| A,C | System will first search for floppy disk drive then hard disk drive. |
| CDROM, C,A | System will first search for CDROM drive, then hard disk drive and then floppy disk drive. |
| C, CDROM, A | System will first search for hard disk drive, then CDROM drive, and then floppy disk drive. |

Swap Floppy Drive

This item allows you to determine whether enable the swap floppy drive or not.

The choice: Enabled/Disabled.

Boot Up Floppy Seek

During POST, BIOS will determine if the floppy disk drive installed is 40 or

80tracks. 360K type is 40 tracks while 760K, 1.2M and 1.44M are all 80 tracks.

| Enabled | BIOS searches for floppy disk drive to determine if it is 40 or 80 tracks. Note that BIOS can not tell from 720K, 1.2M or 1.44M drive type as they are all 80 tracks. |
| --- | --- |
| Disabled | BIOS will not search for the type of floppy disk drive by track number. Note that there will not be any warning message if the drive installed is 360K. |

Boot Up NumLock Status

This allows you to determine the default state of the numeric keypad. By default, the system boots up with NumLock on.

| On | Keypad is number keys |
| --- | --- |
| Off | Keypad is arrow keys |

Boot Up System Speed

Selects the default system speed- the normal operating speed at power up.

| High | Set the speed to high |
| --- | --- |
| Low | Set the speed to low |

Gate A20 Option

This entry allows you to select how the gate A20 is handled. The gate A20 is a device used to address memory above 1 Mbytes. Initially, the gate A20 was handled via a pin on the keyboard. Today, while keyboards still provide this support, it is more common, and much faster, for the system chipset to provide support for gate A20.

| Normal | keyboard |
| --- | --- |
| Fast | chipset |

Typematic Rate Setting

This determines if the typematic rate is to be used. When disabled, continually holding down a key on your keyboard will generate only one instance. In other words, the BIOS will only report that the key is down.

When the typematic rate is enabled, the BIOS will report as before, but it will then wait a moment, and , if the key is still down, it will begin the report that the key has been depressed repeatedly. For example, you would use such a feature to accelerate cursor movements with the arrow keys.

| Enabled | Enabled typematic rate |
| --- | --- |
| Disabled | Disable typematic rate |

Typematic Rate (Chars/Sec)

When the typematic rate is enabled, this selection allows you select the rate at which the keys are accelerated.

| 6 | 6 characters per second |
| --- | --- |
| 8 | 8 characters per second |
| 10 | 10 characters per second |
| 12 | 12 characters per second |
| 15 | 15 characters per second |
| 20 | 20 characters per second |
| 24 | 24 characters per second |
| 30 | 30 characters per second |

Typematic Delay (Msec)

When the typematic rate is enabled, this selection allows you to select the delay between when the key was first depressed and when the acceleration begins.

| 250 | 250 msec |
| --- | --- |
| 500 | 500 msec |
| 750 | 750 msec |
| 1000 | 1000 msec |

Security Option

This category allows you to limit access to the system and Setup, or just to Setup.

| System | The system will not boot and access to Setup will be denied if the correct password is not entered at the prompt. |
| --- | --- |
| Setup | The system will boot, but access to Setup will be denied if the correct password is not entered at the prompt. |

Note: To disable security, select PASSWORD SETTING at Main Menu and then you will be asked to enter password. Do not type anything and just press <Enter>, it will disable security. Once the security is disabled, the system will boot and you can enter Setup freely.

OS Select for DRAM > 64

This item allows you to access the memory that over 64MB in OS/2.

The choice: Non-OS2, OS2.

PCI/ VGA Palette Snoop

It determines whether the MPEG ISA/VESA VGA Cards can work with PCI/VGA or not.

| Enabled | When PCI/VGA working with MPEG ISA/VESA VGA Card. |
| --- | --- |
| Disabled | When PCI/VGA not working with MPEG ISA/VESA VGA Card. |

Video BIOS Shadow

Determines whether video BIOS will be copied to RAM. However, it is optional depending on chipset design. Video Shadow will increase the video speed.

| Enabled | Video shadow is enabled |
| --- | --- |
| Disabled | Video shadow is disabled |

C8000-CBFFF Shadow/DC000-DFFFF Shadow

These categories determine whether option ROMs will be copied to RAM.

An example of such option ROM would be support of on-board SCSI.

| Enabled | Optional shadow is enabled |
| --- | --- |
| Disabled | Optional shadow is Disabled |

- Supervisor/User Password Setting

You can set either supervisor or user password, or both of them. The differences between them are:

supervisor password: can enter and change the options of the setup menus.

user password: just can enter but do not have the right to change the options of the setup menus.

When you select this function, the following message will appear at the center of the screen to assist you in creating a password.

ENTER PASSWORD:

Type the password, up to eight characters in length, and press <Enter>. The password typed now will clear any previously entered password from CMOS memory. You will be asked to confirm the password. Type the password again and press <Enter>. You may also press <Esc> to abort the selection and not enter a password.

To disable a password, just press <Enter> when you are prompted to enter the password. A message will confirm the password will be disabled. Once the password is disabled, the system will boot and you can enter Setup freely.

PASSWORD DISABLED.

When a password has been enabled, you will be prompted to enter it every time

you try to enter Setup. This prevents an unauthorized person from changing any part of your system configuration.

Additionally, when a password is enabled, you can also require the BIOS to request a password every time your system is rebooted. This would prevent unauthorized use of your computer.

You determine when the password is required within the BIOS Features Setup Menu and its Security option (see Section 4). If the Security option is set to “System”, the password will be required both at boot and at entry to Setup. If set to “Setup”, prompting only occurs when trying to enter Setup.]

3.5 Setup/Integrated Peripherals Features Setup

ROM PCI/ISA BIOS (2A5KKF9A)

CHIPSET FEATURES SETUP

AWARD SOFTWARE. INC.

| Auto Configuration L2 TAG RAM Size AT Bus Clock DRAM Timing SDRAM CAS Latency Pipelined Function Graphics Aperture Size SDRAM Burst X-1-1-1-1-1-1-1 DRAM Data Integrity Mode Memory Hole At 15-16M Host Read DRAM Command AGP Read Burst ISA Line Buffer Passive Release Delay Transaction Primary Frame Buffer VGA Frame buffer Data Merge IO Recovery Period | : Enabled : 8 : CLK2/4 : Normal : 3 : Enabled : 64MB : Disabled : Disabled : Disabled : Bypass : Enabled : Enabled : Disabled : Disabled : Disabled : Disabled : Disabled : 2US | CPU Warning Temperature : 60(C/133(F Current CPU Temperature : 51(C/123(F Shutdown Temperature : 75(C/167(F |
| --- | --- | --- |
|  |  | Quit F1 : Help F5 : Old Values F6 : Load BIOS Defaults F7 : Load Setup Defaults | ((((:Select It PU/PD/+/- : Modify (Shift) F2 : Color |

This section allows you to configure the system based on the specific features of the installed chipset.  This chipset manages bus speeds and access to system memory resources, such as DRAM and the external cache.  It also coordinates communications between the conventional ISA bus and the PCI bus. It must be stated that these items should never need to be altered. The default settings have been chosen because they provide the best operating conditions for your system. The only time you might consider making any changes would be if you discovered that data was being lost while using your system.

DRAM Settings

The first chipset settings deal with CPU access to dynamic random access memory (DRAM).

Auto Configuration

Pre-defined values for DRAM, cache.. Timing according to CPU type & system clock.

The Choice: Enabled, Disabled.

Note: When this item is enabled, the pre-defined items will become

SHOW-ONLY.

AT Bus Clock

this item allows you to select 7.16MHZ, CLK2/2, CLK2/3, CLK2/4, CLK2/5,

CLK2/6, clocks.  The default is clk2/4.

Asysc. SRAM Read/Write WS

This item allows you to select x-3-3-3, x-2-2-2.  The default is x-3-3-3.

EDO Read WS

This item allows you to select x-3-3-3, x-2-2-2 .  The default is x-3-3-3.

Page Mode Read WS

This item allows you to select x-3-3-3, x-4-4-4 .  The default is x-3-3-3.

DRAM Write WS

This item allows you to select x-3-3-3, x-2-2-2 .  The default is x-2-2-2.

CPU to DRAM Page Mode

The default is Disabled.

DRAM Refresh Period

This item allows you to select 15us, 30us, 60us, 120us.  The default is 60us.

DRAM Date Integrity Mode

This item allows you to select between two methods of DRAM error checking, ECC and Parity.  The default is Parity.

Pipelined Function

This item allows you to select Disabled, Enabled, Turbo.  The default is Disabled.

16 Bit ISA I/O, Mem Command WS

This item allows you to select Normal, 1 to 3 Wait .  The default is 2 Wait.

Local Memory 15-16M

This item allows you to select Disabled, Enabled .  The default is Enabled.

Passive Release

This item allows you to select Disabled, Enabled .  The default is Enabled.

ISA Line Buffer

This item allows you to select Disabled, Enabled .  The default is Enabled.

Delay Transaction

This item allows you to select Disabled, Enabled .  The default is Enabled.

Primary Frame Buffer

This item allows you to select Disabled. 1,2,4,8,16MB.  The default is 2MB.

VGA Frame Buffer

This item allows you to select Disabled, Enabled.  The default is Enabled.

Linear Merge

This item allows you to select Disabled, Enabled.  The default is Enabled.

Word Merge

This item allows you to select Disabled, Enabled.  The default is Enabled.

Byte Merge

This item allows you to select Disabled, Enabled.  The default is Disabled.

Fast Back-to-Back

The default is Disabled.

PCI Write Burst

This item allows you to select Disabled, Enabled.  The default is Disabled

M1 Linear Burst Mode

This item allows you to select Disabled, Enabled.  The default is Disabled.

Integrated Peripherals

ROM PCI/ISA BIOS (2A5KKF9A)

INTEGRATED PERIPHERALS

AWARD SOFTWARE. INC.

| On-Chip Primary IDE Master PIO Slave PIO Master Ultra DMA Slave Ultra DMA On-Chip Secondary IDE Master PIO Slave PIO Master Ultra DMA Slave Ultra DMA IDE HDD Block Mode On-Chip USB Controller | : Enabled : Auto : Auto : Auto : Auto : Enabled : Auto : Auto : Auto : Auto : Enabled : Disabled | Onboard FDC Controller : Enabled Onboard Serial Port 1 : Auto UR1 Mode : Normal Onboard Serial Port 2 : Auto UR2 Mode : Normal Onboard Parallel Port : 378/IRQ7 Parallel Port Mode : SPP |
| --- | --- | --- |
| Init AGP Display First Ring In Controller RTC Alarm Controller | : PCI Slot : Disabled : Disabled | ESC : Quit F1 : Help F5 : Old Values F6 : Load BIOS Defaults F7 : Load Setup Defaults | (((( : Select Item PU/PD/+/- : Modify (Shift) F2 : Color |

IDE HDD Block Mode

This allows your hard disk controller to use the fast block mode to transfer

data to and from your hard disk drive (HDD).

| Enabled | IDE controller uses block mode. |
| --- | --- |
| Disabled | IDE controller uses standard mode. |

Enabled is the default.

PCI Slot IDE 2nd Channel

This item allows you designate an IDE controller board inserted into one of

the physical PCI slots as your secondary IDE controller.

| Enabled | External IDE controller designated as the secondary controller |
| --- | --- |
| Disabled | No IDE controller occupying a PCI slot. |

Enabled is the default.

IDE PIO

IDE hard drive controllers can support up to two separate hard disk drivers.

These drives have a master / slave relationship which are determined by the cabling configuration used to attach them to the controller. Your system

supports two IDE controllers-a primary and a secondary-so you have to

ability to install up to four separate hard disks.

PIO means Programmed Input / Output. Rather than have the BIOS issue a

series of commands to effect a transfer to or from the disk drive, PIO allows

the BIOS to tell the controller what it wants and then let the controller and

the CPU perform the complete task by themselves. This simpler and more efficient (and faster).

Your system supports five modes, numbered from 0 (default) to 4, which

primarily differ in timing. When Auto is selected, the BIOS will select the

best available mode. This is true for the next four setup items.

- IDE Primary Master PIO

- IDE Primary Slave PIO

- IDE Secondary Master PIO

- IDE Secondary Slave PIO

On-Chip Primary PCI IDE

As stated above, your system includes two built-in IDE controllers, both of which operate on the PCI bus. This setup item allows you either to enable or disable the primary controller. You might choose to disable the controller if you were to add a higher performance or specialized controller.

| Enabled | Primary HDD controller used-Default |
| --- | --- |
| Disabled | Primary HDD controller not used. |

On-Chip Secondary PCI IDE

As above for the Primary controller, this setup item you either to enable or disable the secondary controller. You might choose to disable the controller if you were to add a higher performance or specialized controller.

| Enabled | Primary HDD controller used |
| --- | --- |
| Disabled | Primary HDD controller not used. |

Enabled is the default

3.6 Setup Power Management

The Power Management Setup allows you to configure your system to most effectively save energy while operating in a manner consistent with your own style of computer use.

ROM PCI/ISA BIOS (2A5KKF9A)

POWER MANAGEMENT SETUP

AWARD SOFTWARE. INC.

| ACPI Function Power Management PM Control by APM MODEM Use IRQ Video Off Option Video Off Method ** PM Monitor HDD Power Down Doze Mode Standby Mode Suspend Mode Throttle Duty Cycle ** PM Events Bus Master | : Enabled : User Define : Yes : 3 : Susp, Stby (( Off : DPMS Support ** : Disabled : Disabled : Disabled : Disabled : 62.5% -75( ** : Disabled | ** External Power Button DOCK I/O SMI AC Power SMI Thermal SMI | Switch ** : Power Off ; Disabled : Disabled : Disabled |
| --- | --- | --- | --- |
| Primary HDD Floppy COM Ports Keyboard LPT Ports | : Disabled : Disabled : Enabled : Enabled : Disabled | ESC : Quit F1 : Help F5 : Old Values F6 : Load BIOS Defaults F7 : Load Setup Defaults | ((((: Select Item PU/PD/+/- : Modify (Shift) F2 : Color |

Power Management

This category allows you to select the type (or degree) of power saving and is directly related to the following modes:

- Doze Mode

- Standby Mode

- Suspend Mode

- HDD Power Down

There are four selections for Power Management, three of which have fixed mode settings.

| Disable (default) | No power management. Disables all four modes |
| --- | --- |
| Min. Power Saving | Minimum power management. Doze Mode = 1hr. Standby Mode = 1 hr., Suspend Mode = 1 hr., and HDD Power Down = 15 min. |
| Max. Power Saving | Maximum power management -ONLY AVAILABLE FOR SL CPU’S. Doze Mode = 1 min., Standby Mode = 1 min., Suspend Mode = 1 min., and HDD Power Down = 1 min. |
| User Defined | Allows you to set each mode individually. When not disabled, each of the ranges are from 1 min. to 1 from 1 min. to 15 min. and disable. |

PM Control APM

When enabled, an Advanced Power Management device will be activated to enhance the Max. Power Saving mode and stop the CPU internal clock.

If the Max. Power Saving is not enabled, this will be preset to No.

Video Off Method

This determines the manner in which the monitor is blanked.

| V/H SYNC+Blank | This selection will cause the system to turn off the vertical and horizontal synchronization ports and write blanks to the video buffer. |
| --- | --- |
| Blank Screen | This option only writes blanks to the video buffer. |
| DPMS | Initial display power management signaling. |

PM Timers

The following four modes are Green PC power saving functions which are only user configurable when User Defined Power Management has been selected. See above for available selections.

Doze Mode

When enabled and after the set time of system inactivity, the CPU clock will run at slower speed while all other devices still operate at full speed.

Standby Mode

When enabled and after the set time of system inactivity, the fixed disk drive and the video would be shut off while all other devices still operate at full speed.

Suspend Mode

When enabled and after the set time of system inactivity, all devices except the CPU will be shut off.

HDD Power Down

When enabled and after the set time of system inactivity, the hard disk drive will be powered down while all other devices remain active.

Power Down & Resume Events

Power Down and Resume events are I/O events whose occurrence can prevent the system from entering a power saving mode or can awake the system from such a mode. In effect, the system remains alert for anything which occurs to a device which is configured a On, even when the system is in a power down mode.

As above, the choices are On and Off. Off is the default.

When set On, activity will neither prevent the system from going into a power management mode nor awake it.

( IRQ3 (COM2)

( IRQ4 (COM1)

( IRQ5 (LPT2)

( IRQ6 (Floppy Disk)

( IRQ7 (LPT1)

( IRQ8 (RTC Alarm)

( IRQ9 (IRQ2 Redir)

( IRQ10 (Reserved)

( IRQ11 (Reserved)

( IRQ12 (Reserved)

( IRQ13 (Coprocessor)

( IRQ14 (Hard Disk)

( IRQ15 (Reserved)

Soft-off By PWR-BTTN  (For ATX POWER ONLY)

This item allows you to select Delay 4 sec or Instant-off.

Resume By Ring  (For ATX POWER ONLY)

This item allows you to select Disabled ,Enabled.

If a Fax Modem was connected with serial ports,

the computer will be awoke when it received a signal from outside.

Resume By Ring, Setup for MS-DOS mode

- Select Resume By Ring: Enabled

- Save the Value and Exit. This system will Reboot.

- Power off your system by pressing the power button on the panel.

Resume By Ring, Setup for WIN95 mode

- Select Resume By Ring: Enabled

- Save the Value and Exit. This system will Reboot.

- When you want leave WIN95 , select Shut down. The powor off by software

Resume By Alarm (For ATX POWER ONLY)

This item allows you to select Disabled ,Enabled.

Which allows the user setting date(Day/Hour/Minute)

in advance for turning on the system with a range in 30 days.

The system will be awoke on the date according to the user’ setup.

Resume By Alarm Setup for MS-DOS mode

- Select Resume By Alarm: Enabled

- Set the (Day/Hour/Minute) you desire to wake up your system

- Save the Value and Exit. This system will Reboot.

- Power off your system by pressing the power button on the panel.

Resume By Alarm Setup for win95 mode

- Select Resume By Alarm: Enabled

- Set the (Day/Hour/Minute) you desire to wake up your system

- Save the Value and Exit. This system will Reboot.

- When you want leave WIN95 , select Shut down. The power off by software

.7 Setup PnP/PCI Configuration

This section describes configuring the PCI bus system.PCI, or Personal Computer Interconnect, is a system which allows I/O devices to operate at speeds nearing the speed the CPU itself uses when communicating with its own special components.  This section covers some very technical items and it is strongly recommended that only experienced users should make any changes to the default settings.

ROM PCI/ISA BIOS (2A5KKF9A)

PNP/PCI CONFIUGURATION

AWARD SOFTWARE. INC.

| PNP OS Installed Resources Controlled by Resources Configuration Data | : No : Manual : Disabled | PCI IDE 2 nd Channel PCI IRQ Actived By PCI IDE IRQ Map To | : Disabled : Level : ISA |
| --- | --- | --- | --- |
| IRQ-3 assigned to IRQ-4 assigned to IRQ-5 assigned to IRQ-7 assigned to IRQ-9 assigned to IRQ-10 assigned to IRQ-11 assigned to IRQ-12 assigned to IRQ-14 assigned to IRQ-15 assigned to | : Legacy ISA : Legacy ISA : PCI/ISA PnP : Legacy ISA : PCI/ISA PnP : PCI/ISA PnP : PCI/ISA PnP : PCI/ISA PnP : Legacy ISA : Legacy ISA |  |  |
| DMA-0 assigned to DMA-3 assigned to DMA-5 assigned to DMA-6 assigned to DMA-7 assigned to | : PCI/ISA PnP : PCI/ISA PnP : PCI/ISA PnP : PCI/ISA PnP : PCI/ISA PnP | ESC : Quit F1 : Help F5 : Old Values F6 : Load BIOS Defaults F7 : Load Setup Defaults | (((( : Select Item PU/PD/+/- : Modify (Shift) F2 : Color |

Resource Controlled by

The Award Plug and Play BIOS has the capacity to automatically configure

all of the boot and Plug and Play compatible devices.  However, this capability means absolutely nothing unless you are using a Plug and Play Operating system such as Windows( 95.

Choices are Auto and Manual (default).

Reset Configuration Data

This item allows you to determine reset the configuration data or not.

Choices are Enabled and Disabled (default).

IRQ3/4/5/7/9/10/11/12/14/15, DMA0/1/3/5/6/7 assigned to

This item allows you to determine the IRQ / DMA assigned to the ISA bus and is not available to any PCI slot.

Choices are Legacy ISA and PCI/ISA PnP.

PCI IRQ Activated by

This sets the method by which the PCI bus recognizes that an IRQ service is being requested by a device. Under all circumstances, you should retain the default configuration unless advised otherwise by your system’s manufacturer.

Choices are Level (default) and Edge.

PCI IDE IRQ MAP to

This allows you to configure your system to the type of IDE disk controller in use. By default, Setup assumes that your controller is an ISA (Industry Standard Architecture) device rather than a PCI controller. The more apparent difference is the type of slot being used.

If you have equipped your system with a PCI controller, changing this allows you to specify which slot has the controller and which PCI interrupt (A, B, C or D) is associated with the connected hard drives.

Remember that this setting refers to the hard disk drive itself, rather than individual partitions. Since each IDE controller supports two separate hard disk drivers, you can select the INT# for each. Again, you will note that the primary has a lower interrupt than the secondary as described in “Slot x Using INT#” above.

Selecting 1allows the system to automatically determine how your IDE disk system is configured.

The default timings have been carefully chosen and should only be altered if data is being lost. Such a scenario might well occur if your system had mixed speed DRAM chips installed so that greater delays may be required to preserve the integrity of the data held in the slower memory chips.

# Text boxes

# 4.5X

12

11

10

9

8

# 4X

12

11

10

9

8

7

6

5

4

3

2

1

# Product Name

# CPU Speed

(MHZ)

BUS CLK    (MHZ)

JP1

# Multiplier

AMD-K6-   PR200

200(MHZ)

100

6

7

8

12

100

10

9

4

11

3

5

1

2

2X

400

AMD-K6-PR400

# 3.5X

10

11

12

9

AMD-K6-PR250

8

7

6

5

4

3

2

1

100

350

AMD-K6-PR350

# 3X

12

11

10

9

8

7

6

5

4

3

2

1

100

300

AMD-K6-PR300

2.5X

12

11

10

9

8

7

6

5

4

3

2

1

100

250

7

10

8

11

9

12

# 5X

10

9

8

12

7

6

9

Product Name

CPU Speed

BUS

JP1

Multiplier

Cyrix-M2-PR233

200

100

5

4

2X

8

7

6

11

2.5X

100

250

5

4

3

2

CYRIX-M2-PR333

12

11

10

1

PENTIUM MMX-166

166

66

1

2

3

4

5

6

7

8

9

10

11

12

2.5x

PENTIUM-MMX-200

200

66

1

2

3

4

5

6

7

8

9

10

11

12

3X

PENTIUM-MMX- 233

233

66

1

2

3

4

5

6

7

8

9

10

11

12

3.5X

CPU POWER TYPE/JUMPER

JP7

DUAL 2.8V & 3.3V

1

2

3

4

5

6

7

8

3.5X

12

11

10

9

8

7

6

5

4

3

2

1

66

233

AMD K6- 233

3X

12

11

10

9

8

7

6

5

4

3

2

1

66

200

AMD K6-200

2.5X

12

11

10

9

8

7

6

5

4

3

2

1

66

166

AMD K6-166

2.5X

11

10

5

12

4

7

3

5

2

3

1

1

11

# 5.5X

11

12

12

11

9

9

8

7

6

5

7

3

10

1

12

10

9

3.5X

12

11

10

9

8

7

6

5

4

3

2

1

95

333

AMD K6- 333

5X

12

11

10

9

8

7

6

5

4

3

2

1

66

333

AMD K6-333

CPU TYPE

CPU POWER

TYPE /JUMPER

JP7

AMD-K6-166/200

DUAL 2.9V & 3.3V

1

2

3

4

5

6

7

8

AMD-K6-233 /266

DUAL 3.2V & 3.3V

1

2

3

4

5

6

7

8

AMD-K6-266/300

AMD-K6-333

DUAL 2.2V &3.3V

DUAL 2.2V &3.45V

1

2

3

4

5

6

7

8

2X

12

11

10

9

8

7

6

5

4

3

2

1

60

120

PENTIUM-120

AMD K5-PR150

1.5X

12

11

10

9

8

7

6

5

4

3

2

1

66

100

PENTIUM-100

AMD K5-PR100

AMD K5-PR133

1.5x

12

11

10

9

8

7

6

5

4

3

2

1

60

90

PENTIUM -90

AMD K5-PR90

AMD K5-PR120

2.5X

12

11

10

9

8

7

6

5

4

3

2

1

66

166

PENTIUM-166

AMD K5-PR166

2.5X

12

11

10

9

8

7

6

5

4

3

2

1

60

150

PENTIUM-150

2x

12

11

10

9

8

7

6

5

4

3

2

1

66

133

PENTIUM -133

2X

12

11

10

7

8

5

6

3

4

1

2

ONLY 3.52V

AMD-K5

PR90-PR166

7

8

5

6

3

4

1

2

ONLY 3.3V

PENTIUM

90-200

3X

12

11

10

9

8

7

6

5

4

3

2

1

11

200

PENTIUM-200

3X

12

11

10

9

8

7

6

5

4

3

2

1

60

180

PENTIUM -180

9

8

7

6

5

4

3

2

1

75

150

6X86-P200-GP

2X

12

11

10

9

8

7

6

5

4

3

2

1

66

133

6X86-P166-GP

2X

12

11

10

9

8

7

6

5

4

3

2

1

60

120

6X86-P150-GP

66

7

8

8

5

6

3

4

1

2

ONLY 2.8V &3.3V

1

2

7

8

5

6

3

4

#### SET CPU VOLTAGE

ONLY 3.3V

ONLY 3.52V

3

4

5

6

7

8

4.5X

12

11

10

9

8

7

6

5

4

3

2

1

66

300

AMD K6- 300

4X

12

11

10

9

8

7

6

5

4

3

2

1

66

266

AMD K6-266

9

8

7

6

5

4

3

2

1

66

166

CYRIX-M2-PR200

2X

12

11

10

9

8

7

6

5

4

3

2

1

66

133

CYRIX-M2-PR166

2.5x

12

11

10

9

8

7

6

5

4

3

2

1

60

150(MHZ)

CYRIX-M2-PR166

2X

12

11

10

9

8

7

6

5

4

3

2

1

83

166

CYRIX-M2-PR233

2.5X

12

11

10

9

8

7

6

5

4

3

2

1

75

188

CYRIX-M2-PR233

2x

12

11

10

9

8

7

6

5

4

3

2

1

75

150

CYRIX-M2-PR200

3X

12

11

10

9

8

7

6

5

4

3

2

1

75

225

CYRIX-M2-PR300

3.5X

12

11

10

9

8

7

6

5

4

3

2

1

66

233

CYRIX-M2-PR300

2.5x

12

11

10

9

8

7

6

5

4

3

2

1

83

208

CYRIX-M2-PR266

3.5X

12

11

10

9

8

7

6

5

4

3

2

1

83

291

CYRIX-M2-PR350

3.5X

12

11

10

9

8

7

6

5

4

3

2

1

75

263

CYRIX-M2-PR333

3x

12

11

10

9

8

7

6

5

4

3

2

1

83

250

CYRIX-M2-PR333

4X

12

11

10

9

8

7

6

5

4

3

2

1

75

300

CYRIX-M2-PR350

7

8

5

6

3

4

1

2

DUAL 2.9V & 3.3V

JP7

CPU POWER TYPE/JUMPER

CPU TYPE

IBM-6X86MXPR166/PR200/PR233

PR266

PR300/PR333

1

2

Multiplier

JP1

BUS CLK

CPU Speed

Product Name

7

6

5

4

3

2

1

100

450

AMD-K6-PR450

6

5

4

3

2

1

100

500

AMD-K6-

PR500

CPU POWER

TYPE/JUMPER

JP7

DUAL 2.2V & 3.3V

OR

DUAL 2.2V & 3.45V

1

2

3

4

5

6

7

8

3

2

1

CYRIX-M2-PR350

300

100

3X

1

2

3

4

5

6

7

8

9

10

11

12

CPU POWER

TYPE/JUMPER

# DUAL 2.9V & 3.3V

JP7

1

2

3

4

5

6

7

8

Product Name

CPU Speed

BUS CLK

JP1

Multiplier

Product Name

CPU Speed

BUS CLK

JP1

Multiplier

11

10

9

8

7

6

5

4

3

2

1

2.5X

66

166

CYRIX-M2-PR200

2X

66

133

CYRIX-M2-PR166

12

11

10

9

8

7

6

5

4

3

2

1

2.5X

60

150

Cyrix-M2-PR166

Multiplier

JP1

BUS CLK

(MHZ)

CPU Speed

(MHZ)

Product Name

CPU Power

Type/Jumper

12

# Multiplier

JP1

# BUS CLK

# CPU Speed

# Product Name

# Multiplier

JP1

# BUS CLK

# CPU Speed

# Product Name

# Multiplier

JP1

# BUS CLK

# CPU Speed

# Product Name

# Multiplier

JP1

# BUS CLK

# CPU Speed

# Product Name

# Multiplier

JP1

# BUS CLK

# CPU Speed

# Product Name

# Multiplier

JP1

# BUS CLK

# CPU Speed

# Product Name

# Multiplier

JP1

# BUS CLK

# CPU Speed

# Product Name

# Multiplier

JP1

# BUS CLK

# CPU Speed

# Product Name

# Multiplier

JP1

# BUS CLK

# CPU Speed

# Product Name

# Multiplier

JP1

# BUS CLK

# CPU Speed

# Product Name

JP7

12

11

10

9

8

7

6

5

4

3

2

1

12

11

10

9

8

7

6

5

4

3

2

1

2X

83

166

CYRIX-M2-PR233

2.5X

75

188

CYRIX-M2-PR233

12

11

10

9

8

7

6

5

4

3

2

1

2X

75

150

Cyrix-M2-PR200

Multiplier

JP1

BUS CLK

(MHZ)

CPU Speed

(MHZ)

Product Name

6

5

4

3

2

1

12

11

10

9

8

7

6

5

4

3

2

1

12

11

10

9

8

7

6

5

4

3

2

1

3X

75

225

CYRIX-M2-PR300

3.5X

66

233

CYRIX-M2-PR300

12

11

10

9

8

7

6

5

4

3

2

1

2.5X

83

208

Cyrix-M2-PR266

Multiplier

JP1

BUS CLK

(MHZ)

CPU Speed

(MHZ)

Product Name

12

11

10

9

8

7

6

5

4

3

2

1

12

11

10

9

8

7

6

5

4

3

2

1

3.5X

83

291

CYRIX-M2-PR350

3.5X

75

263

CYRIX-M2-PR333

12

11

10

9

8

7

6

5

4

3

2

1

3X

83

250

Cyrix-M2-PR333

Multiplier

JP1

BUS CLK

CPU Speed

Product Name

12

11

10

9

8

7

6

5

4

3

2

1

4X

75

300

CYRIX-M2-PR350

CPU TYPE

CPU Power

Type/Jumper

JP7

IBM-6X86MX

/PR166/PR200

/PR233/PR266

/PR300/PR333

# DUAL 2.9V & 3.3V

1

2

3

4

5

6

7

8

# Multiplier

JP1

# BUS CLK

# CPU Speed

# Product Name

# Multiplier

JP1

BUS CLK

(MHZ)

# CPU Speed

(MHZ)

# Product Name

# Multiplier

JP1

# BUS CLK

(MHZ)

# CPU Speed

# Product Name

8

7

6

5

4

3

2

1

100

550

AMD-K6-

PR550

4X

12

11

10

9

8

7

6

5

4

3

2

1

95

380

AMD K6- 380

5.5X

12

11

10

9

8

7

6

5

4

3

2

1

66

366

AMD K6-366