M537D Mainboard Component Locations

IO

Chips

VX PRO+

82C371

VX PRO+

82C371

DIMM Socket

DIMM Socket

VX PRO+

82C437

VX PRO+

82C437

VX PRO

82C438

VX PRO

82C438

VX PRO

82C438

VX PRO

82C438

12888B

12888B

512K Pipeline Cache

512K Pipeline Cache

PRN 1

PRN 1

PS1

PS1

SIM1  SIM2  SIM3  SIM4

SIMM 
Socket

COM1

COM1

USB

USB

COM2

COM2

Power
Connector

Power
Connector

ISA SLOT

ISA SLOT

PCI SLOT

PCI SLOT

IDE2    IDE1    FDC

IDE2    IDE1    FDC

1

JP1

1

JP1

1

JP2

1

JP2

DIMM1 DIMM2

DIMM1 DIMM2

1

JP4

1

JP4

Key Lock

Key Lock

JP3

A   B   C   D

JP3

A   B   C   D

JP51

JP51

JP9

JP9

SPK

SPK

A  B C  D

JP6

A  B C  D

JP6

K/B BIOS

K/B BIOS

RST

RST

TB-SW

TB-SW

TB-LED

TB-LED

HDD-LED

HDD-LED

Quick Installation Guide

1.	Set JP1 to CMOS RAM discharge jumper (pin 1-2).

2.	Set JP3 to select CPU speed & JP9 to select CPU type.

3.	Set JP5 to select CPU Internal Clock Speed.

4.	Set JP6-A, B, C, D to select CPU Voltage Regulator Output.

5.	Insert CPU to CPU socket.

6.	Insert 72-pin SIMM module into SIMM1-4 and / or insert 168-pin DIMM modules into DIMM1-2.  Notice that DIMM2 and SIMM1,2 cannot be installed at the same time.

7.	Install mainboard into system chassis.

8.	Connect keyboard to J1.

9.	Install the display card and other peripheral cards (if required) on to the mainboard.

10.	Connect hard disk(s) to IDE primary/secondary connection(s).

11.	Connect floppy drives(s) to FDC1 connector.

12.	Connect serial ports to COM1 and COM2 connectors

13.	Connect parallel port to PRM1 connector.

14.	Connect J3-HDD LED to “Hard Disk Busy” LED on the system chassis.

15.	Connect J3-TB LED to Turbo LED on the system chassis.

16.	Connect J3-RST to Reset Switch on the system chassis.

17.	Connect J3-SPK to Speaker on the system chassis.

18.	Connect J3-KBYLOCK to keylock and power LED on the system chassis.

19.	Connect power cord to J2 Power Supply Connector.

20.	Close system chassis, connect all external cables to your computer.

Jumper Setting

J1	Keyboard Connector

A standard five-pin female DIN Keyboard connector is located at the rear of the board J1.

| Pin | Description |
| --- | --- |
| 1 | Keyboard Clock |
| 2 | Keyboard Data |
| 3 | N.C. |
| 4 | Ground |
| 5 | +5VDC |

J2	Power Supply Connector

| Pin | Description | Pin | Description |
| --- | --- | --- | --- |
| 1 | Power Good | 7 | Ground |
| 2 | +5VDC | 8 | Ground |
| 3 | +12VDC | 9 | -5VDC |
| 4 | -12VDC | 10 | +5VDC |
| 5 | Ground | 11 | +5VDC |
| 6 | Ground | 12 | +5VDC |

JP1	CMOS RAM Discharge Jumper

| Pin | Description |  | Decription | JP1 |
| --- | --- | --- | --- | --- |

1

1

|  | Internal Battery Positive |  | Internal Battery Mode |  |
| --- | --- | --- | --- | --- |

1

2

Connector to CMOS

Discharge CMOS

| 3 | Ground |  |  |  |
| --- | --- | --- | --- | --- |

JP2	DIMM Module Voltage Selector

| Description | JP2 |
| --- | --- |

5V

3.3V

A      B

1

For SDRAM DIMM 
Module (3.3V)

5V

3.3V

A      B

1

For EDO DRAM/Fast Page DRAM DIMM Module (5V)

PS1	PS/2 Mouse Connector

| Pin | Description |
| --- | --- |
| 1 | Mouse Data |
| 2 | N.C. |
| 3 | Ground |
| 4 | +5V |
| 5 | Mouse CLK |
| 6 | N.C. |

USB1	2 Sets of Univeral Serial Bus Connector

| Pin | Description |
| --- | --- |
| 1,2 | +5VDC |
| 3,4 | Data - |
| 5,6 | Data+ |
| 7,8 | Ground |
| 9,10 | Ground |

J3	RST (Reset Switch Connector)

| Setting | Description |
| --- | --- |
| Open | Normal Mode |
| Short | Reset System |

KEYLOCK (Keylock & Power LED Connector)

| Pin | Description |
| --- | --- |
| 1 | LED Output |
| 2 | N.C. |
| 3 | Ground |
| 4 | Keylock |
| 5 | Ground |

TB LED (Turbo LED Connector)

| Setting | Description |
| --- | --- |
| 1 | Anode (+) |
| 2 | Cathode (-), Ground |

SPK (Speaker Connector)

| Pin | Description |
| --- | --- |
| 1 | Speaker Out |
| 2 | Ground |
| 3 | Ground |
| 4 | 5V |

HDD LED (Hard Disk LED Connector)

| Setting | Description |
| --- | --- |
| Open | Normal Mode |
| Short | Reset System |

12V

5V

JP4	Flash ROM Voltage Jumper

12V

5V

| Description | JP4 |
| --- | --- |
| 12Volt Flash programming (Default) |  |
| 5Volt Flash programming |  |

JP3	CPU Speed Jumpers

| CPU Clock | JP3 A B C | CPU Clock |
| --- | --- | --- |

JP3

A    B    C

|  | PCI CLK |
| --- | --- |

JP3D

1

1

1

| 50MHz |  | 66MHz |
| --- | --- | --- |

|  | CPUCLK/2 |
| --- | --- |

1

1

1

| 55MHz |  | 75MHz |
| --- | --- | --- |

|  | 33MHz |
| --- | --- |

1

1

1

| 60MHz |  | 83MHz |  |  |  |
| --- | --- | --- | --- | --- | --- |

1

JP5	CPU Internal Clock Speed Selectors

|  | JP5 A B |  | JP5 A B |
| --- | --- | --- | --- |

1

1.5X

2.5X

1

1

2.0X

|  |  | 3.0X |  |
| --- | --- | --- | --- |

JP6	P54C/P55C CPU Voltage Selectors

|  | JP10 A B C D |  | JP10 A B C D |
| --- | --- | --- | --- |
| 3.5V |  | 2.8V |  |
| 3.2V |  | 2.5V |  |
| 2.9V |  |  |  |