GA - 586AP

USER'S MANUAL

PCI - ISA SOLUTION

PENTIUM( PCI - ISA BUS MAINBOARD

REV. 1A First Edition

The author assumes no responsibility for any errors or omissions which may appear in this document nor does it make a commitment to update the information contained herein.

IBM PC/AT, PC/XT are trademarks of International Business Machine Corporation.

PENTIUM is a trademark of Intel Corporation.

AWARD is a trademark of Award Software, Inc.

MS-DOS WINDOWS NT are registered trademarks of Microsoft Corporation.

UNIX is a trademark of Bell Laboratories.

JANUARY 01, 1995 Taipei, Taiwan

TABLE OF CONTENTS

1.	INTRODUCTION	1-1

1.1. PREFACE	1-1

1.2. KEY FEATURES	1-1

1.3. PERFORMANCE LIST	1-2

1.4. BLOCK DIAGRAM	1-3

1.5. INTRODUCE THE PCI - BUS	1-4

1.6. FEATURES	1-4

2.	SPECIFICATION	2-1

2.1. HARDWARE	2-1

2.2. SOFTWARE	2-2

2.3. ENVIRONMENT	2-2

3.	HARDWARE INSTALLATION	3-1

3.1. UNPACKING	3-1

3.2. MAINBOARD LAYOUT	3-2

3.3. QUICK REFERENCE FOR JUMPERS & CONNECTORS	3-2

3.4. DRAM INSTALLATION	3-4

3.5. SRAM INSTALLATION AND JUMPERS SETUP	3-5

3.6. CPU INSTALLATION AND JUMPERS SETUP	3-5

3.7. CMOS RTC & ISA CFG CMOS SRAM	3-6

3.8. SPEAKER CONNECTOR INSTALLATION	3-6

3.9. POWER LED & KEY LOCK CONNECTOR INSTALLATION	3-6

3.10. TURBO SWITCH CONNECTOR INSTALLATION	3-7

3.11. TURBO LED CONNECTOR INSTALLATION	3-7

3.12. HARDWARE RESET SWITCH CONNECTOR INSTALLATION	3-7

3.13. GREEN FUNCTION INSTALLATION	3-7

3.14. PERIPHERAL DEVICE INSTALLATION	3-7

4.	BIOS CONFIGURATION	4-1

4.1. ENTERING SETUP	4-1

4.2. CONTROL KEYS	4-1

4.3. GETTING HELP	4-2

4.3.1. Main Menu	4-2

4.3.2. Status Page Setup Menu / Option Page Setup Menu	4-2

4.4. THE MAIN MENU	4-2

4.5. STANDARD CMOS SETUP MENU	4-4

4.6. BIOS FEATURES SETUP	4-9

4.7. CHIPSET FEATURES SETUP	4-12

4.8. POWER MANAGEMENT SETUP	4-14

4.9. PCI SLOT CONFIGURATION	4-16

4.10. LOAD SETUP DEFAULTS	4-18

4.11. PASSWORD SETTING	4-19

4.12. IDE HDD AUTO DETECTION	4-20

4.13. SAVE & EXIT SETUP	4-21

4.14. EXIT WITHOUT SAVING	4-22

4.15. KEYBOARD SETTING FUNCTION	4-22

5.	AT TECHNICAL INFORMATION	5-1

5.1. I/O BUS CONNECTOR PIN OUT	5-1

5.1.1. ISA SLOT PIN OUT	5-1

5.1.2. PCI - BUS SLOT PIN OUT	5-2

5.2. I/O & MEMORY MAP	5-3

5.3. TIMER & DMA CHANNELS MAP	5-3

5.4. INTERRUPT MAP	5-4

5.5. RTC & CMOS RAM MAP	5-5

APPENDIX A: POST MESSAGE	A-1

APPENDIX B: POST CODES	B-1

APPENDIX C: BIOS DEFAULT DRIVE TABLE	C-1

APPENDIX D: PROBLEM SHEET	D-1

1.	INTRODUCTION

1.1. PREFACE

Welcome to use the GA - 586AP motherboard. The motherboard is a 256 KB / 512 KB / 1 MB CACHE PENTIUM( CPU based PC / AT compatible system with ISA bus and PCI Local Bus, and has been designed to be the fastest PC / AT system. There are some new features allow you to operate the system with just the performance you want.

This manual also explains how to install the motherboard for operation, and how to set up your CMOS CONFIGURATION with BIOS SETUP program.

1.2. KEY FEATURES

Pentium( based PC / AT compatible mainboard with PCI - ISA Bus.

3 Master / Slave PCI Bus slots, 4 ISA Bus slots.

Supports 3.3V Pentium processor / P54CT running at 75-100 MHz.

Supports true 64 bits CACHE and DRAM access mode.

Supports 320 Pins (Socket 5) ZIF white socket on board.

Supports 256 KB / 512 KB / 1 MB second cache memory.

CPU  L1 / L2 Write-Back cache operation.

Supports 2 - 192 MB DRAM memory on board.

Supports 2 channels Enhance PCI IDE ports for 4 IDE Device.

Supports 2xCOM (16550), 1xLPT (EEP / ECP), 1x1.44MB Floppy port.

Supports Hardware and Software speed change function.

Supports Green function.

Licensed AWARD BIOS, FLASH EEPROM for BIOS update.

BENCHMARQ / ODIN 3287 RTC on board.

3/4BABY AT size, 4 layers PCB.

1.3. PERFORMANCE LIST

The following performance data list is the testing results of some popular benchmark testing programs. These data are just referred by users, and there is no responsibility for different testing data values gotten by users.           (The different Hardware & Software configuration will result in different benchmark testing results.)

| CPU | Pentium( processor 75/90/100 MHz |  | DRAM | 32 MB - 70 ns |  | CACHE SIZE | 256 KB |  | DISPLAY | ATi Mach64 PCI VGA |  | STORAGE | Onboard CMD IDE port + Seagate 1220A 1GB H.D. |  | O.S. | MS DOS V6.22 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

(MAINBOARD(

| Testing Program | Item | Unit | Pentium 100 | Pentium 90 | Pentium 75 |  | LandMark V2.0 | CPU | MHz | 578.54 | 520.68 | 433.9 |  |  | FPU | MHz | 1942.13 | 1747.9 | 1456.55 |  | SI V7.0 | CPU |  | 317.6 | 285.9 | 238.2 |  | BenchMark V9.0 | CPUmark 16 |  | 197.25 | 177.39 | 147.94 |  | PM 1.7 | MIPS | Mips | 68.4 | 60.9 | 51.3 |  |  | Dhrystone | K-Dstone/s | 87.7 | 78.1 | 64.9 |  |  | Whetstone | K-Wstone/s | 19594.4 | 17844.9 | 14695.8 |  | Byte V2.1 | CPU | AT Class | 32.87 | 27.97 | 21.64 |  |  |  | 386 Class | 11.21 | 11.22 | 8.45 |  |  | FPU | AT Class | 228.46 | 202.94 | 152.06 |  |  |  | 386 Class | 31.97 | 28.39 | 21.28 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

( IDE(

| Program | Ver. | Item | Unit | Pentium 100 | Pentium 90 | Pentium 75 |  | Core | 2.92 | Data Transfer Rate | KB/s | 10200.4 | 9251.1 | 7923.0 |  |  |  | Average Seek Time | ms | 9.9 | 10.0 | 10.0 |  |  |  | Track-Track Seek | ms | 2.2 | 2.3 | 2.3 |  |  |  | Performance Index |  | 66.290 | 60.582 | 52.689 |  | Benchmark | 9.0 | Disk Mix |  | 751.76 | 624.42 | 635.9 |  | PM | 1.7 | Data Transfer Rate | KB/s | 16116.9 | 16116.9 | 16116.9 |  |  |  | Mean Seek | ms/seek | 9.9 | 9.9 | 9.7 |  |  |  | Track-Track Seek | ms/seek | 2.2 | 2.2 | 2.2 |  |  |  | Aggregate | PUM's | 2478.2 | 2478.2 | 2477.7 |  | Byte | 2.1 | Disk | AT Class | 96.93 | 77.1 | 53.37 |  |  |  |  | 386 Class | 56.4 | 44.87 | 31.06 |  | SI | 7.0 | Data Transfer Rate | KB/s | 2510.5 | 2501.0 | 2509.3 |  |  |  | Average Seek | ms | 8.86 | 8.88 | 8.81 |  |  |  | Track-Track Seek | ms | 2.55 | 2.59 | 2.49 |  |  |  | HDD Index |  | 19.4 | 19.3 | 19.4 |  | Winbench95 | 4.0 | Disk Winmark95 | KB/s | 779 | 761 | 719 |  | Winstone95 | 1.0 | Winstone95 |  | 150.0 | 139.4 | 122.1 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

1.4. BLOCK DIAGRAM

(Figure 1.1(

1.5. INTRODUCE THE PCI - BUS

Connecting devices to a CPU local bus can dramatically increase the speed of I/O-bound peripherals with only a slight increase in cost over traditional systems. This price / performance point has created a vast market potential for local bus products. The main barrier to this market has been the lack of an accepted standard for local bus peripherals. Many mainboard and chipset manufactures developed their own local bus implementations, but they are incompatible with each other. The VL (Video Electronics Standards Association) local bus and PCI (Peripheral Component Interconnect) bus specification was created to end this confusion.

The PCI - bus standard, under development since Jun. 1992, which is designed to bring workstation-level performance to standard PC platform. The PCI - bus removes many of the bottlenecks that have hampered PC for several years. On the PCI - bus, peripherals operate at the native speed of the computer system, thus enabling data transfer between peripherals and the system at maximum speed. This performance is critical for bandwidth-constrained devices such as video, multimedia, mass storage, and networking adapters.

PCI - bus standard provides end-users with a low-cost, extendible and portable local bus design, which will allow system and peripherals from different manufactures to work together.

1.6. FEATURES

32 bits bus transfer mode.

Bus Master or Slave access.

Memory burst transfer to 132 MB/sec.

33 MHz operation speed.

10 device loading ability.

CPU independent.

2.	SPECIFICATION

2.1. HARDWARE

CPU

Pentium( processor 75 / 90 / 100 MHz, P54CT.

| 320 pins (socket 5) ZIF white socket on board. |  | COPROCESSOR | Included in Pentium. |  | SPEED |
| --- | --- | --- | --- | --- | --- |

50 / 60 / 66 MHz system and 25 / 30 / 33

PCI-Bus speed.

7.5 / 8 MHz AT bus speed.

Hardware and Software speed switchable

| function (half speed). |  | DRAM MEMORY |
| --- | --- | --- |

3 banks 72 pins SIMM module socket on board.

Use 1 / 2 / 4 / 8 / 16 / 32 MB 70 ns SIMM

module DRAM.

2 ~ 192 MB DRAM size.

| Support Fast Page DRAM access mode. |  | CACHE MEMORY |
| --- | --- | --- |

16 KB cache memory included in Pentium.

256 KB / 512 KB / 1 MB second cache memory

on board.

Support Write Back cache function for both CPU

| & on board cache. |  | SHADOW RAM |
| --- | --- | --- |

Main BIOS shadow function.

Video BIOS shadow function programmable.

| Shadow RAM cacheable function. |  | I/O BUS SLOTS |
| --- | --- | --- |

3 Master / Slave PCI-Bus.

| 4 16 bits ISA Bus. |  | IDE PORTS |
| --- | --- | --- |

2 Enhanced IDE channels on board. (Using

IRQ14, 15)

Support Mode 3,4 IDE & ATAPI CD - ROM.

Driver Support DOS, WINDOWS, OS/2, NT,

| Netware. |  | I/O PORTS |
| --- | --- | --- |

Supports 2 16550 COM ports. (Using IRQ4, 3)

Supports 1 EPP/ECP LPT port. (Using IRQ7)

Supports 1 1.44MB Floppy port. (Using DMA2 &

| IRQ6) |  | GREEN FUNCTION |
| --- | --- | --- |

Standby & Suspend mode support.

Green switch & LED support.

IDE & Display power down support.

| Monitor all IRQ / DMA / Display / I/O events. |  | BIOS | 128KB FLASH EEPROM. |  | DIMENSION | 3/4Baby AT size / 4 layers. |  |
| --- | --- | --- | --- | --- | --- | --- | --- |

2.2. SOFTWARE

BIOS

Licensed AWARD BIOS.

AT CMOS Setup, BIOS / Chipset Setup and

| Hard Disk Utility included. |  | O.S. & IDE DRIVER |
| --- | --- | --- |

Operation with MS-DOS, WINDOWS NT,

| OS/2, NOVELL and SCO UNIX. |  |
| --- | --- |

2.3. ENVIRONMENT

| Ambient Temp. | 0(C to +50(C (Operating). |  | Relative Hum. | 0 to +85% (Operating). |  | Altitude | 0 to 10,000 feet (Operating). |  | Vibration | 0 to 1,000 Hz. |  | Electricity |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

4.9 V to 5.2 V.

| 5 A to 7 A current. |  |
| --- | --- |

3.	HARDWARE INSTALLATION

3.1. UNPACKING

The mainboard package should contain the following:

The GA - 586AP mainboard.

Diskette for Enhanced IDE Device Driver ( 1 x 1.44MB Diskette).

USER'S MANUAL.

Cable set for I/O Device.

The mainboard contains sensitive electric components which can be easily damaged by static electricity, so the mainboard should be left in its original packing until it is installed.

Unpacking and installation should be done on a grounded anti-static mat. The operator should be wearing an anti static wristband, grounded at the same point as the anti-static mat.

Inspect the mainboard carton for obvious damage. Shipping and handling may cause damage to your board. Be sure there are no shipping and handling damages on the board before proceeding.

After opening the mainboard carton, extract the system board and place it only on a grounded anti-static surface component side up. Again inspect the board for damage. Press down on all of the socket IC's to make sure that they are properly seated. Do this only on with the board placed on a firm flat surface.

DO NOT APPLY POWER TO THE BOARD IF IT HAS BEEN DAMAGED.

You are now ready to install your maniboard. The mounting hole pattern on the mainboard matches the IBM-AT system board. It is assumed that the chassis is designed for a standard IBM XT/AT mainboard mounting.

Place the chassis on the anti-static mat and remove the cover. Take the plastic clips, Nylon stand-off and screws for mounting the system board, and keep them separate.

3.2. MAINBOARD LAYOUT

(Figure 3.1(

3.3. QUICK REFERENCE FOR JUMPERS & CONNECTORS

| P1: Keyboard Connector |  |  | Pin No. | Function |  | 1 | Key Clock. |  | 2 | Key Data. |  | 3 | NC. |  | 4 | VCC (+5V). |  | 5 | GND. |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| P3: Power Connector |  |  | Pin No. | Function |  | 1 | Power Good signal |  | 2,10,11,12 | VCC (+5V) |  | 3 | +12V |  | 4 | -12V |  | 5,6,7,8 | GND |  | 9 | -5V |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| JP14: Reset Switch |  |  | Open | For normal operation. |  | Close | For hardware reset system. |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| JP18: Power LED and Key-Lock Connector |  |  | Pin No. | Function |  | 1 | LED anode (+). |  | 2 | NC. |  | 3 | LED cathode (-). |  | 4 | Key lock. |  | 5 | GND. |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| JP15: Turbo Switch |  |  | Pin No. | Function |  | Close | For low speed (Non-cache). |  | Open | For high speed. |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| JP16: Turbo LED Connector |  |  | Pin No. | Function |  | 1 | LED anode (+). |  | 2 | LED cathode (-). |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| JP17: Speaker Connector |  |  | Pin No. | Function |  | 1 | VCC. |  | 2 | NC. |  | 3 | NC. |  | 4 | Data. |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| JP12: Green Function Switch |  |  | Pin No. | Function |  | Close | For system entering Green mode ( Suspend mode). |  | Open | Normal operation. |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| JP13: Green Function LED |  |  | Pin No. | Function |  | 1 | LED anode (+). |  | 2 | LED cathode (-). |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| JP2 | JP3 | Second Cache Size Selection |  | Pin No. |  | Function |  | 1-2 | 1-2 | Close for 256 KB cache size ( using 32K x 8 SRAM ). |  | 1-2 | 2-3 | Close for 512 KB cache size ( using 64K x 8 SRAM ). |  | 2-3 | 2-3 | Close for 1 MB cache size ( using 128K x 8 SRAM ). |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| JP21: System Speed Selection |  |  |  | JP11 | JP10 | Function |  | 2-3 | 2-3 | For 50 MHz system speed ( CPU 75 MHz ). |  | 1-2 | 1-2 | For 60 MHz system speed ( CPU 90 MHz ). |  | 2-3 | 1-2 | For 66 MHz system speed ( CPU 100 MHz ). |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| JP1: CPU Cooling Fan Power Connector |  |  | Pin No. | Function |  | 1 | +12V |  | 2 | GND |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| CN1-6 I/O Ports Connector |  |  | CN1 | For COM 1/3 (Serial port1) |  | CN2 | For COM 2/4 (Serial port2) |  | CN3 | For Floppy port |  | CN4 | For LPT port |  | CN5 | For Primary IDE port |  | CN6 | For Secondary IDE port |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

3.4. DRAM INSTALLATION

The mainboard can be installed with 1 / 2 / 4 / 8 / 16 / 32 MB 72 pins SIMM module DRAM, and the DRAM speed must be 70 ns. The DRAM memory system on mainboard consists of bank 0 & bank 1. The DRAM of bank 0 must be installed first. Each bank consist of 2 PCs, 72 pins SIMM module DRAM. Because the 72 pins SIMM module is 32 bits width, using 2 PCs which can match a 64 bits system. The total memory size is 2 - 192 MB, and various configuration of DRAM types in the following TABLE are for reference:

| Bank0 | Bank1 | Bank2 | Sigle: | Single bank SIMM Module |  | Single | None | None |  | Ex. 1MB, 4MB, 16MB |  | Single | Single | None |  |  |  | Single | Single | Single | Double: | Double banks SIMM Module |  | Double | None | None |  | Ex. 2MB, 8MB, 32MB |  | Double | Single | None |  |  |  | Double | Single | Single |  |  |  | Double | Single | Double |  |  |  | Double | Double | Double |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

The DRAM installation position refer to Figure 3.1, and notice the Pin 1 of SIMM module must match with the Pin 1 of SIMM socket when the DRAM SIMM module is installed.

Insert the DRAM SIMM module into the SIMM socket at 45 degree angle. If there is  a wrong direction of Pin 1, the DRAM SIMM module couldn't be inserted into socket completely. After completely insert SIMM module into socket, then press the SIMM module in vertical direction until the left and right metal holders can keep the SIMM module standing up con-firmly.

3.5. SRAM INSTALLATION AND JUMPERS SETUP

The cache memory system consists of Data SRAM & TAG SRAM (U12), the Data SRAM type is 32Kx8-15  ns, 64Kx8-15/20  ns or 128Kx8-15  ns.

The mainboard can be installed with 256 KB, 512 KB or 1 MB cache memory when using 32Kx8, 64Kx8, 128Kx8 type DATA SRAM separately. Please refer to the following table to install cache memory system :

| SIZE | Data SRAM | JP3 | JP2 | TAG SRAM (U12) |  | 256 KB | 32 KB x 8 | 1-2 | 1-2 | 8 KB x 8 - 32 K x 8 |  | 512 KB | 64 KB x 8 | 2-3 | 1-2 | 16 KB x 8,32 K x 8 |  | 1 MB | 128 KB x 8 | 2-3 | 2-3 | 32 KB x 8 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Because there are not standard IC's coding number of SRAM, refer to the following table to identify the SRAM component:

| 16 K x 8 | 32 K x 8 | 64 K x 8 | 128 K x 8 |  | AE88128AK-15 | W24257AK-15 | W24512AK-15 | W241024AK-15 |  |  | UM61256-15 | UM61512K-15 | UM611024AK-15 |  |  | AS7C256-15 | UM61512K | UM611024AK-15 |  |  | CY7C199 |  |  |  |  | MCM6206 |  |  |  |  | KM68257BP |  |  |  |  | TC555328P |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

3.6. CPU INSTALLATION AND JUMPERS SETUP

The system's speed depends on the frequency of CLOCK GENERATOR. The user can change the JUMPER (JP10, JP11) selection to set up the system speed to 50 MHz, 60 MHz or 66 MHz for 75 MHz, 90 MHz or 100 MHz 3.3 V PENTIUM( processor.

The mainboard can use PENTIUM( or P54CT CPU, and the CPU speed must match with the frequency of CLOCK GEN. It will cause system hanging up if the CLOCK GEN.'S frequency is higher than CPU's.

| JP11 | JP10 | CPU Type | CLK. GEN. Speed | CPU Speed |  | 2-3 | 2 - 3 | PENTIUM( - 75 | 50 MHz | 75 MHz |  | 1-2 | 1 - 2 | PENTIUM( - 90 | 60 MHz | 90 MHz |  | 2-3 | 1 - 2 | PENTIUM( - 100 | 66 MHz | 100 MHz |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

The CPU is a sensitive electric component and it can be easily damaged by static electricity, so users must keep it away from metal surface when the CPU is installed onto mainboard.

When the user installs the CPU on socket, please notice the PIN 1 of CPU is in the same corner as the PIN 1 of socket!

Before the CPU is installed, the mainboard must be placed on a flat plane in order to avoid being broken by the pressure of CPU installation.

3.7. CMOS RTC & ISA CFG CMOS SRAM

There're RTC & CMOS SRAM on board, they have a power supply from internal battery to keep the DATA inviolate & effective. The RTC is a REAL-TIME CLOCK device which provides the DATE & TIME to system. The CMOS SRAM is used for keeping the information of ISA device system configuration, so the system can automatically boot OS. every time.

Due to the life-time of RTC internal battery is 10 years, the user can change a new RTC to replace old one after it can not work. The new one's brand and type must be same with old one.

3.8. SPEAKER CONNECTOR INSTALLATION

There is always a speaker in AT system for sound purpose. The 4 - Pins connector JP17 is used to connect speaker. The speaker can work well in both direction of connector when it is installed to the connector JP17 on mainboard.

3.9. POWER LED & KEY LOCK CONNECTOR INSTALLATION

There are a system power LED lamp and a key on the panel of case. The power LED will light on when system is powered-on, and the key can lock the keyboard input or unlock it, both of them are connected to a 5 PIN connector. The connector should  be installed to JP18 of mainboard in correct direction.

3.10. TURBO SWITCH CONNECTOR INSTALLATION

The TURBO switch on the panel is used for controlling the system speed. Some program developed on XT should be executed with a low speed system, so a high speed system needs the speed switching function to change its running speed.

The mainboard uses helf speed method to implement TURBO switching function. The JP15 on mainboard should be connected to the TURBO switch on panel, and user can push in or pop out the TURBO switch to enable or disable the turbo function of system.

If not necessary, please don't use De-turbo mode. (always keep system in Turbo mode)

3.11. TURBO LED CONNECTOR INSTALLATION

The TURBO LED on panel can indicate the current speed status of system. The TURBO LED connector should be installed to JP16 in correct direction.

3.12. HARDWARE RESET SWITCH CONNECTOR INSTALLATION

The RESET switch on panel provides users with HARDWARE RESET function which is almost the same as power-on/off. The system will do a cold start after  the RESET switch is pushed and released by user. The RESET switch is a 2 PIN connector and should be installed to JP14 on mainboard.

3.13. GREEN FUNCTION INSTALLATION

For the purpose of power saving, there are two jumpers, JP13 and JP12, to make sure the power saving function doing well. The JP13 is a indicator (green LED) for green function. If the green LED is ON, the system is operating in green mode. The JP12 is a switch to force the  system get into green mode immediately.

3.14. PERIPHERAL DEVICE INSTALLATION

After the device installation and jumpers setup, the mainboard can be mounted into the case and fixed by screw. To complete the mainboard installation, the peripheral device could be installed now. The basic system needs a display interface card and a disk device.

If the PCI - Bus device is to be installed in the system, any one of three PCI - Bus slots can be used no matter Slave or Master PCI - Bus device being installed.

After installing the peripheral device, the user should check everything again, and prepare to power-on the system.

4.	BIOS CONFIGURATION

Award's BIOS ROM has a built-in Setup program that allows users to modify the basic system configuration. This type of information is stored in battery-backed CMOS SRAM so that it retains the Setup information when the power is turned off.

4.1. ENTERING SETUP

Power ON the computer and press <Del> immediately will allow you to enter Setup. The other way to enter Setup is to power on the computer, when the below message appears briefly at the bottom of the screen during the POST (Power On Self Test), press <Del> key or simultaneously press <Ctrl>, <Alt>,  and  <Esc> keys.

TO ENTER SETUP BEFORE BOOT PRESS CTRL-ALT-ESC OR DEL KEY

If the message disappears before you respond and you still wish to enter Setup, restart the system to try again by turning it OFF then ON or pressing the "RESET" bottom on the system case. You may also restart by simultaneously press <Ctrl>,<Alt>, and <Del> keys. If you do not press the keys at the correct time and the system does not boot, an error message will be displayed and you will again be asked to,

PRESS F1 TO CONTINUE, CTRL-ALT-ESC OR DEL TO ENTER SETUP

4.2. CONTROL KEYS

| Up arrow | Move to previous item |  | Down arrow | Move to next item |  | Left arrow | Move to the item in the left hand |  | Right arrow | Move to the item in the right hand |  | Esc key | Main Menu - Quit and not save changes into CMOS Status Page Setup Menu and Option Page Setup Menu - Exit current page and return to Main Menu |  | PgUp key | Increase the numeric value or make changes |  | PgDn key | Decrease the numeric value or make changes |  | F1 key | General help, only for Status Page Setup Menu and Option Page Setup Menu |  | F2 key | Change color from total 16 colors |  | F3 key | Calendar, only for Status Page Setup Menu |  | F4 key | Reserved |  | F5 key | Restore the previous CMOS value from CMOS, only for Option Page Setup Menu |  | F6 key | Load the default CMOS value from BIOS default table, only for Option Page Setup Menu |  | F7 key | Load the default |  | F8 key | Reserved |  | F9 key | Reserved |  | F10 key | Save all the CMOS changes, only for Main Menu |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

4.3. GETTING HELP

4.3.1.	Main Menu

The on-line description of the highlighted setup function is displayed at the bottom of the screen.

4.3.2.	Status Page Setup Menu / Option Page Setup Menu

Press F1 to pop up a small help window that describes the appropriate keys to use and the possible selections for the highlighted item. To exit the Help Window press <Esc>.

4.4. THE MAIN MENU

Once you enter Award BIOS CMOS Setup Utility, the Main Menu (Figure 4.1) will appear on the screen. The Main Menu allows you to select from seven setup functions and two exit choices. Use arrow keys to select among the items and press <Enter> to accept or enter the sub-menu.

Figure 4.1: Main Menu

Standard CMOS setup

This setup page includes all the items in a standard compatible BIOS.

BIOS features setup

This setup page includes all the items of Award special enhanced features.

Chipset features setup

This setup page includes all the items of chipset special features.

Power management  setup

This setup page includes all the items of Green function features.

PCI configuration setup

This setup page includes all the configurations of PCI slots parameters.

Load setup defaults

BIOS defaults indicates the most appropriate value of the system parameter which the system would be in maximum performance.

Password setting

Change, set, or disable password. It allows you to limit access to the system and Setup, or just to Setup.

IDE HDD auto detection

Automatically configure hard disk parameter.

Save & exit setup

Save CMOS value changes to CMOS and exit setup.

Exit without save

Abandon all CMOS value changes and exit setup.

4.5. STANDARD CMOS SETUP MENU

The items in Standard CMOS Setup Menu (Figure 4.2) are divided into 9 categories. Each category includes no, one or more than one setup items. Use the arrows to highlight the item and then use the <PgUp> or <PgDn> keys to select the value you want in each item.

Figure 4.2: Standard CMOS Setup Menu

Date

The date format is <day>, <date> <month> <year>. Press <F3> to show the calendar.

| day | The day, from Sun to Sat, determined by the BIOS and is display-only |  | date | The date, from 1 to 31 (or the maximum allowed in the month) |  | month | The month, Jan. through Dec. |  | year | The year, from 1900 through 2099 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Time

The time format in <hour> <minute> <second>. The time is calculated base on the 24-hour military-time clock. For example, 1 p.m. is 13:00:00.

Primary HDDs / Secondary HDDs

The category identify the types of hard disk drive C drive F 4 devices that has been installed in the computer. There are 46 pre-defined types and a user definable type. Type 1 to Type 46 are pre-defined. Type User is user-definable.

Press PgUp or PgDn to select a numbered hard disk type or type the number and press <Enter>. Note that the specifications of your drive must match with the drive table. The hard disk will not work properly if you enter improper information for this category. If your hard disk drive type is not matched or listed, you can use Type User to define your own drive type manually.

If you select Type User, related information is asked to be entered to the following items. Enter the information directly from the keyboard and press <Enter>. Those information should be provided in the documentation form your hard disk vendor or the system manufacturer.

| CYLS. | number of cylinders |  | HEADS | number of heads |  | PRECOMP | write precom |  | LANDZONE | landing zone |  | SECTORS | number of sectors |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

If a hard disk has not been installed select NONE and press <Enter>.

Drive A type / Drive B type

The category identify the types of floppy disk drive A or drive B that has been installed in the computer.

| None | No floppy drive installed |  | 360K, 5.25 in. | 5-1/4 inch PC-type standard drive; 360 kilobyte capacity |  | 1.2M, 5.25 in. | 5-1/4 inch AT-type high-density drive; 1.2 megabyte capacity |  | 720K, 3.5 in. | 3-1/2 inch double-sided drive; 720 kilobyte capacity |  | 1.44M, 3.5 in. | 3-1/2 inch double-sided drive; 1.44 megabyte capacity |  | 2.88M, 3.5 in. | 3-1/2 inch double-sided drive; 2.88 megabyte capacity |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Video

The category detects the type of adapter used for the primary system monitor that must matches your video display card and monitor. Although secondary monitors are supported, you do not have to select the type in setup.

| EGA/VGA | Enhanced Graphics Adapter/Video Graphics Array. For EGA, VGA, SVGA, or PGA monitor adapters |  | CGA 40 | Color Graphics Adapter, power up in 40 column mode |  | CGA 80 | Color Graphics Adapter, power up in 80 column mode |  | MONO | Monochrome adapter, includes high resolution monochrome adapters |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Halt on

The category determines whether the computer will stop if an error is detected during power up.

| NO errors | Whenever the BIOS detects a non-fatal error the system will be stopped and you will be prompted |  | All errors | The system boot will not be stopped for any error that may be detected |  | All,But Keyboard | The system boot will not stop for a keyboard error; it will stop for all other errors |  | All, But Diskette | The system boot will not stop for a disk error; it will stop for all other errors |  | All, But Disk/Key | The system boot will not stop for a keyboard or disk error; it will stop for all other errors |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Memory

The category is display-only which is determined by POST (Power On Self Test) of the BIOS.

Base Memory

The POST of the BIOS will determine the amount of base (or conventional) memory installed in the system. The value of the base memory is typically 512 K for systems with 512 K memory installed on the motherboard, or 640 K for systems with 640 K or more memory installed on the motherboard.

Extended Memory

The BIOS determines how much extended memory is present during the POST. This is the amount of memory located above 1 MB in the CPU's memory address map.

Expanded Memory

Expanded Memory in memory defined by the Lotus/Intel/Microsoft (LIM) standard as EMS. Many standard DOS applications can not utilize memory above 640 K, the Expanded Memory Specification (EMS) swaps memory which not utilized by DOS with a section, or frame, so these applications can access all of the system memory. Memory can be swapped by EMS is usually 64 K within 1 MB or memory above 1 MB, depends on the chipset design.

Expanded memory device driver is required to use memory as Expanded Memory.

Other Memory

This refers to the memory located in the 640 K to 1024 K address space. This is memory that can be used for different applications. DOS uses this area to load device drivers to keep as much base memory free for application programs. Most use for this area is Shadow RAM.

4.6. BIOS FEATURES SETUP

Virus Warning

This category flashes on the screen. During and after the system boots up, any attempt to write to the boot sector or partition table of the hard disk drive will halt the system and the following error message will appear, in the mean time, you run can anti-virus program to locate the problem. Default value is Enabled.

| Enabled | Activate automatically when the system boots up causing a warning message to appear when anything attempts to access the boot sector or hard disk partition table |  | Disabled | No warning message to appear when anything attempts to access the boot sector or hard disk partition table |  |
| --- | --- | --- | --- | --- | --- |

CPU Internal Cache / External Cache

These two categories speed up memory access. However, it depends on CPU / chipset design. The default value is Enabled.

| Enabled | Enable cache |  | Disabled | Disable cache |  |
| --- | --- | --- | --- | --- | --- |

Quick Power On Self Test

This category speeds up Power On Self Test (POST) after you power on the computer. If it is set to Enable, BIOS will shorten or skip

# Comments

Se