TIARA Computer Systems, Inc.
		      (C) Copyright 1992.  All Rights Reserved.

     ---------------------------------------------------------------------------
                           NDIS Device Driver Installation
                                       - for -
                    Microsoft Lan Manager Versions 1.10 and 2.00
     ---------------------------------------------------------------------------
     Please note that these instructions assume that the user is already
     familiar with the requirements of the particular environment in terms of
     workstation setup and software generation.  That is, these instructions
     only deal with the basic issue of merging the TIARA device driver into the
     particular environment so that workstation generation may then be performed
     by the user.

     Copyright/Trademark Information:--

          Microsoft is a registered trademark of Microsoft Corporation.

          OS/2 is a registered trademark of International Business Machines
          Corporation.

     General Instructions:--

          In the instructions which follow, "S:" is used to designate the
          (SOURCE) drive containing the TIARA driver distribution diskette,
          and "T:" is used to designate the (TARGET) drive to which the
          particular item is to be installed.

          For example, if the TIARA diskette is in drive "A:" and the user
          is installing to drive "B:", then the user should substitute "A:"
          for "S:" and "B:" for "T:" as follows:

               Original command:   "COPY S:FILENAME T:"
               Modified command:   "COPY A:FILENAME B:"

     Installation instructions for version 2.00

          The MSLANMAN.DOS and MSLANMAN.OS2 directories have been constructed in
          accordance with the requirements of the Lan Manager SETUP utility
          Action menu Import function.

















                                                                                     ___________________________________________________________________________
     Document:	LANMAN.DOC	    June 12, 1992			  Page 1




                            TIARA Computer Systems, Inc.
		      (C) Copyright 1992.  All Rights Reserved.

     ---------------------------------------------------------------------------
                           NDIS Device Driver Installation
                                       - for -
                    Microsoft Lan Manager Versions 1.10 and 2.00
     ---------------------------------------------------------------------------
     Installation instructions for version 1.10

          OS/2 diskette preparation.

	       1.   Use the DISKCOPY command to make a duplicate of the OS/2
		    NET TRANSPORTS & NDIS DRIVERS diskette for steps 2 and 3.

               2.   Create the TIARA device driver directory:

                    MD T:\LANMAN\DRIVERS\TNDIS

               3.   Copy the TIARA driver files to the above directory:

                    COPY S:\MSLANMAN.OS2\DRIVERS\ETHERNET\TNDIS\TNDIS.OS2
                         T:\LANMAN\DRIVERS\TNDIS

                    COPY S:\MSLANMAN.110\OS2\TNDIS.NIF T:\LANMAN\DRIVERS\TNDIS

                    COPY S:\MSLANMAN.110\OS2\PROTOCOL.INI
                         T:\LANMAN\DRIVERS\TNDIS

          DOS diskette preparation.

               1.   Use the DISKCOPY command to make a duplicate of the DOS NET
                    TRANSPORTS & NDIS DRIVERS diskette #2 for steps 2 and 3.

               2.   Create the TIARA device driver directory:

                    MD T:\LANMAN\DRIVERS\TNDIS

               3.   Copy the TIARA driver files to the above directory:

                    COPY S:\MSLANMAN.DOS\DRIVERS\ETHERNET\TNDIS\TNDIS.DOS
                         T:\LANMAN\DRIVERS\TNDIS

                    COPY S:\MSLANMAN.110\DOS\TNDIS.NIF T:\LANMAN\DRIVERS\TNDIS

                    COPY S:\MSLANMAN.110\DOS\PROTOCOL.INI
                         T:\LANMAN\DRIVERS\TNDIS











                                                                                     ___________________________________________________________________________
     Document:	LANMAN.DOC	    June 12, 1992			  Page 2





                            TIARA Computer Systems, Inc.
		      (C) Copyright 1992.  All Rights Reserved.

     ---------------------------------------------------------------------------
                        TNDIS PROTOCOL Parameter Descriptions
     ---------------------------------------------------------------------------
     The following parameters are generic to any model of the EtherStar-based
     LanCard/E.

     KeyWord       Minimum Maximum Default   Description / Comments
     ------------  ------- ------- -------   -----------------------------------
     DriverName                     TNDIS$   REQUIRED Parameter.

                                             Up to nine copies of this driver
                                             may be loaded into memory at once,
                                             one for each LanCard/E supported.

                                             The default name specified will
                                             apply to the first copy of the
                                             driver.  Additional copies should
                                             use the following names in the
                                             order specified:

                                             TNDIS2$, TNDIS3$, TNDIS4$, TNDIS5$,
                                             TNDIS6$, TNDIS7$, TNDIS8$, TNDIS9$

     MaxTransmits        1     142       6   Maximum number of Transmit Requests
                                             which can be queued by the driver.




     The following parameters are specific to the particular version of
     LanCard/E.

          ISA-bus:  Industry Standard Architecture.

          MCA-bus:  Micro Channel Architecture.

     KeyWord       Minimum Maximum Default   Description / Comments
     ------------  ------- ------- -------   -----------------------------------
     Interrupt           2      15       3   Interrupt Request Level for ISA-bus
                                             machines.

                                             For allowable values, consult the
                                             appropriate owner's manual.

     IOAddress           0 0x0FFE0   0x300   Input/Output Base Address for ISA-
                                             bus machines

                                             For allowable values, consult the
                                             appropriate owner's manual.






                                                                                     ___________________________________________________________________________
     Document:	LANMAN.DOC	    June 12, 1992			  Page 3




                            TIARA Computer Systems, Inc.
		      (C) Copyright 1992.  All Rights Reserved.

     ---------------------------------------------------------------------------
                        TNDIS PROTOCOL Parameter Descriptions
     ---------------------------------------------------------------------------

     KeyWord       Minimum Maximum Default   Description / Comments
     ------------  ------- ------- -------   -----------------------------------
     Slot                0       8       0   Slot Number for MCA-bus machines.

                                             If the Slot Number is set to zero,
                                             or unspecified on a MCA-bus
                                             machine, the driver will execute a
                                             search algorithm scanning from slot
                                             1 to 8 in an attempt to identify a
                                             slot containing a LanCard/E*MC.

                                             If the above search is
                                             unsuccessful, or the specified slot
                                             does not contain a LanCard/E*MC,
                                             the driver will use the IOAddress
                                             and Interrupt parameters just as
                                             though it were operating in an ISA-
                                             bus machine.













                                                                                     ___________________________________________________________________________
     Document:	LANMAN.DOC	    June 12, 1992			  Page 4