TIARA Computer Systems, Inc.
		      (C) Copyright 1992.  All Rights Reserved.

     ---------------------------------------------------------------------------
                     Novell NetWare 286/386 Driver Installation
     ---------------------------------------------------------------------------
     This file describes the steps needed for installation of the TIARA NetWare
     device driver(s) in the following environments:--

		       NetWare 286 Versions 2.12 and 2.15c
		       NetWare 386 Versions 3.0 and 3.1x

     Please note that these instructions assume that the user is familiar with
     the requirements for Server and Workstation installation per Novell's
     instructions for standard NetWare 286/386.

     Files which pertain to NetWare 286 Installations:--

	  Filename	       Description
	  ----------	       -------------------------------------------------
	  ATIARA.OBJ	       Object file for Server/Bridge Generation (LANA)
	  BTIARA.OBJ	       Object file for Server/Bridge Generation (LANB)
	  CTIARA.OBJ	       Object file for Server/Bridge Generation (LANC)
	  DTIARA.OBJ	       Object file for Server/Bridge Generation (LAND)
	  TIARA.LAN	       Configuration file for Server/Bridge Generation

	  STIARA.OBJ	       Object file for Shell (IPX) Generation
	  STIARA.LAN	       Configuration file for Shell (IPX) Generation





     General Instructions:--

          In the instructions which follow, "S:" is used to designate the
          (SOURCE) drive containing the TIARA driver distribution diskette,
          and "T:" is used to designate the (TARGET) drive to which the
          particular item is to be installed.

          For example, if the TIARA diskette is in drive "A:" and the user
          is installing to drive "B:", then the user should substitute "A:"
          for "S:" and "B:" for "T:" as follows:

               Original command:   "COPY S:FILENAME T:"
               Modified command:   "COPY A:FILENAME B:"












                                                                                     ___________________________________________________________________________
     Document:	NETWARE.DOC	   October 9, 1992			  Page 1




                            TIARA Computer Systems, Inc.
		      (C) Copyright 1992.  All Rights Reserved.

     ---------------------------------------------------------------------------
                     Novell NetWare 286/386 Driver Installation
     ---------------------------------------------------------------------------
     Installation instructions for NetWare version 2.1x.

          Note that the TIARA distribution diskette has been given a DOS volume
          label of "LAN_DRV_223" which conforms to the requirements of the
          ELSGEN/NETGEN/BRGEN/SHGEN utilities.

          Floppy Disk Generations:

               1.   Proceed according to the NetWare instructions for the
                    particular type of generation.

               2.   At the LAN driver selection menu, for the first (or only)
                    driver, choose the "Load and Select" option and insert the
                    TIARA distribution diskette (LAN_DRV_223) when prompted to
                    do so.

               3.   Respond to any informational or warning prompts as they
                    occur.

                    In normal circumstances, the only message/prompt which
		    should appear is the one which informs the user of the
		    Lan Option Name of the loaded TIARA driver(s).

          First-time Hard Disk Generations:

	       1.   Follow the NetWare instructions pertaining to initial
		    upload of the NetWare diskette(s).

               2.   When asked the question "Upload Additional Diskettes?"
		    answer yes, and insert the TIARA megadiskette when
                    requested to do so.

          Pre-existing Hard Disk Generations:

               The following instructions assume that the current directory is
               set to the NetWare generation directory.

               1.   Create the TIARA directory:

                    MD LAN_DRV_.223

               2.   For a NetWare Server or Bridge generation, copy the
                    following files to the TIARA directory (LAN_DRV_.223):

                    ATIARA.OBJ, BTIARA.OBJ, CTIARA.OBJ, DTIARA.OBJ, and
                    TIARA.LAN

               3.   For a NetWare Shell (IPX) generation, copy the following
                    files to the TIARA directory (LAN_DRV_.223):

                    STIARA.OBJ, and STIARA.LAN

                                                                                     ___________________________________________________________________________
     Document:	NETWARE.DOC	   October 9, 1992			  Page 2




                            TIARA Computer Systems, Inc.
		      (C) Copyright 1992.  All Rights Reserved.

     ---------------------------------------------------------------------------
                     Novell NetWare 286/386 Driver Installation
     ---------------------------------------------------------------------------
     Installation instructions for NetWare 386.

          Please Note:  TIARA strongly recommends that all modifications
	  outlined below be made to DUPLICATE copies of the stated diskettes
	  and NOT to the originals.

	  Version 3.0 Server

	       1.   Copy NETWARE.386\LANCARDE.LAN to the Netware 386 "SYSTEM"
                    diskette.

	       2.   Follow the instructions in the Novell Installation Manual
		    to load the driver.

	  Version 3.0 DOS Workstation

	       1.   Copy NETWARE.386\LANCARDE.COM to the master workstation
                    diskette.

	       2.   Follow the instructions in the Novell Installation Manual
		    to load the driver.

	  Version 3.1x Server

	       1.   Copy NETWARE.386\LANCARDE.LAN to the Netware 386 "Operating
                    System-2" diskette.

	       2.   Follow the instructions in the Novell Installation Manual
		    to load the driver.

	  Version 3.1x DOS Workstation

	       1.   Copy NETWARE.386\LANCARDE.COM to the master workstation
                    diskette.

	       2.   Follow the instructions in the Novell Installation Manual
		    to load the driver.

	  Requester for OS/2 Workstation

	       1.   If Novell's OS/2 Requester is not already installed,
		    install it now.

	       After the installation but BEFORE rebooting:

	       2.  Edit CONFIG.SYS to replace the current hardware driver with
		   this one.
			Example:  old driver - device=c:\netware\ne2000.sys
				replace with - device=c:\netware\lcarde.sys

	       3.  Copy LCARDE.SYS from the floppy to the directory specified
		   in the config.sys load statement.
			Example:  copy a:lcarde.sys c:\netware\lcarde.sys

                                                                                     ___________________________________________________________________________
     Document:	NETWARE.DOC	   October 9, 1992			  Page 3




                            TIARA Computer Systems, Inc.
		      (C) Copyright 1992.  All Rights Reserved.

     ---------------------------------------------------------------------------
                     Novell NetWare 286/386 Driver Installation
     ---------------------------------------------------------------------------

	       4.  Edit NET.CFG, if necessary.	Include a section in NET.CFG
		   if you are currently using any special keywords with the
		   old driver.
			Example:  old driver - link driver NE2000
						   frame ethernet_802.2
					 add - link driver LCARDE
						   frame ethernet_802.2

		   Note:  If you have set your hardware configuration jumpers
		   to something other than the default settings (IRQ 3, port
		   300), NET.CFG MUST be modified.
		   Example:  if your hardware is set to IRQ 5 and port 320h
		   add the following statements to NET.CFG:
			link driver LCARDE
			   port 320
			   int 5

	       5.  Reboot your computer.


     Industry Standard Architecture (ISA) Configuration options supported:

	  I/O Base Address	   300h, 320h, 380h, 3E0h,
				   260h, 280h, 2A0h, 2E0h
          Interrupt Request        3, 4, 5, 7, 9, 10, 11, 12, 15
				   Note that for the LanCard/E*PC, interrupt
				   request jumper 2 is the same as interrupt
                                   request 9 to the driver.
          Node ID:                 Configurable.
	  Protocol ID:		   Ethernet_802.3 (default), Ethernet_802.2,
				   Ethernet_II, Ethernet_SNAP.

     Micro Channel Architecture (MCA) Configuration options supported:

          Slot Number:             1, 2, 3, 4, 5, 6, 7, 8.
          Node ID:                 Configurable.
	  Protocol ID:		   Ethernet_802.3 (default), Ethernet_802.2,
				   Ethernet_II, Ethernet_SNAP.
                                                                                     ___________________________________________________________________________
     Document:	NETWARE.DOC	   October 9, 1992			  Page 4