TSOUND  v1.2

	 Copyright (C) 1991 PC Enterprises 1-908-280-0025

	 Permission is granted to distribute TSOUND.COM and TSOUND.DOC
	 free of charge provided the two programs are distributed
	 together and no portion of either program and/or the
	 contained messages have been altered.

	 Dedicated exclusively to the support of the IBM PCjr since
	 1984.	PCjr owners can receive a FREE PCjr products catalog by
	 calling 1-800-922-PCJR

	 TSOUND.COM is a PCjr utility for controlling the PCjr's
	 enhanced sound capabilities as well as PC Enterprises' Tandy
	 Sound Modification which adds Tandy four voice sound.	For
	 more information about these system board enhancements, call
	 either of the two phone numbers listed above.


	 HISTORY OF PC, PCjr, AND TANDY 1000 SOUND SUBSYSTEMS:

	 To understand what TSOUND.COM can do, you should first
	 understand more about your PCjr's sound subsystem and how the
	 PCE Tandy Sound modification adds to those capabilities.

	 The original IBM PC produced sound through a small speaker
	 mounted on the system board.  It could play a wide variety of
	 tones by using a programmable timer chip to modulate the
	 speaker with digital information, but only at a fixed volume.
	 Using this design, the PC can play only one tone at a time
	 and only at one volume level.	PC compatible sound is
	 therefore primarily used to produce beeps for signaling
	 certain events.

	 The PC also has BIOS support to emulate an on-off switch
	 between the timer and system board speaker.  In this document
	 file this feature is referred to as the system board speaker
	 switch.  In most cases, this feature gives software the
	 ability to turn off the system board sound, however because
	 the hardware does not actually include a physical switch, the
	 system board speaker can still beep under certain conditions
	 such as during an error.

	 When the PCjr was designed, it was obvious to IBM that the
	 PC's single voice beeper alone would not impress the home
	 computer market.  As a result, the PCjr received a special
	 sound chip which is known as the Complex Sound Generator
	 (CSG).  This chip can play three tones and one noise
	 simultaneously.  Each voice of the CSG is completely
	 independent, each having its own frequency and volume
	 control.  Nevertheless, even with these new capabilities, it
	 was still very important to remain 100% compatible with the
	 PC's sound subsystem since many PC programs were already












	 coded to use it.

	 When the PCjr is first powered on, the PC compatible sound
	 subsystem is automatically selected.  This means the system
	 board speaker is turned on.  In addition, the PCjr's enhanced
	 sound subsystem, which always produces sound through the
	 external speaker, is also set up to produce PC compatible
	 beeper sound.	When a PC compatible program produces sound,
	 it will be heard through both speakers.

	 Software designed to use the CSG can then select the CSG when
	 necessary, by using a multiplexor which is part of the PCjr's
	 sound subsystem.  A multiplexor is something like an
	 electronic switching box that allows one of four inputs to be
	 selectively connected to the PCjr's external speaker.

	 The PCjr's sound system, through use of the multiplexor, can
	 allow the sound from either its programmable timer chip, CSG,
	 cassette I/O, or external input to be heard through the
	 external speaker.

	 If software knows it's running on a PCjr and was designed to
	 use the CSG, all the software has to do is make the
	 multiplexor select the CSG instead of the programmable timer
	 and then send the music data to the CSG.  Since the
	 programmable timer gets selected automatically by the PCjr
	 when the computer is powered on, software designed to use the
	 PC's sound subsystem and not the CSG, works fine.  The
	 software just sends the PC compatible sound data to the
	 programmable timer chip without requiring the multiplexor to
	 change its default setting.  This way the PCjr has the best
	 of both worlds, PC compatibility and enhanced sound.

	 When Tandy came out with their 1000 computer, it was clear
	 that they had based their designs on the PCjr.  They did,
	 however, improve the sound system.  While retaining the
	 beeper and the CSG designs, they added a feature which
	 allows software to select both, the PC compatible beeper and
	 the CSG sound, at the same time.

	 The PCE Tandy Sound Modification eliminates this difference.
	 Once this modification is installed the PCjr, like the Tandy,
	 it can play four tones concurrently through the external
	 speaker by using the multiplexor to select an input that has
	 the timer chip and CSG together on one channel.  Since all
	 Tandy 1000s were shipped with a diskette drive, there was no
	 need for cassette recorders, so cassette support was dropped
	 in favor of four voice sound.	When the Tandy Sound
	 Modification is in use on the PCjr, cassette support is
	 disabled.
















	 USING THE TSOUND.COM UTILITY:

	 Running TSOUND.COM without any parameters will report the
	 current settings for the sound subsystem.  It will report the
	 current state of the system board speaker switch and
	 multiplexor.  It will also report whether the PCE Tandy Sound
	 Modification has been installed.

	 Running TSOUND.COM with the /? option will display a help
	 screen that shows all the options of the TSOUND utility.

	 The /T option will cause the single voice beeper and all
	 three voices of the CSG to play tones, testing and
	 demonstrating the current settings of the computer's sound
	 subsystem.  Whether the sounds being played can be heard
	 through the external speaker or system board speaker is
	 determined by the state of the multiplexor and the state of
	 the system board speaker switch.

	 If you have the PC Enterprises' Tandy Sound Modification and
	 are about to run a Tandy program that supports Tandy four
	 voice sound, run the TSOUND utility with the /4 option.  This
	 will permit the PCjr to produce up to four sounds through the
	 external speaker (This option allows Tandy software to
	 produce one, two, three, or four voice sound).

	 There is usually no need for selecting the External Input
	 option (/E) for other than experimentation or for turning off
	 the external speaker.	At this time, this input is selected
	 only by programs that support the IBM PCjr Speech Attachment.
	 Future PCE sound products will most likely make use of this
	 input also.

	 There is also no need to select the Cassette (/C) option for
	 other than experimentation.  Programs that use cassette
	 drives will automatically select this channel to store and
	 retrieve data from cassette as necessary.

The IBM PCjr sound subsystem:
									 /³
		       ÚÄÄÄÄÄÄÄÄÄÄÄ/ ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ< ³
		       ³  System board speaker switch			 \³
		       ³				   System board speaker
		       ³	ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
Programmable Timer ÄÄÄÄÁÄÄÄÄÄÄÄÄ¶		      Oº
				ºI		      uº		 /³
CSG ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶n    Multiplexor     tº		/ ³
				ºp		      pÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ<  ³
Cassette I/O ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶u		      uº		\ ³
				ºt		      tº		 \³
External input ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶		       º       External speaker
				ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


Note: These diagrams may not be able to be duplicated on some printers.

To print a copy of this document enter the following command at the DOS prompt:

		COPY TSOUND.DOC PRN: