The MEGADSK.SYS file included on this diskette is the latest
         release of PC Enterprises Megaboard software.
          
         The most significant enhancement to this new release is that
         it permits you to create a ramdisk, then reboot your PCjr
         with either a warm boot (Ctrl/Alt/Del), or a Cartridge Reset
         (wiggle a cartridge in the cartridge slot), without losing
         the contents of your PCE Megaboard ramdisk!
          
         This offers significant improvement over prior releases
         because Megaboard users can now store information on their
         Megaboard ramdisk without concern that they may need to
         reboot their PCjr, thereby loosing all ramdisk information
         which has not been saved.
          
         To use the device driver, simply add the line:
         DEVICE=MEGADSK.SYS /* to your CONFIG.SYS file.  This will
         cause all available PCE memory to be used as a Megaboard
         ramdisk.
          
         To limit the amount of PCE memory allocated to a Megaboard
         ramdisk, replace the /* with the actual amount of memory you
         would like to allocate.
          
         For example, the following CONFIG.SYS file will allow DOS to
         recognize 736KB of conventional memory, and also set up two
         360KB drives (ramdisks) in PCE memory:
          
         DEVICE=JRCONFIG.SYS -L
         DEVICE=MEGADSK.SYS /360
         DEVICE=MEGADSK.SYS /360
          
         Of course, you will need a PCE Megaboard with adequate PCE
         memory to operate in this configuration.
          
          
         IMPORTANT NOTE:
          
         At times you may power down the PCjr in order to
         intentionally erase the contents of your Megaboard ramdisk.
         When this is done, you may need to keep your PCjr off for 20
         seconds or more, before turning the power back on.