RUNCART v1.0
	 Copyright (C) 1990 PC Enterprises  908 280-0025

	 RUNCART.COM can be copied onto your hard disk drive and
	 distributed as only if it is copied with RUNCART.DOC and
	 neither file is modified in any way.

	 This program will allow PCjr users who have added a PC
	 Enterprises self booting hard drive or Turbo-Drive to use IPL
	 cartridges without removing any hardware.

	 IPL (Initial Program Loadable) cartridges are cartridges
	 which can not be run by entering a command from the DOS
	 prompt.  The only way to run an IPL cartridge is to start the
	 computer with the cartridge installed and the door to drive
	 A: open.

	 Three Spinnaker cartridges: Kindercomp, Fraction Fever, and
	 Facemaker are examples of IPL cartridges.  If you have a self
	 booting hard drive or Turbo-Drive you will need to use the
	 RUNCART program in order to use these cartridges.  This is
	 because the PCjr is programmed to boot from hard drive or
	 Turbo-Drive before running any IPL cartridges.  So if one of
	 these self-booting devices is installed, you normally would
	 have to remove it to run your IPL cartridges.

	 To use the RUNCART program simply start your computer in the
	 usual manner with the IPL cartridge inserted into either
	 cartridge slot.  Note that only one IPL cartridge should be
	 inserted at a time.  Next, insert the diskette which contains
	 the RUNCART program, enter the command RUNCART, and then
	 press Enter.

	 Once a cartridge is activated from DOS by using the RUNCART
	 program you may need to reboot the computer in order to get
	 back to the DOS prompt.  Many IPL cartridges do not have a
	 provision for exiting the cartridge since the cartridge is
	 not expected to be run from DOS.